## Slide 1: Computer Organization and Architecture Designing for Performance
11th Edition, Global Edition
Chapter 4
The Memory Hierarchy: Locality and Performance

## Slide 2: Principle of Locality (1 of 2)
Also referred to as the locality of reference
Reflects the observation that during the course of execution of a program, memory references by the processor tend to cluster
Locality is based on three assertions:
    During any interval of time, a program references memory location non-uniformly
    As a function of time, the probability that a given unit of memory is referenced tends to change slowly
    The correlation between immediate past and immediate future memory reference patterns is high and tapers off as the time interval increases
Notes: One of the most important concepts related to computer systems is principle of
locality [DENN05], also referred to as the locality of reference . The principle reflects
the observation that during the course of execution of a program, memory references
by the processor, for both instructions and data, tend to cluster. Programs typically
contain a number of iterative loops and subroutines. Once a loop or subroutine
is entered, there are repeated references to a small set of instructions. Similarly, operations
on tables and arrays involve access to a clustered set of data words. Over a
long period of time, the clusters in use change, but over a short period of time, the
processor is primarily working with fixed clusters of memory references.
We can put these observations more specifically. As we discuss in Section 4.3,
for different types of memory, memory is accessed and retrieved in units of different
sizes, ranging from individual words to large blocks of cache memory to much
larger segments of disk memory. Denning observed that locality is based on three
assertions [DENN72]:
1. During any interval of time, a program references memory locations
non-uniformly. That is, some units of memory are more likely to be accessed
than others.
2. As a function of time, the probability that a given unit of memory is referenced
tends to change slowly. Put another way, the probability distribution
of memory references across the entire memory space tends to change slowly
over time.
3. The correlation between immediate past and immediate future memory reference
patterns is high, and tapers off as the time interval increases.
Intuitively, the principle of locality makes sense. Consider the following line
of reasoning:
1. Except for branch and call instructions, which constitute only a small fraction
of all program instructions, program execution is sequential. Hence, in most
cases, the next instruction to be fetched immediately follows the last instruction
fetched.
2. It is rare to have a long uninterrupted sequence of procedure calls followed
by the corresponding sequence of returns. Rather, a program remains confined
to a rather narrow window of procedure-invocation depth. Thus, over
a short period of time, references to instructions tend to be localized to a few
procedures.
3. Most iterative constructs consist of a relatively small number of instructions
repeated many times. For the duration of the iteration, computation is therefore
confined to a small contiguous portion of a program.
4. In many programs, much of the computation involves processing data structures,
such as arrays or sequences of records. In many cases, successive references
to these data structures will be to closely located data items.

## Slide 3: Principle of Locality (2 of 2)
Two forms of locality
    Temporal locality
        Refers to the tendency of a program to reference in the near future those units of memory referenced in the recent past
        Constants, temporary variables, and working stacks are also constructs that lead to this principle
Spatial locality
    Spatial locality
        Refers to the tendency of a program to reference units of memory whose addresses are near one another
        Also reflects the tendency of a program to access data locations sequentially, such as when processing a table of data
Notes: Numerous studies, stretching back to the early 1970s, confirm these observations.
[FEIT15] provides a summary of many of these studies.
A distinction is made in the literature between two forms of locality:
1. Temporal locality : Refers to the tendency of a program to reference in the
near future those units of memory referenced in the recent past. For example,
when an iteration loop is executed, the processor executes the same set
of instructions repeatedly. Constants, temporary variables, and working stacks
are also constructs that lead to this principle.
2. Spatial locality: Refers to the tendency of a program to reference units of
memory whose addresses are near one another. That is, if a unit of memory x
is referenced at time t, it is likely that units in the range x - k through x + k
will be referenced in the near future, for a relatively small value of k. This
reflects the tendency of a processor to access instructions sequentially. Spatial
location also reflects the tendency of a program to access data locations
sequentially, such as when processing a table of data.

## Slide 4: Figure 4.1
Notes: A crude analogy may help illuminate the distinction between these two concepts
(Figure 4.1). Suppose that Bob is working in an office and spends much of his
time dealing with documents in file folders. Thousand of folders are stored in file
cabinets in the next room, and for convenience Bob has a file organizer on his desk
that can hold a few dozen files. When Bob is working on a file and temporarily is
finished, it may be likely that he will need to read or write one of the documents in
that file in the near future, so he keeps it in his desk organizer. This is an example
of exploiting temporal locality. Bob also observes that when he retrieves a folder
from the filing cabinets, it is likely that in the near future he will need access to some
of the nearby folders as well, so he retrieves the folder he needs plus a few folders
on either side at the same time. This is an example of exploiting spatial locality. Of
course, Bob's desktop file organizer soon fills up, so that when he goes to retrieve
a folder from the file cabinets, he needs to return folders from his desk. Bob needs
some policy for replacing folders. If he focuses on temporal locality, Bob could
choose to replace only one folder at a time, on the reasoning that he might need
any of the folders currently on his desk in the near future. So Bob could replace
perhaps the folder that had been on the desk the longest or the one that had be the
least recently used. If Bob focuses on spatial locality, when he needs a folder not on
his desk, he could return and refile all the folders on his desk and retrieve a batch
of contiguous folders that includes the one he needs plus other nearby folders sufficient
to fill up his desktop organizer. It is likely that neither policy is optimal. In the
first case, he might have to make frequent trips to the next room to get one folder he
doesn’t have but which is near one he does have. In the second case, he might have
to make frequent trips to the next room to get a folder that he had just recently put
away. So perhaps a policy of returning and retrieving in batches equal to 10% or
20% of his desktop capacity would be closer to optimal.
For cache memory, temporal locality is traditionally exploited by keeping recently
used instruction and data values in cache memory and by exploiting a cache hierarchy.
Spatial locality is generally exploited by using larger cache blocks and by incorporating
prefetching mechanisms (fetching items of anticipated use) into the cache control logic.
Over the years, there has been considerable research on refining these techniques to
achieve greater performance, but the basic strategies remain the same.

## Slide 5: Figure 4.2
Notes: Figure 4.2 provides a rough depiction of the behavior of programs that exhibit
temporal locality. For a unit of memory accessed at time t , the figure shows the distribution
of probability of the time of the next access to the same memory unit.

## Slide 6: Figure 4.3
Notes: Similarly, Figure 4.3 provides a rough depiction of the behavior of programs that exhibit
spatial locality. For spatial locality, the probability distribution curve is symmetrical
around the location of the most recent memory access address.
Many programs exhibit both temporal and spatial locality for both instruction
and data access. It has been found that data access patterns generally show a greater
variance than instruction access patterns [AHO07]. Figure 4.3 suggests this distinction
between the distribution of data location accesses (read or write) and instruction
fetch addresses. Typically, each instruction execution involves fetching the instruction
from memory and, during execution, accessing one or more data operands from
one or more regions of memory. Thus, there is a dual locality of data spatial
Locality and instruction spatial locality . And, of course, temporal locality exhibits this same
dual behavior: data temporal locality and instruction temporal locality . That is, when
an instruction is fetched from a unit of memory, it is likely that in the near future,
additional instructions will be fetched from that same memory unit; and when a data
location is accessed, it is likely that in the near future, additional instructions will be
fetched from that same memory unit.

## Slide 7: Figure 4.4
Notes: An example of data locality is illustrated in Figure 4.4 [BAEN97]. This shows
the results of a study of Web-based document access patterns, where the documents
are distributed among a number of servers. In this case, the unit of access is a single
document and temporal locality is measured. The access scheme makes use of a document
cache at the browser that can temporarily retain a small number of documents
to facilitate reuse. The study covered 220,000 documents distributed over 11,000
servers. As shown in Figure 4.4, only a very small subset of pages incorporates a high
number of references while most documents are accessed relatively infrequently.

## Slide 8: Figure 4.5
Notes: Figure 4.5 shows an example of instruction locality based on executing the integer
benchmark programs in the SPEC CPU2006 benchmark suite; similar results were
obtained for the floating-point programs. The following terms are used in the plot:
1. Static instruction : An instruction that exists in the code to be executed.
2. Dynamic instruction : Instructions that appear in the execution trace of a
program.
Thus, each static instruction is represented by zero or more instances of
dynamic instructions when the program is executed. Each line in the graph represents
a separate benchmark program. In the figure, the cumulative percentage of dynamic
instructions executed by a program is shown on the y -axis and the cumulative count
of static instructions is shown on the x -axis. The first point in the line plot for each
benchmark represents the most frequently called subroutine, with the x coordinate
showing the number of static instructions in the routine and y coordinate showing
the percentage of dynamic instructions that it represents. The second,
third, fourth, and fifth points respectively represent the top 5, 10, 15, and 20 most frequently called
subroutines. Many programs initially show a steep upward climb as the static instruction
count increases, which suggests very good instruction locality.

## Slide 9: Table 4.1 Key Characteristics of Computer Memory Systems
Location Internal (e.g., processor registers, cache, main memory) External (e.g., optical disks, magnetic disks, tapes) Capacity Number of words Number of bytes Unit of Transfer Word Block Access Method Sequential Direct Random Associative | Performance Access time Cycle time Transfer rate Physical Type Semiconductor Magnetic Optical Magneto-optical Physical Characteristics Volatile/nonvolatile Erasable/nonerasable Organization Memory modules
Notes: The complex subject of computer memory is made more manageable if we classify
memory systems according to their key characteristics. The most important of these
are listed in Table 4.1.

## Slide 10: Characteristics of Memory Systems
Location
  Refers to whether memory is internal and external to the computer
  Internal memory is often equated with main memory
  Processor requires its own local memory, in the form of registers
  Cache is another form of internal memory
  External memory consists of peripheral storage devices that are accessible to the processor via I/O controllers
Capacity
  Memory is typically expressed in terms of bytes
Unit of transfer
  For internal memory the unit of transfer is equal to the number of electrical lines into and out of the memory module
Notes: The term location in Table 4.1 refers to whether memory is internal and external
to the computer. Internal memory is often equated with main memory. But there
are other forms of internal memory. The processor requires its own local memory, in
the form of registers (e.g., see Figure 2.3). Further, as we shall see, the control unit
portion of the processor may also require its own internal memory. We will defer
discussion of these latter two types of internal memory to later chapters. Cache is
another form of internal memory. External memory consists of peripheral storage
devices, such as disk and tape, that are accessible to the processor via I/O controllers.
An obvious characteristic of memory is its capacity. For internal memory, this is
typically expressed in terms of bytes (1 byte = 8 bits) or words. Common word lengths
are 8, 16, and 32 bits. External memory capacity is typically expressed in terms of bytes.
A related concept is the unit of transfer. For internal memory, the unit
of transfer is equal to the number of electrical lines into and out of the memory
module. This may be equal to the word length, but is often larger, such as 64, 128, or
256 bits. To clarify this point, consider three related concepts for internal memory:
• Word: The “natural” unit of organization of memory. The size of a word is typically
equal to the number of bits used to represent an integer and to the instruction
length. Unfortunately, there are many exceptions. For example, the CRAY
C90 (an older model CRAY supercomputer) has a 64-bit word length but uses
a 46-bit integer representation. The Intel x86 architecture has a wide variety of
instruction lengths, expressed as multiples of bytes, and a word size of 32 bits.
• Addressable units: In some systems, the addressable unit is the word. However,
many systems allow addressing at the byte level. In any case, the relationship
between the length in bits A of an address and the number N of addressable
units is 2A = N.
• Unit of transfer: For main memory, this is the number of bits read out of or
written into memory at a time. The unit of transfer need not equal a word or
an addressable unit. For external memory, data are often transferred in much
larger units than a word, and these are referred to as blocks

## Slide 11: Method of Accessing Units of Data
Sequential access
Memory is organized into units of data called records
Access must be made in a specific linear sequence
Access time is variable
Direct access
Involves a shared read-write mechanism
Individual blocks or records have a unique address based on physical location
Access time is variable
Random access
Each addressable location in memory has a unique, physically wired-in addressing mechanism
The time to access a given location is independent of the sequence of prior accesses and is constant
Any location can be selected at random and directly addressed and accessed
Main memory and some cache systems are random access
Associative
A word is retrieved based on a portion of its contents rather than its address
Each location has its own addressing mechanism and retrieval time is constant independent of location or prior access patterns
Cache memories may employ associative access
Notes: Another distinction among memory types is the method of accessing units of
data. These include the following:
• Sequential access: Memory is organized into units of data, called records.
Access must be made in a specific linear sequence. Stored addressing information
is used to separate records and assist in the retrieval process. A shared
read–write mechanism is used, and this must be moved from its current location
to the desired location, passing and rejecting each intermediate record.
Thus, the time to access an arbitrary record is highly variable. Tape units, discussed
in Chapter 7, are sequential access.
Direct access: As with sequential access, direct access involves a shared
read–write mechanism. However, individual blocks or records have a unique
address based on physical location. Access is accomplished by direct access
to reach a general vicinity plus sequential searching, counting, or waiting to
reach the final location. Again, access time is variable. Disk units, discussed in
Chapter 6, are direct access.
• Random access: Each addressable location in memory has a unique, physically
wired-in addressing mechanism. The time to access a given location is independent
of the sequence of prior accesses and is constant. Thus, any location
can be selected at random and directly addressed and accessed. Main memory
and some cache systems are random access.
• Associative: This is a random access type of memory that enables one to make
a comparison of desired bit locations within a word for a specified match, and
to do this for all words simultaneously. Thus, a word is retrieved based on a
portion of its contents rather than its address. As with ordinary random-access
memory, each location has its own addressing mechanism, and retrieval time
is constant independent of location or prior access patterns. Cache memories
may employ associative access.

## Slide 12: Capacity and Performance:
The two most important characteristics of memory
Three performance parameters are used:
Access time (latency)
For random-access memory it is the time it takes to perform a read or write operation
For non-random-access memory it is the time it takes to position the read-write mechanism at the desired location
Memory cycle time
Access time plus any additional time required before second access can commence
Additional time may be required for transients to die out on signal lines or to regenerate data if they are read destructively
Concerned with the system bus, not the processor
Transfer rate
The rate at which data can be transferred into or out of a memory unit
For random-access memory it is equal to 1/(cycle time)
Notes: From a user’s point of view, the two most important characteristics of memory
are capacity and performance. Three performance parameters are used:
• Access time (latency): For random-access memory, this is the time it takes to
perform a read or write operation, that is, the time from the instant that an
address is presented to the memory to the instant that data have been stored
or made available for use. For non-random-access memory, access time is the
time it takes to position the read–write mechanism at the desired location.
• Memory cycle time: This concept is primarily applied to random-access memory
and consists of the access time plus any additional time required before a second
access can commence. This additional time may be required for transients to die
out on signal lines or to regenerate data if they are read destructively. Note that
memory cycle time is concerned with the system bus, not the processor.
• Transfer rate: This is the rate at which data can be transferred into or out of a
memory unit. For random-access memory, it is equal to 1/(cycle time).

## Slide 13: Memory
  The most common forms are:
  Semiconductor memory
  Magnetic surface memory
  Optical
  Magneto-optical
  Several physical characteristics of data storage are important:
  Volatile memory
    Information decays naturally or is lost when electrical power is switched off
  Nonvolatile memory
    Once recorded, information remains without deterioration until deliberately changed
    No electrical power is needed to retain information
  Magnetic-surface memories
    Are nonvolatile
  Semiconductor memory
    May be either volatile or nonvolatile
  Nonerasable memory
    Cannot be altered, except by destroying the storage unit
    Semiconductor memory of this type is known as read-only memory (ROM)
  For random-access memory the organization is a key design issue
  Organization refers to the physical arrangement of bits to form words
Notes: A variety of physical types of memory have been employed. The most common
today are semiconductor memory, magnetic surface memory, used for disk and
tape, and optical and magneto-optical.
Several physical characteristics of data storage are important. In a volatile
memory, information decays naturally or is lost when electrical power is switched
off. In a nonvolatile memory, information once recorded remains without deterioration
until deliberately changed; no electrical power is needed to retain information.
Magnetic-surface memories are nonvolatile. Semiconductor memory (memory
on integrated circuits) may be either volatile or nonvolatile. Nonerasable memory
cannot be altered, except by destroying the storage unit. Semiconductor memory of
this type is known as read-only memory (ROM). Of necessity, a practical nonerasable
memory must also be nonvolatile.
For random-access memory, the organization is a key design issue. In this context,
organization refers to the physical arrangement of bits to form words. The
obvious arrangement is not always used, as is explained in Chapter 6.

## Slide 14: Memory Hierarchy
Design constraints on a computer’s memory can be summed up by three questions:
  How much, how fast, how expensive
There is a trade-off among capacity, access time, and cost
  Faster access time, greater cost per bit
  Greater capacity, smaller cost per bit
  Greater capacity, slower access time
Notes: The design constraints on a computer’s memory can be summed up by three questions:
How much? How fast? How expensive?
The question of how much is somewhat open ended. If the capacity is there,
applications will likely be developed to use it. The question of how fast is, in a sense,
easier to answer. To achieve greatest performance, the memory must be able to
keep up with the processor. That is, as the processor is executing instructions, we
would not want it to have to pause waiting for instructions or operands. The final
question must also be considered. For a practical system, the cost of memory must
be reasonable in relationship to other components.
As might be expected, there is a trade-off among the three key characteristics
of memory: capacity, access time, and cost. A variety of technologies are used to
implement memory systems, and across this spectrum of technologies, the following
relationships hold:
• Faster access time, greater cost per bit
• Greater capacity, smaller cost per bit
• Greater capacity, slower access time
The dilemma facing the designer is clear. The designer would like to use memory
technologies that provide for large-capacity memory, both because the capacity
is needed and because the cost per bit is low. However, to meet performance
requirements, the designer needs to use expensive, relatively lower-capacity memories
with short access times.

## Slide 15: Figure 4.6
Notes: The way out of this dilemma is not to rely on a single memory component or technology,
but to employ a memory hierarchy . A typical hierarchy is illustrated in
Figure 4.6. As one goes down the hierarchy, the following occur:
a. Decreasing cost per bit
b. Increasing capacity
c. Increasing access time
d. Decreasing frequency of access of the memory by the processor

## Slide 16: Figure 4.7
Notes: Figure 4.7 (in a general way and not to scale) illustrates these relationships
across the memory hierarchy.
Thus, smaller, more expensive, faster memories are supplemented by larger,
cheaper, slower memories. The key to the success of this organization is item (d):
decreasing frequency of access, which can be achieved by exploiting the principle
of locality, described in Section 4.1. We discuss techniques for exploiting locality in
the treatment of cache, in Chapter 5, and virtual memory, in Chapter 9. A general
discussion is provided at this point.
It is possible to organize data across the hierarchy such that the percentage of
accesses to each successively lower level is substantially less than that of the level
above.

## Slide 17: Figure 4.8
Notes: Suppose that the processor has access to two levels of memory. Level
1 contains X words and has an access time of 0.01 μs; level 2 contains 1000 x X words
and has an access time of 0.1 μs. Assume that if a word to be accessed is in level 1, then the
processor accesses it directly. If it is in level 2, then the word is first transferred to level 1
and then accessed by the processor. For simplicity, we ignore the time required for the processor
to determine whether the word is in level 1 or level 2. Figure 4.8 shows the general
shape of the curve that covers this situation. The figure shows the average access time to
a two-level memory as a function of the hit ratio H, where H is defined as the fraction of
all memory accesses that are found in the faster memory (e.g., the cache), T1 is the access
time to level 1, and T2 is the access time to level 2. As can be seen, for high percentages
of level 1 access, the average total access time is much closer to that of level 1 than that
of level 2.
In our example, suppose 95% of the memory accesses are found in level 1. Then the
average time to access a word can be expressed as
(0.95)(0.01 μs) + (0.05)(0.01 μs + 0.1 μs) = 0.0095 + 0.0055 = 0.015 μs
The average access time is much closer to 0.01 μs than to 0.1 μs, as desired.
Let level 2 memory contains all program instructions and data. The current clusters can be
temporarily placed in level 1. From time to time, one of the clusters in level 1 will
have to be swapped back to level 2 to make room for a new cluster coming in to
level 1. On average, however, most references will be to instructions and data contained
in level 1.
The use of two levels of memory to reduce average access time works in principle,
but only if conditions (a) through (d) apply. By employing a variety of technologies,
a spectrum of memory systems exists that satisfies conditions (a) through
(c). Fortunately, condition (d) is also generally valid due to the principle of locality.

## Slide 18: Figure 4.9
Notes: This principle can be applied across more than two levels of memory, as suggested
by the hierarchy shown in Figure 4.6. In practice, the dynamic movement of
chunks of data between levels during program execution involves registers, one
or more levels of cache, main memory, and virtual memory stored on disk. This is
shown in Figure 4.9, with an indication of the size of the chunks of data exchanged
between levels.

## Slide 19: Table 4.2 Characteristics of Memory Devices in a Memory Architecture
Memory level | Typical technology | Unit of transfer with next larger level (typical size) | Managed by
Registers | CMOS | Word (32 bits) | Compiler
Cache | Static RAM (SRAM); Embedded dynamic RAM (eDRAM) | Cache block (32 bytes) | Processor hardware
Main memory | DRAM | Virtual memory page (1 kB) | Operating system (OS)
Secondary memory | Magnetic disk | Disk sector (512 bytes) | OS/user
Offline bulk memory | Magnetic tape |  | OS/User
Table 4.2 Characteristics of Memory Devices in a Memory Architecture
Notes: Table 4.2 lists some characteristics of key elements of the memory hierarchy. The
fastest, smallest, and most expensive type of memory consists of the registers internal
to the processor. Typically, a processor will contain a few dozen such registers,
although some machines contain hundreds of registers. Next will be typically multiple
layers of cache. Level 1 cache (L1 cache), closest to the processor registers, is
almost always divided into an instruction cache and a data cache. This split is also
common for L2 caches. Most contemporary machines also have an L3 cache and
some have an L4 cache; these two caches generally are not split between instruction
and data and may be shared by multiple processors. Traditionally, cache memory has
been constructed using a technology called static random access memory (SRAM).
More recently, higher levels of cache on many systems have been implemented using
embedded dynamic RAM (eDRAM), which is slower than SRAM but faster than
the DRAM used to implement the main memory of the computer.
Main memory is the principal internal memory system of the computer. Each
location in main memory has a unique address. Main memory is visible to the programmer,
whereas cache memory is not. The various levels of cache are controlled
by hardware and are used for staging the movement of data between main memory
and processor registers to improve performance.

## Slide 20: Memory
The use of three levels exploits the fact that semiconductor memory comes in a variety of types which differ in speed and cost
Data are stored more permanently on external mass storage devices
External, nonvolatile memory is also referred to as secondary memory or auxiliary memory
Notes: The three forms of memory just described are, typically, volatile and employ
semiconductor technology. The use of three levels exploits the fact that semiconductor
memory comes in a variety of types, which differ in speed and cost. Data are
stored more permanently on external mass storage devices, of which the most common
are hard disk and removable media, such as removable magnetic disk, tape,
and optical storage. External, nonvolatile memory is also referred to as secondary
memory or auxiliary memory . These are used to store program and data files and
are usually visible to the programmer only in terms of files and records, as opposed
to individual bytes or words. Disk is also used to provide an extension to main memory
known as virtual memory, which is discussed in Chapter 9. Other forms of
secondary memory include optical disks and flash memory.

## Slide 21: Figure 4.10
Notes: Figure 4.10 illustrates the memory hierarchy for the IBM z13 mainframe computer
[LASC16]. It consists of the following levels:
■ L1 and L2 caches use SRAM, and are private for each core (Figure 1.5).
■ L3 cache uses eDRAM and is shared by all eight cores within the PU chip
(Figure 1.4). Each CPC drawer has six L3 caches. A four-CPC drawer system
therefore has 24 of them, resulting in 1536 MB (24 * 64 MB) of this shared
PU chip-level cache.
■ L4 cache also uses eDRAM, and is shared by all PU chips on the node of a
CPC drawer. Each L4 cache has 480 MB for previously owned and some least
recently used (LRU) L3-owned lines and 224 MB for a non-data inclusive coherent
(NIC) directory that points to L3 owned lines that have not been included
in L4 cache. A four-CPC drawer system has 3840 MB (4 * 2 * 384 MB) of
shared L4 cache and 1792 MB (4 * 2 * 224 MB) of NIC directory.
■ Main storage has up to 2.5 TB addressable memory per CPC drawer, using
DRAM. A four-CPC drawer system can have up to 10 TB of main storage.
■ Secondary memory holds virtual memory and is stored in disks accessed by
various I/O technologies.

## Slide 22: Design Principles for a Memory Hierarchy
Locality
The principle that makes effective use of a memory hierarchy possible
Inclusion
This principle dictates that all information items are originally stored in level Mn where n is the level most remote from the processor
Coherence
Copies of the same data unit in adjacent memory levels must be consistent
If a word is modified in the cache, copies of that word must be updated immediately or eventually at all higher levels
Notes: Three principles guide the design of a memory hierarchy and the supporting memory
management hardware and software:
1. Locality : Locality is the principle that makes effective use of a memory hierarchy
possible.
2. Inclusion : This principle dictates that all information items are originally stored
in level Mn , where n is the level most remote from the processor. During the
processing, subsets of Mn are copied into Mn-1 . similarity, subsets of Mn-1 are
copied into Mn-2 , and so on.
3. Coherence: Copies of the same data unit in adjacent memory levels must be
consistent. If a word is modified in the cache, copies of that word must be
updated immediately or eventually at all higher levels.
Coherence has both vertical and horizontal implications, and is required because
multiple memories at one level may share the same memory at the next higher (greater
value of i ) level. For example, for the IBMz13, eight L2 caches share the same L3
cache, and three L3 caches share the same L4 cache. This leads to two requirements:
■ Vertical coherence: If one core makes a change to a cache block of data at L2,
that update must be returned to L3 before another L2 retrieves that block.
■ Horizontal coherence: If two L2 caches that share the same L3 cache have
copies of the same block of data, then if the block in one L2 cache is updated,
the other L2 cache must be alerted that its copy is obsolete. The topic of coherence
is discussed in future chapters.

## Slide 23: Two-Level Memory Access
A cache acts as a buffer between main memory and processor, creating a two-level internal memory
Exploits locality to provide improved performance over a comparable one-level memory
The main memory cache mechanism is part of the computer architecture, implemented in hardware and typically invisible to the operating system
Two other instances of a two-level memory approach that also exploit locality and that are, at least partially, implemented in the operating system are virtual memory and the disk cache
Notes: In this chapter, reference is made to a cache that acts as a buffer between main
memory and processor, creating a two-level internal memory. In the simplest case,
rarely implemented in modern systems, there is a single level of cache to interact
with main memory. This two-level architecture exploits locality to provide improved
performance over a comparable one-level memory.
The main memory cache mechanism is part of the computer architecture,
implemented in hardware and typically invisible to the operating system. There are
two other instances of a two-level memory approach that also exploit locality and
that are, at least partially, implemented in the operating system: virtual memory
and the disk cache. Virtual memory is explored in Chapter 9; disk cache is beyond
the scope of this book but is examined in [STAL18]. In this subsection, we look at
some of the performance characteristics of two-level memories that are common to
all three approaches.

## Slide 24: Operation of Two-Level Memory
The locality property can be exploited in the formation of a two-level memory
The upper-level memory (M1) is smaller, faster, and more expensive (per bit) than the lower-level memory (M2)
M1 is used as temporary store for part of the contents of the larger M2
When a memory reference is made, an attempt is made to access the item in M1
    If this succeeds, then a quick access is made
    If not, then a block of memory locations is copied from M2 to M1 and the access then takes place via M1
Because of locality, once a block is brought into M1, there should be a number of accesses to locations in that block, resulting in fast overall service
Notes: The locality property can be exploited
in the formation of a two-level memory. The upper-level memory (M1) is smaller,
faster, and more expensive (per bit) than the lower-level memory (M2). M1 is used
as a temporary store for part of the contents of the larger M2. When a memory
reference is made, an attempt is made to access the item in M1. If this succeeds,
then a quick access is made. If not, then a block of memory locations is copied from
M2 to M1 and the access then takes place via M1. Because of locality, once a block
is brought into M1, there should be a number of accesses to locations in that block,
resulting in fast overall service.

## Slide 25: Figure 4.11
Notes: Relationship of Average Memory Cost to Relative Memory Size for a Two-Level
Memory.

## Slide 26: Figure 4.12
Notes: Access Efficiency as a Function of Hit Ratio (r = T2/T1)

## Slide 27: Figure 4.13
Notes: Figure 4.13 suggests the effect that locality has on the hit ratio.
Does the relative size of the
two memories satisfy the cost requirement? The answer is clearly yes. If we need
only a relatively small upper-level memory to achieve good performance, then the
average cost per bit of the two levels of memory will approach that of the cheaper
lower-level memory.

## Slide 28: Figure 4.14
Notes: Figure 4.14 is a flowchart that provides a simplified memory access model for
a memory hierarchy, which we can use to develop a formula for the average access
time. It can be described as follows:
1. The processor generates a memory address request. The first step is to determine
if the cache block containing that address resides in the L1 cache (memory
level M1 ). The probability of that is h1 . If the desired word is present in the
cache, that word is delivered to the processor. The average time required for
this operation is t1 .
2. For subsequent levels i , 2 ≤ i ﹤ n , if the addressed word is not found in
Mi-1 , then the memory management hardware checks to determine if it is
in Mi-1, which occurs with a probability of hi. If the desired word is present
in Mi, the word is delivered from Mi to the processor, and the appropriate
size block containing the word is copied to Mi-1. The average time for this
operation is ti-1.
3. In the typical memory hierarchy, Mn is a disk used in a virtual memory scheme.
In this case, if the word is not found in any of the preceding levels and is found
in Mn, then the word must be first moved as part of a page into main memory
(Mn-1), from where it can be transferred to the processor. We designate the
total time for this operation as tn .
Looking at Figure 4.14, there are a number of different paths from start to
finish.

## Slide 29: Summary
Chapter 4
Principle of locality
Characteristics of memory systems
Performance modeling of a multilevel memory hierarchy
    Two-level memory access
    Multilevel memory access
  The memory hierarchy
      Cost and performance characteristics
      Typical members of the memory hierarchy
      The IBM z13 memory hierarchy
      Design principles for a memory hierarchy
The Memory Hierarchy: Locality and Performance
Notes: Chapter 4 summary.