## Slide 1: Computer Organization and Architecture Designing for Performance
11th Edition, Global Edition
Chapter 5
Cache Memory

## Slide 2: Figure 5.1 Cache and Main Memory
Notes: Cache memory is designed to combine the memory access time of expensive, high-
speed memory combined with the large memory size of less expensive, lower-
speed memory. The concept is illustrated in Figure 5.1a. There is a relatively large and slow
main memory together with a smaller, faster cache memory. The cache contains
a copy of portions of the main memory. When the processor attempts
to read a word of memory, a check is made to determine if the word is in the
cache. If so, the word is delivered to the processor. If not, a block of main
memory, consisting of some fixed number of words, is read into the cache
and then the word is delivered to the processor. Because of the phenomenon
of locality of reference, when a block of data is fetched into the cache
to satisfy a single memory reference, it is likely that there will be future
references to that same memory location or to other words in the block.
Figure 5.1b depicts the use of multiple levels of cache. The L2 cache
is slower and typically larger than the L1 cache, and the L3 cache is slower
and typically larger than the L2 cache.

## Slide 3: Cache Memory Principles
Block
    The minimum unit of transfer between cache and main memory
Frame
    To distinguish between the data transferred and the chunk of physical memory, the term frame, or block frame, is sometimes used with reference to caches
Line
    A portion of cache memory capable of holding one block, so-called because it is usually drawn as a horizontal object
Tag
    A portion of a cache line that is used for addressing purposes
Line size
    The number of data bytes, or block size, contained in a line
Notes: ■ Block: The minimum unit of transfer between cache and main memory.
In most of the literature, the term block refers both to the unit of data
transferred and to the physical location in main memory or cache.
■ Frame: To distinguish between the data transferred and the chunk of
physical memory, the term frame, or block frame, is sometimes used
with reference to caches. Some texts and some literature use the term
with reference to the cache and some with reference to main memory. It use is
not necessary for purposes of this text.
■ Line: A portion of cache memory capable of holding one block, so-called
because it is usually drawn as a horizontal object (i.e., all bytes of the line are
typically drawn in one row). A line also includes control information.
■ Tag: A portion of a cache line that is used for addressing purposes, as explained
subsequently. A cache line may also include other control bits, as will be shown.
Main memory consists of up to 2n addressable words, with each word having a
unique n-bit address. For mapping purposes, this memory is considered to consist of
a number of fixed-length blocks of K words each. That is, there are M =2n /K blocks
in main memory. The cache consists of m lines. Each line contains K words, plus a tag.
Each line also includes control bits (not shown), such as a bit to indicate whether the
line has been modified since being loaded into the cache. The length of a line, not
including tag and control bits, is the line size . That is, the term line size refers to the
number of data bytes, or block size, contained in a line. They may be as small as 32 bits,
with each “word” being a single byte; in this case the line size is 4 bytes. The number
of lines is considerably less than the number of main memory blocks (m << M ). At
any time, some subset of the blocks of memory resides in lines in the cache. If a word
in a block of memory is read, that block is transferred to one of the lines of the cache.
Because there are more blocks than lines, an individual line cannot be uniquely and
permanently dedicated to a particular block. Thus, each line includes a tag that identifies
which particular block is currently being stored. The tag is usually a portion of the
main memory address, as described later in this section.

## Slide 4: Figure 5.2 Cache/Main Memory Structure
Notes: Figure 5.2 depicts the structure of a cache/main-memory
system.

## Slide 5: Figure 5.3 Cache Read Operation
Notes: Figure 5.3 illustrates the read operation. The processor generates the read
address (RA) of a word to be read. If the word is contained in the cache (cache hit),
it is delivered to the processor.

## Slide 6: Figure 5.4 Typical Cache Organization
Notes: If a cache miss occurs, two things must be accomplished: the block containing
the word must be loaded in to the cache, and the word must be delivered to the processor.
When a block is brought into a cache in the event of a miss, the block is generally
not transferred in a single event. Typically, the transfer size between cache and main
memory is less than the line size, with 128 bytes being a typical line size and a cache main
memory transfer size of 64 bits (2 bytes). To improve performance, the critical
word first technique is commonly used. When there is a cache miss, the hardware
requests the missed word first from memory and sends it to the processor as soon as
it arrives. This enables the processor to continue execution while filling the rest of the
words in the block. Figure 5.3 shows these last two operations occurring in parallel
and reflects the organization shown in Figure 5.4, which is typical of contemporary
cache organizations. In this organization, the cache connects to the processor via data,
control, and address lines. The data and address lines also attach to data and address
buffers, which attach to a system bus from which main memory is reached. When a
cache hit occurs, the data and address buffers are disabled and communication is only
between processor and cache, with no system bus traffic. When a cache miss occurs,
the desired address is loaded onto the system bus and the data are returned through
the data buffer to both the cache and the processor.

## Slide 7: Table 5.1 Elements of Cache Design
Cache Addresses Logical Physical Cache Size Mapping Function Direct Associative Set associative Replacement Algorithm Least recently used (LRU) First in first out (FIFO) Least frequently used (LFU) Random | Write Policy Write through Write back Line Size Number of Caches Single or two level Unified or split
Notes: This section provides an overview of cache design parameters and reports some typical
results. We occasionally refer to the use of caches in high-performance computing
(HPC). HPC deals with supercomputers and their software, especially for scientific
applications that involve large amounts of data, vector and matrix computation, and the
use of parallel algorithms. Cache design for HPC is quite different than for other hardware
platforms and applications. Indeed, many researchers have found that HPC applications
perform poorly on computer architectures that employ caches [BAIL93]. Other
researchers have since shown that a cache hierarchy can be useful in improving performance
if the application software is tuned to exploit the cache [WANG99, PRES01].
Although there are a large number of cache implementations, there are a few
basic design elements that serve to classify and differentiate cache architectures.
Table 5.1 lists key elements.

## Slide 8: Cache Addresses
Virtual Memory
Virtual memory
  Facility that allows programs to address memory from a logical point of view, without regard to the amount of main memory physically available
  When used, the address fields of machine instructions contain virtual addresses
  For reads to and writes from main memory, a hardware memory management unit (MMU) translates each virtual address into a physical address in main memory
Notes: Almost all nonembedded processors, and many embedded processors, support virtual
memory, a concept discussed in Chapter 9. In essence, virtual memory is a facility
that allows programs to address memory from a logical point of view, without
regard to the amount of main memory physically available. When virtual memory is
used, the address fields of machine instructions contain virtual addresses. For reads
to and writes from main memory, a hardware memory management unit (MMU)
translates each virtual address into a physical address in main memory.
When virtual addresses are used, the system designer may choose to place
the cache between the processor and the MMU or between the MMU and main
memory (Figure 5.5). A logical cache , also known as a virtual cache , stores data
using virtual addresses . The processor accesses the cache directly, without going
through the MMU. A physical cache stores data using main memory physical
addresses.
One obvious advantage of the logical cache is that cache access speed is faster
than for a physical cache, because the cache can respond before the MMU performs
an address translation. The disadvantage has to do with the fact that most virtual
memory systems supply each application with the same virtual memory address
space. That is, each application sees a virtual memory that starts at address 0. Thus,
the same virtual address in two different applications refers to two different physical
addresses. The cache memory must therefore be completely flushed with each
application context switch, or extra bits must be added to each line of the cache to
identify which virtual address space this address refers to.
.

## Slide 9: Figure 5.5 Logical and Physical Caches
Notes: Figure 5.5. Logical and Physical Caches

## Slide 10: Cache Size
Preferable for the size of the cache to be:
    Small enough so that the overall average cost per bit is close to that of main memory alone
    Large enough so that the overall average access time is close to that of the cache alone
    Motivations for minimizing cache size:
    The larger the cache, the larger the number of gates involved in addressing the cache resulting in large caches being slightly slower than small ones
    The available chip and board area also limits cache size
    Because the performance of the cache is very sensitive to the nature of the workload, it is impossible to arrive at a single “optimum” cache size
Notes: The second item in Table 5.1, cache size, has already been discussed. We would
like the size of the cache to be small enough so that the overall average cost per
bit is close to that of main memory alone and large enough so that the overall
average access time is close to that of the cache alone. There are several other
motivations for minimizing cache size. The larger the cache, the larger the number
of gates involved in addressing the cache. The result is that large caches tend to be
slightly slower than small ones—even when built with the same integrated circuit
technology and put in the same place on a chip and circuit board. The available
chip and board area also limits cache size. Because the performance of the cache
is very sensitive to the nature of the workload, it is impossible to arrive at a single
“optimum” cache size.

## Slide 11: Table 5.2 Cache Sizes of Some Processors
Processor | Type | Year of Introduction | L1 Cachea | L2 cache | L3 Cache
IBM 360/85 | Mainframe | 1968 | 16 to 32 kB | – | –
PDP-11/70 | Minicomputer | 1968 | 1 kB | – | –
IBM 3033 | Mainframe | 1968 | 64 kB | – | –
IBM 3090 | Mainframe | 1968 | 128 to 256 kB | – | –
Intel 80486 | PC | 1968 | 8 kB | – | –
Pentium | PC | 1968 | 8 kB/8 kB | 256 to 512 kB | –
PowerPC 620 | PC | 1968 | 32 kB/32 kB | – | –
IBM S/390 G6 | Mainframe | 1968 | 256 kB | 8 MB | –
Pentium 4 | PC/server | 1968 | 8 kB/8 kB | 256 kB | –
Itanium | PC/server | 1968 | 16 kB/16 kB | 96 kB | 4 MB
Itanium 2 | PC/server | 1968 | 32 kB | 256 kB | 6 MB
IBM POWER5 | High-end server | 1968 | 64 kB | 1.9 MB | 36 MB
CRAY XD-1 | Supercomputer | 1968 | 64 kB/64 kB | 1 MB | –
IBM POWER6 | PC/server | 1968 | 64 kB/64 kB | 4 MB | 32 MB
IBM z10 | Mainframe | 1968 | 64 kB/128 kB | 3 MB | 24-48 MB
Intel Core i7 EE 990 | Workstaton/ Server | 1968 | 6 × 32 kB/32 kB | 6 × 1.5 MB | 12 MB
IBM zEnterprise 196 | Mainframe/ Server | 1968 | 24 × 64 kB/128 kB | 24 × 1.5 MB | 24 MB L3 192 MB L4
IBM z13 | Mainframe/ server | 1968 | 24 × 96 kB/128 kB | 24 × 2 MB/2 MB | 64 MB L3 480 MB L4
Intel Core i0-7900X | Workstation/ server | 1968 | 8 × 32 kB/32 kB | 8 × 1 MB | 14 MB
a Two values separated by a slash refer to instruction and data caches.
(Table can be found on page 145 in the textbook.)
Notes: Table 5.2 lists the cache sizes of some current and past
processors

## Slide 12: Table 5.3 Cache Access Methods
Method | Organization | Mapping of Main Memory Blocks to Cache | Access using Main Memory Address
Direct Mapped | Sequence of m lines | Each block of main memory maps to one unique line of cache. | Line portion of address used to access cache line; Tag portion used to check for hit on that line.
Fully Associative | Sequence of m lines | Each block of main memory can map to any line of cache. | Tag portion of address used to check every line for hit on that line.
Set Associative | Sequence of m lines organized as v sets of k lines each (m = v × k) | Each block of main memory maps to one unique cache set. | Line portion of address used to access cache set; Tag portion used to check every line in that set for hit on that line.
Notes: Because there are fewer cache lines than main memory blocks, an algorithm is needed
for mapping main memory blocks into cache lines. Further, a means is needed for
determining which main memory block currently occupies a cache line. The choice
of the mapping function dictates how the cache is logically organized.
Three techniques can be used: direct, associative, and set-associative. We examine each of these
in turn. In each case, we look at the general structure and then a specific example.
Table 5.3 provides a summary of key characteristics of the three approaches.

## Slide 13: Figure 5.6 Mapping from Main Memory to Cache: Direct and Associative
Notes: The simplest technique, known as direct mapping, maps
each block of main memory into only one possible cache line.
The mapping is expressed as
i = j modulo m
where
i = cache line number
j = main memory block number
m = number of lines in the cache
Figure 5.6a shows the mapping for the first m blocks of main memory.
Each block of main memory maps into one unique line of the cache. The next
m blocks of main memory map into the cache in the same fashion; that is, block Bm
of main memory maps into line L0 of cache, block Bm+1 maps into line L1 , and so on.

## Slide 14: Figure 5.7 Direct-Mapping Cache Organization
Notes: The mapping function is easily implemented using the main memory address.
Figure 5.7 illustrates the general mechanism.
Figure 5.7 indicates the logical structure of the cache hardware access mechanism.
When the cache hardware is presented with an address from the processor,
the Line Number portion of the address is used to index into the cache. A compare
function compares the tag of that line with the Tag field of the address. If there is a
match (hit), an enable signal is sent to a select function, which uses the Offset field
of the address and the Line Number field of the address to read the desired word or
byte from the cache. If there is no match (miss) then the select function is not enabled
and data is accessed from main memory, or the next level of cache. Figure 5.7
illustrates the case in which the line number refers to the third line in the cache and
there is a match, as indicated by the heavier arrowed lines.
The direct mapping technique is simple and inexpensive to implement. Its
main disadvantage is that there is a fixed cache location for any given block. Thus,
if a program happens to reference words repeatedly from two different blocks that
map into the same line, then the blocks will be continually swapped in the cache,
and the hit ratio will be low (a phenomenon known as thrashing ).

## Slide 15: Figure 5.8 Direct Mapping Example
Notes: Figure 5.8. Direct Mapping Example
Figure 5.8 shows our example system using direct mapping. In the example,
m = 16K = 214 and i = j modulo 214. The mapping becomes
Cache Line Starting Memory Address of Block
0 000000, 010000, …, FF0000
1 000004, 010004, …, FF0004
. .
. .
. .
214 - 1 00FFFC, 01FFFC, …, FFFFFC
Note that no two blocks that map into the same line number have the same tag number. Thus,
blocks with starting addresses 000000, 010000, …, FF0000 have tag numbers 00, 01, …, FF, respectively.
Referring back to Figure 5.3, a read operation works as follows. The cache system is presented
with a 24-bit address. The 14-bit line number is used as an index into the cache to access a particular
line. If the 8-bit tag number matches the tag number currently stored in that line, then the 2-bit word
number is used to select one of the 4 bytes in that line. Otherwise, the 22-bit tag-plus-line
field is used to fetch a block from main memory. The actual address that is used for the fetch is the 22-bit
tag-plus-line concatenated with two 0 bits, so that 4 bytes are fetched starting on a block boundary.

## Slide 16: Content-Addressable Memory (CAM)
Also known as associative storage
Content-addressable memory is constructed of static RAM (SRAM) cells but is considerably more expensive and holds much less data than regular SRAM chips
A CAM with the same data capacity as a regular SRAM is about 60% larger
A CAM is designed such that when a bit string is supplied, the CAM searches its entire memory in parallel for a match
    If the content is found, the CAM returns the address where the match is found and, in some architectures, also returns the associated data word
    This process takes only one clock cycle
Notes: Before discussing associative cache
organization, we need to introduce the concept of content-addressable memory (CAM),
also known as associative storage [PAGI06]. Content-addressable memory (CAM) is
constructed of static RAM (SRAM) cells (see static RAM) but is considerably more
expensive and holds much less data than regular SRAM chips. Put another way, a
CAM with the same data capacity as a regular SRAM is about 60% larger [SHAR03].
A CAM is designed such that when a bit string is supplied, the CAM searches
its entire memory in parallel for a match. If the content is found, the CAM returns
the address where the match is found and, in some architectures, also returns the
associated data word. This process takes only one clock cycle.

## Slide 17: Figure 5.9 Content-Addressable Memory
Notes: Figure 5.9a is a simplified illustration of the search function of a small CAM
with four horizontal words, each word containing five bits, or cells. CAM cells
contain both storage and comparison circuitry. The is a match line corresponding
to each word, feeding into match line sense amplifiers, and there is a differential
search line pair corresponding to each bit of the search word. The encoder maps the
match line of the matching location to its encoded address.
Figure 5.9b shows a logical block diagram of a CAM cell array, consisting of m
words of n bits each. Search, read, and write enable pins are used to enable one of the
three operating modes of the CAM. For a search operation, the data to be searched
is loaded in an n-bit search register that sets/resets the logic states of the search lines.
The logic within and between cells of a row is such that a match lines is asserted if and
only if all the cells in a row match the search line values. A simple read operation,
as opposed to a search, is performed to read the data stored in the storage nodes of
CAM cells using Read Enable control signal. The data words to be stored in CAM
cell array are provided during a write operation through data input port.

## Slide 18: Figure 5.10 Fully Associative Cache Organization
Notes: Associative mapping overcomes the disadvantage of
direct mapping by permitting each main memory block to be loaded into any line
of the cache (Figure 5.6b). In this case, the cache control logic interprets a memory
address simply as a Tag and a Word field. The Tag field uniquely identifies a block
of main memory. To determine whether a block is in the cache, the cache control
logic must simultaneously examine every line’s tag for a match. Figure 5.10
illustrates the logic.
Note that no field in the address corresponds to the line number, so that the number
of lines in the cache is not determined by the address format. Instead, if there is a
hit, the line number of the hit is sent to the select function by the cache hardware, as
shown in Figure 5.9.

## Slide 19: Figure 5.11 Associative Mapping Example
Notes: With associative mapping, there is flexibility as to which block to replace when
a new block is read into the cache. Replacement algorithms, discussed later in this
section, are designed to maximize the hit ratio. The principal disadvantage of associative
mapping is the complex circuitry required to examine the tags of all cache
lines in parallel.
Figure 5.11 shows our example using associative mapping. A main
memory address consists of a 22-bit tag and a 2-bit byte number. The 22-bit tag must be
stored with the 32-bit block of data for each line in the cache. Note that it is the leftmost
(most significant) 22 bits of the address that form the tag. Thus, the 24-bit hexadecimal
address 16339C has the 22-bit tag 058CE7. This is easily seen in binary notation:
memory address 0001 0110 0011 0011 1001 1100 (binary)
1 6 3 3 9 C (hex)
tag (leftmost 22 bits) 00 0101 1000 1100 1110 0111 (binary)
0 5 8 C E 7 (hex)
With associative mapping, there is flexibility as to which block to replace when
a new block is read into the cache. Replacement algorithms, discussed later in this
section, are designed to maximize the hit ratio. The principal disadvantage of associative
mapping is the complex circuitry required to examine the tags of all cache
lines in parallel.

## Slide 20: Set Associative Mapping
Compromise that exhibits the strengths of both the direct and associative approaches while reducing their disadvantages
Cache consists of a number of sets
Each set contains a number of lines
A given block maps to any line in a given set
e.g. 2 lines per set
  2 way associative mapping
  A given block can be in one of 2 lines in only one set
Notes: Set-associative mapping is a compromise that
exhibits the strengths of both the direct and associative approaches while reducing
their disadvantages.
In this case, the cache consists of a number sets, each of which consists of a
number of lines. The relationships are
m = v* k
i = j modulo v
where
i = cache set number
j = main memory block number
m = number of lines in the cache
v = number of sets
k = number of lines in each set
This is referred to as k-way set-associative mapping. With set-associative
mapping block Bj can be mapped into any of the lines of set j.

## Slide 21: Figure 5.12 Mapping from Main Memory to Cache: k-Way Set Associative
Notes: Figure 5.12a illustrates
this mapping for the first v blocks of main memory. As with associative mapping,
each word maps into multiple cache lines. For set-associative mapping, each word
maps into all the cache lines in a specific set, so that main memory block B0 maps
into set 0, and so on. Thus, the set-associative cache can be physically implemented
as n associative caches. It is also possible to implement the set-associative cache as
k direct mapping caches, as shown in Figure 5.12b. Each direct-mapped cache is
referred to as a way, consisting of v lines. The first v lines of main memory are direct
mapped into the v lines of each way; the next group of v lines of main memory are
similarly mapped, and so on. The direct-mapped implementation is typically used
for small degrees of associativity (small values of k) while the associative-mapped
implementation is typically used for higher degrees of associativity [JACO08].

## Slide 22: Figure 5.13 k-Way Set Associative Cache Organization
Notes: For set-associative mapping, the cache control logic interprets a memory
address as three fields: Tag, Set, and Word. The d set bits specify one of v = 2d sets.
The s bits of the Tag and Set fields specify one of the 2s blocks of main memory.
Figure 5.13 illustrates the cache control logic. With fully associative mapping, the
tag in a memory address is quite large and must be compared to the tag of every line
in the cache. With k-way set-associative mapping, the tag in a memory address is
much smaller and is only compared to the k tags within a single set. As shown in
Figure 5.12, if there is match of tags on any of the lines in the set, the corresponding
select function is enabled and retrieves the desired work. If all comparisons report a
miss, then the desired word is retrieved from main memory.

## Slide 23: Figure 5.14 Two-Way Set-Associative Mapping Example
Notes: Figure 5.14 shows our example using set-associative
mapping with two lines in each set, referred to as two-way
set-associative. The 13-bit set number identifies
a unique set of two lines within the cache. It also gives the number of the block in
main memory, modulo 213. This determines the mapping of blocks into lines. Thus, blocks
000000, 008000, …, FF8000 of main memory map into cache set 0. Any of those blocks can
be loaded into either of the two lines in the set. Note that no two blocks that map into the
same cache set have the same tag number. For a read operation, the 13-bit set number is
used to determine which set of two lines is to be examined. Both lines in the set are examined
for a match with the tag number of the address to be accessed.
In the extreme case of v = m , k = 1, the set-associative
technique reduces to direct mapping, and for v = 1, k = m , it reduces to associative mapping. The use of
two lines per set (v = m /2, k = 2) is the most common set-associative
organization. It significantly improves the hit ratio over direct mapping. Four- way set associative
(v = m /4, k = 4) makes a modest additional improvement for a relatively small
additional cost [MAYB84, HILL89]. Further increases in the number of lines per
set have little effect.

## Slide 24: Figure 5.15 Varying Associativity over Cache Size
Notes: Figure 5.15 shows the results of one simulation study of set-associative cache
performance as a function of cache size [GENU04]. The difference in performance
between direct and two-way set associative is significant up to at least a cache size of
64 kB. Note also that the difference between two-way and four-way at 4 kB is much
less than the difference in going from for 4 kB to 8 kB in cache size. The complexity
of the cache increases in proportion to the associativity, and in this case would not
be justifiable against increasing cache size to 8 or even 16 Kbytes. A final point to
note is that beyond about 32 kB, increase in cache size brings no significant increase
in performance.
The results of Figure 5.15 are based on simulating the execution of a GCC
compiler. Different applications may yield different results. For example, [CANT01]
reports on the results for cache performance using many of the CPU2000 SPEC
benchmarks. The results of [CANT01] in comparing hit ratio to cache size follow
the same pattern as Figure 5.15, but the specific values are somewhat different.

## Slide 25: Replacement Algorithms
Once the cache has been filled, when a new block is brought into the cache, one of the existing blocks must be replaced
For direct mapping there is only one possible line for any particular block and no choice is possible
For the associative and set-associative techniques a replacement algorithm is needed
To achieve high speed, an algorithm must be implemented in hardware
Notes: Once the cache has been filled, when a new block is brought into the cache, one
of the existing blocks must be replaced. For direct mapping, there is only one possible
line for any particular block, and no choice is possible. For the associative
and set-associative techniques, a replacement algorithm is needed. To achieve high
speed, such an algorithm must be implemented in hardware.

## Slide 26: The most common replacement algorithms are:
Least recently used (LRU)
  Most effective
  Replace that block in the set that has been in the cache longest with no reference to it
  Because of its simplicity of implementation, LRU is the most popular replacement algorithm
First-in-first-out (FIFO)
  Replace that block in the set that has been in the cache longest
  Easily implemented as a round-robin or circular buffer technique
Least frequently used (LFU)
  Replace that block in the set that has experienced the fewest references
  Could be implemented by associating a counter with each line
Notes: A number of algorithms
have been tried. We mention four of the most common. Probably the most
effective is least recently used (LRU): Replace that block in the set that has been in
the cache longest with no reference to it. For two-way set associative, this is easily
implemented. Each line includes a USE bit. When a line is referenced, its USE bit
is set to 1 and the USE bit of the other line in that set is set to 0. When a block is to
be read into the set, the line whose USE bit is 0 is used. Because we are assuming
that more recently used memory locations are more likely to be referenced, LRU
should give the best hit ratio. LRU is also relatively easy to implement for a fully
associative cache. The cache mechanism maintains a separate list of indexes to all
the lines in the cache. When a line is referenced, it moves to the front of the list.
For replacement, the line at the back of the list is used. Because of its simplicity of
implementation, LRU is the most popular replacement algorithm.
Another possibility is first-in-first-out (FIFO): Replace that block in the set
that has been in the cache longest. FIFO is easily implemented as a round-robin
or circular buffer technique. Still another possibility is least frequently used (LFU):
Replace that block in the set that has experienced the fewest references. LFU could
be implemented by associating a counter with each line. A technique not based on
usage (i.e., not LRU, LFU, FIFO, or some variant) is to pick a line at random from
among the candidate lines. Simulation studies have shown that random replacement
provides only slightly inferior performance to an algorithm based on usage [SMIT82].

## Slide 27: Write Policy
When a block that is resident in the cache is to be replaced there are two cases to consider:
If the old block in the cache has not been altered then it may be overwritten with a new block without first writing out the old block
If at least one write operation has been performed on a word in that line of the cache then main memory must be updated by writing the line of cache out to the block of memory before bringing in the new block
There are two problems to contend with:
More than one device may have access to main memory
A more complex problem occurs when multiple processors are attached to the same bus and each processor has its own local cache - if a word is altered in one cache it could conceivably invalidate a word in other caches
Notes: When a block that is resident in the cache is to be replaced, there are two cases to
consider. If the old block in the cache has not been altered, then it may be overwritten
with a new block without first writing out the old block. If at least one write
operation has been performed on a word in that line of the cache, then main memory
must be updated by writing the line of cache out to the block of memory before
bringing in the new block. A variety of write policies, with performance and economic
trade-offs, is possible. There are two problems to contend with. First, more
than one device may have access to main memory. For example, an I/O module
may be able to read-write directly to memory. If a word has been altered only in the
cache, then the corresponding memory word is invalid. Further, if the I/O device
has altered main memory, then the cache word is invalid. A more complex problem
occurs when multiple processors are attached to the same bus and each processor
has its own local cache. Then, if a word is altered in one cache, it could conceivably
invalidate a word in other caches.

## Slide 28: Write Through and Write Back
Write through
  Simplest technique
  All write operations are made to main memory as well as to the cache
  The main disadvantage of this technique is that it generates substantial memory traffic and may create a bottleneck
Write back
  Minimizes memory writes
  Updates are made only in the cache
  Portions of main memory are invalid and hence accesses by I/O modules can be allowed only through the cache
  This makes for complex circuitry and a potential bottleneck
Notes: The simplest technique is called write through. Using this technique, all write
operations are made to main memory as well as to the cache, ensuring that main
memory is always valid. Any other processor–cache module can monitor traffic to
main memory to maintain consistency within its own cache. The main disadvantage
of this technique is that it generates substantial memory traffic and may create a bottleneck.
An alternative technique, known as write back, minimizes memory writes.
With write back, updates are made only in the cache. When an update occurs, a
dirty bit, or use bit, associated with the line is set. Then, when a block is replaced, it
is written back to main memory if and only if the dirty bit is set. The problem with
write back is that portions of main memory are invalid, and hence accesses by I/O
modules can be allowed only through the cache. This makes for complex circuitry
and a potential bottleneck. Experience has shown that the percentage of memory
references that are writes is on the order of 15% [SMIT82]. However, for HPC
applications, this number may approach 33% (vector-vector multiplication) and can
go as high as 50% (matrix transposition).

## Slide 29: Write Miss Alternatives
There are two alternatives in the event of a write miss at a cache level:
    Write allocate
        The block containing the word to be written is fetched from main memory (or next level cache) into the cache and the processor proceeds with the write cycle
    No write allocate
        The block containing the word to be written is modified in the main memory and not loaded into the cache
Either of these policies can be used with either write through or write back
No write allocate is most commonly used with write through
Write allocate is most commonly used with write back
Notes: There is another dimension to the write policy when a miss occurs at a cache
level. There are two alternatives in the event of a write miss:
■ Write Allocate: The block containing the word to be written is fetched from
main memory (or next level cache) into the cache and the processor proceeds
with the write cycle.
■ No Write Allocate: The block containing the word to be written is modified in
the main memory and not loaded into the cache.
Either of these policies can be used with either write through or write back.
Most commonly, no write allocate is used with write through. The reasoning is that
even if locality holds and a write will be made to the same block in the near future,
the write-through policy will generate a write to main memory anyway, so bringing
the block into the cache does not seem efficient. For example, the ARM Cortex
processors can be configured to use write allocate or no write allocate with write
back, but only no write allocate with write through.
With write back, write allocate is most commonly used, although some systems,
such as the ARM Cortex, also allow no write allocate. The reasoning for using
write allocate is that subsequent writes to the same block, if the block originally
caused a miss, will hit in the cache next time, setting the dirty bit for the block. That
will eliminate extra memory accesses and result in efficient execution. The write
back, no write allocate option eliminates the time spent in bringing a block into
the cache. Depending on locality patterns for reads and writes, there may be some
advantage to this technique.

## Slide 30: Cache Coherency
A new problem is introduced in a bus organization in which more than one device has a cache and main memory is shared
If data in one cache are altered, this invalidates not only the corresponding word in main memory, but also that same word in other caches
Even if a write-through policy is used, the other caches may contain invalid data
Possible approaches to cache coherency include:
    Bus watching with write through
        Each cache controller monitors the address lines to detect write operations to memory by other bus masters
        If another master writes to a location in shared memory that also resides in the cache memory, the cache controller invalidates that cache entry
        This strategy depends on the use of a write-through policy by all cache controllers
    Hardware transparency
        Additional hardware is used to ensure that all updates to main memory via cache are reflected in all caches
        If one processor modifies a word in its cache, this update is written to main memory
    Noncacheable memory
        Only a portion of main memory is shared by more than one processor, and this is designated as noncacheable
        All accesses to shared memory are cache misses, because the shared memory is never copied into the cache
        The noncacheable memory can be identified using chip-select logic or high-address bits
Notes: In a bus organization in which more than one device (typically a processor)
has a cache and main memory is shared, a new problem is introduced. If data in one
cache are altered, this invalidates not only the corresponding word in main memory,
but also that same word in other caches (if any other cache happens to have that
same word). Even if a write-through policy is used, the other caches may contain
invalid data. A system that prevents this problem is said to maintain cache coherency.
Possible approaches to cache coherency include the following:
• Bus watching with write through: Each cache controller monitors the address
lines to detect write operations to memory by other bus masters. If another
master writes to a location in shared memory that also resides in the cache
memory, the cache controller invalidates that cache entry. This strategy depends
on the use of a write-through policy by all cache controllers.
• Hardware transparency: Additional hardware is used to ensure that all updates
to main memory via cache are reflected in all caches. Thus, if one processor
modifies a word in its cache, this update is written to main memory. In addition,
any matching words in other caches are similarly updated.
• Non-cacheable memory: Only a portion of main memory is shared by more
than one processor, and this is designated as non-cacheable. In such a system,
all accesses to shared memory are cache misses, because the shared memory
is never copied into the cache. The non-cacheable memory can be identified
using chip-select logic or high-address bits.

## Slide 31: Line Size
When a block of data is retrieved and placed in the cache not only the desired word but also some number of adjacent words are retrieved
As the block size increases the hit ratio will at first increase because of the principle of locality
As the block size increases more useful data are brought into the cache
The hit ratio will begin to decrease as the block becomes bigger and the probability of using the newly fetched information becomes less than the probability of reusing the information that has to be replaced
Two specific effects come into play:
Larger blocks reduce the number of blocks that fit into a cache
As a block becomes larger each additional word is farther from the requested word
Notes: Another design element is the line size. When a block of data is retrieved and placed
in the cache, not only the desired word but also some number of adjacent words are
retrieved. As the block size increases from very small to larger sizes, the hit ratio
will at first increase because of the principle of locality, which states that data in the
vicinity of a referenced word are likely to be referenced in the near future. As the
block size increases, more useful data are brought into the cache. The hit ratio will
begin to decrease, however, as the block becomes even bigger and the probability
of using the newly fetched information becomes less than the probability of reusing
the information that has to be replaced. Two specific effects come into play:
• Larger blocks reduce the number of blocks that fit into a cache. Because each
block fetch overwrites older cache contents, a small number of blocks results
in data being overwritten shortly after they are fetched.
• As a block becomes larger, each additional word is farther from the requested
word and therefore less likely to be needed in the near future.
The relationship between block size and hit ratio is complex, depending on
the locality characteristics of a particular program, and no definitive optimum value
has been found. A size of from 8 to 64 bytes seems reasonably close to optimum
[SMIT87, PRZY88, PRZY90, HAND98]. For HPC systems, 64- and 128-byte cache
line sizes are most frequently used.

## Slide 32: Multilevel Caches
As logic density has increased it has become possible to have a cache on the same chip as the processor
The on-chip cache reduces the processor’s external bus activity and speeds up execution time and increases overall system performance
  When the requested instruction or data is found in the on-chip cache, the bus access is eliminated
  On-chip cache accesses will complete appreciably faster than would even zero-wait state bus cycles
  During this period the bus is free to support other transfers
Two-level cache:
  Internal cache designated as level 1 (L1)
  External cache designated as level 2 (L2)
Potential savings due to the use of an L2 cache depends on the hit rates in both the L1 and L2 caches
The use of multilevel caches complicates all of the design issues related to caches, including size, replacement algorithm, and write policy
Notes: As logic density has increased, it has become possible to
have a cache on the same chip as the processor: the on-chip cache. Compared with
a cache reachable via an external bus, the on-chip cache reduces the processor’s
external bus activity and therefore speeds up execution times and increases overall
system performance. When the requested instruction or data is found in the on-chip
cache, the bus access is eliminated. Because of the short data paths internal to
the processor, compared with bus lengths, on-chip cache accesses will complete
appreciably faster than would even zero-wait state bus cycles. Furthermore, during
this period the bus is free to support other transfers.
The inclusion of an on-chip cache leaves open the question of whether an
off-chip, or external, cache is still desirable. Typically, the answer is yes, and most contemporary
designs include both on-chip and external caches. The simplest such organization
is known as a two-level cache, with the internal cache designated as level 1 (L1)
and the external cache designated as level 2 (L2). The reason for including an L2 cache
is the following: If there is no L2 cache and the processor makes an access request
for a memory location not in the L1 cache, then the processor must access DRAM or
ROM memory across the bus. Due to the typically slow bus speed and slow memory
access time, this results in poor performance. On the other hand, if an L2 SRAM (static
RAM) cache is used, then frequently the missing information can be quickly retrieved.
If the SRAM is fast enough to match the bus speed, then the data can be accessed
using a zero-wait state transaction, the fastest type of bus transfer.
Two features of contemporary cache design for multilevel caches are noteworthy.
First, for an off-chip L2 cache, many designs do not use the system bus as
the path for transfer between the L2 cache and the processor, but use a separate
data path, so as to reduce the burden on the system bus. Second, with the continued
shrinkage of processor components, a number of processors now incorporate the L2
cache on the processor chip, improving performance.
The potential savings due to the use of an L2 cache depends on the hit rates
in both the L1 and L2 caches. Several studies have shown that, in general, the use
of a second-level cache does improve performance (e.g., see [AZIM92], [NOVI93],
[HAND98]). However, the use of multilevel caches does complicate all of the design
issues related to caches, including size, replacement algorithm, and write policy; see
[HAND98] and [PEIR99] for discussions.

## Slide 33: Figure 5.16 Total Hit Ratio (L1 and L2) for 8-kB and 16-kB L1
Notes: Figure 5.16 shows the results of one simulation study of two-level cache performance
as a function of cache size [GENU04]. The figure assumes that both
caches have the same line size and shows the total hit ratio. That is, a hit is counted
if the desired data appears in either the L1 or the L2 cache. The figure shows the
impact of L2 on total hits with respect to L1 size. L2 has little effect on the total
number of cache hits until it is at least double the L1 cache size. Note that the steepest
part of the slope for an L1 cache of 8 Kbytes is for an L2 cache of 16 Kbytes.
Again for an L1 cache of 16 Kbytes, the steepest part of the curve is for an L2 cache
size of 32 Kbytes. Prior to that point, the L2 cache has little, if any, impact on total
cache performance. The need for the L2 cache to be larger than the L1 cache to
affect performance makes sense. If the L2 cache has the same line size and capacity
as the L1 cache, its contents will more or less mirror those of the L1 cache.
With the increasing availability of on-chip area available for cache, most contemporary
microprocessors have moved the L2 cache onto the processor chip and
added an L3 cache. Originally, the L3 cache was accessible over the external bus.
More recently, most microprocessors have incorporated an on-chip L3 cache. In
either case, there appears to be a performance advantage to adding the third level
(e.g., see [GHAI98]). Further, large systems, such as the IBM mainframe zEnterprise
systems, now incorporate 3 on-chip cache levels and a fourth level of cache
shared across multiple chips [BART15

## Slide 34: Unified Versus Split Caches
Has become common to split cache:
  One dedicated to instructions
  One dedicated to data
  Both exist at the same level, typically as two L1 caches
Advantages of unified cache:
  Higher hit rate
    Balances load of instruction and data fetches automatically
    Only one cache needs to be designed and implemented
Trend is toward split caches at the L1 and unified caches for higher levels
Advantages of split cache:
  Eliminates cache contention between instruction fetch/decode unit and execution unit
    Important in pipelining
Notes: When the on-chip cache first made an appearance,
many of the designs consisted of a single cache used to store references to both data
and instructions. More recently, it has become common to split the cache into two:
one dedicated to instructions and one dedicated to data. These two caches both exist
at the same level, typically as two L1 caches. When the processor attempts to fetch an
instruction from main memory, it first consults the instruction L1 cache, and when the
processor attempts to fetch data from main memory, it first consults the data L1 cache.
There are two potential advantages of a unified cache:
• For a given cache size, a unified cache has a higher hit rate than split caches
because it balances the load between instruction and data fetches automatically.
That is, if an execution pattern involves many more instruction fetches
than data fetches, then the cache will tend to fill up with instructions, and if an
execution pattern involves relatively more data fetches, the opposite will occur.
• Only one cache needs to be designed and implemented.
The trend is toward split caches at the L1 and unified caches for higher levels,
particularly for superscalar machines, which emphasize parallel instruction execution
and the prefetching of predicted future instructions. The key advantage of the
split cache design is that it eliminates contention for the cache between the instruction
fetch/decode unit and the execution unit. This is important in any design that
relies on the pipelining of instructions. Typically, the processor will fetch instructions
ahead of time and fill a buffer, or pipeline, with instructions to be executed. Suppose
now that we have a unified instruction/data cache. When the execution unit performs
a memory access to load and store data, the request is submitted to the unified cache.
If, at the same time, the instruction prefetcher issues a read request to the cache for
an instruction, that request will be temporarily blocked so that the cache can service
the execution unit first, enabling it to complete the currently executing instruction.
This cache contention can degrade performance by interfering with efficient use of
the instruction pipeline. The split cache structure overcomes this difficulty.

## Slide 35: Inclusion Policy
Inclusive policy
    Dictates that a piece of data in one cache is guaranteed to be also found in all lower levels of caches
    Advantage is that it simplifies searching for data when there are multiple processors in the computing system
    This property is useful in enforcing cache coherence
Exclusive policy
    Dictates that a piece of data in one cache is guaranteed not to be found in all lower levels of caches
    The advantage is that it does not waste cache capacity since it does not store multiple copies of the same data in all of the caches
    The disadvantage is the need to search multiple cache levels when invalidating or updating a block
    To minimize the search time, the highest-level tag sets are typically duplicated at the lowest cache level to centralize searching
Noninclusive policy
    With the noninclusive policy a piece of data in one cache may or may not be found in lower levels of caches
    As with the exclusive policy, this policy will generally maintain all higher-level cache sets at the lowest cache level
Notes: Recall from Chapter 4 that we defined the inclusion principle for memory hierarchies
as follows: All information items are originally stored in level Mn , where n is the
level most remote from the processor (lowest level). During the processing, subsets of
Mn are copied into Mn –1. Similarity, subsets of Mn –1 are copied into Mn –2, and so on.
This is expressed concisely as Mi Mi +1. Thus, if a word is found in Mi , then copies of
the same word also exist in all lower layers Mi +1, Mi +2,…, Mn . In a multilevel cache
environment, in which there may be multiple caches at one level that share the same
cache at the next lower level, inclusion between these two levels may not always be
desirable. Three inclusion policies are found in contemporary cache systems:
The inclusive policy dictates that a piece of data in one cache is guaranteed to
be also found in all lower levels of caches. The advantage of the inclusive policy is that
it simplifies searching for data when there are multiple processors in the computing
system. For example, if one processor wants to know whether another processor has
the data it needs, it does not need to search all levels of caches of that other processor
but only the lowest-level cache. This property is useful in enforcing cache coherence,
which is discussed in Chapter 20.
The exclusive policy dictates that a piece of data in one cache is guaranteed
not to be found in all lower levels of caches. The advantage of the exclusive policy
is that it does not waste cache capacity since it does not store multiple copies of
the same data in all of the caches. The disadvantage is the need to search multiple
cache levels when invalidating or updating a block. To minimize the search time, the
higher-level tag sets are typically duplicated at the lowest cache level to centralize
searching.
With the noninclusive policy , a piece of data in one cache may or may not be
found in lower levels of caches. This can be contrasted with the other two policies with
the following examples. Suppose that the L2 line size is a multiple of the L1 line size.
For the inclusive policy, if a block is evicted from the L2 cache, the corresponding multiple
blocks will be evicted from the L1 cache. In contrast, with a noninclusive policy,
the L1 cache my retain portions of a block recently evicted from the L2 cache. For the
same difference in block size, if a portion of a block is promoted from the L2 cache to
the L1 cache, the exclusive policy requires the entire L2 block be evicted. In contrast,
the noninclusive policy does not require this eviction. As with the exclusive policy,
a noninclusive policy will generally maintain all higher-level cache sets at the lowest
cache level.

## Slide 36: Table 5.4 Intel Cache Evolution
Problem | Solution | Processor on Which Feature First Appears
External memory slower than the system bus. | Add external cache using faster memory technology. | 386
Increased processor speed results in external bus becoming a bottleneck for cache access. | Move external cache on-chip, operating at the same speed as the processor. | 486
Internal cache is rather small, due to limited space on chip. | Add external L2 cache using faster technology than main memory. | 486
Contention occurs when both the Instruction Prefetcher and the Execution Unit simultaneously require access to the cache. In that case, the Prefetcher is stalled while the Execution Unit’s data access takes place. | Create separate data and instruction caches. | Pentium
Increased processor speed results in external bus becoming a bottleneck for L2 cache access. | Create separate back-side bus that runs at higher speed than the main (front-side) external bus. The BSB is dedicated to the L2 cache. | Pentium Pro
 | Move L2 cache on to the processor chip. | Pentium II
Some applications deal with massive databases and must have rapid access to large amounts of data. The on-Chip caches are too small. | Add external L3 cache. | Pentium III
 | Move L3 cache on-chip. | Pentium 4
Notes: The evolution of cache organization is seen clearly in the evolution of Intel microprocessors
(Table 5.4). The 80386 does not include an on-chip cache. The 80486
includes a single on-chip cache of 8 kB, using a line size of 16 bytes and a four-way
set-associative organization. All of the Pentium processors include two on-chip
L1 caches, one for data and one for instructions. For the Pentium 4, the L1 data
cache is 16 kB, using a line size of 64 bytes and a four-way set-associative organization.
The Pentium 4 instruction cache is described subsequently. The Pentium II
also includes an L2 cache that feeds both of the L1 caches. The L2 cache is eight-way
set associative with a size of 512 kB and a line size of 128 bytes. An L3 cache
was added for the Pentium III and became on-chip with high-end versions of the
Pentium 4.

## Slide 37: Figure 5.17 Pentium 4 Block Diagram
Notes: Figure 5.17 provides a simplified view of the Pentium 4 organization, highlighting
the placement of the three caches. This cache architecture is similar to those
of more modern x86 systems. The processor core consists of four major components:
■ Fetch/decode unit: Fetches program instructions in order from the L2 cache,
decodes these into a series of micro-operations,and stores the results in the L1
instruction cache.
■ Out-of-order execution logic: Schedules execution of the micro-operations
subject to data dependencies and resource availability; thus, micro-operations
may be scheduled for execution in a different order than they were fetched
from the instruction stream. As time permits, this unit schedules speculative
execution of micro-operations that may be required in the future.
■ Execution units: These units execute micro-operations, fetching the required
data from the L1 data cache and temporarily storing results in registers.
■ Memory subsystem: This unit includes the L2 and L3 caches and the system
bus, which is used to access main memory when the L1 and L2 caches have a
cache miss and to access the system I/O resources.
Unlike the organization used in all previous Pentium models, and in most
other processors, the Pentium 4 instruction cache sits between the instruction
decode logic and the execution core. The reasoning behind this design decision is as
follows: As discussed more fully in Chapter 18, the Pentium processor decodes, or
translates, Pentium machine instructions into simple RISC-like instructions called
micro-operations. The use of simple, fixed-length micro-operations
enables the use of superscalar pipelining and scheduling techniques that enhance performance.
However, the Pentium machine instructions are cumbersome to decode; they have
a variable number of bytes and many different options. It turns out that performance
is enhanced if this decoding is done independently of the scheduling and
pipelining logic. We return to this topic in Chapter 18.
The data cache employs a write-back policy: Data are written to main memory
only when they are removed from the cache and there has been an update.
The Pentium 4 processor can be dynamically configured to support write-
through caching.

## Slide 38: Table 5.5 Pentium 4 Cache Operating Modes
Control Bits |  | Operating Mode |  | 
CD | NW | Cache Fills | Write Throughs | Invalidates
0 | 0 | Enabled | Enabled | Enabled
1 | 0 | Disabled | Enabled | Enabled
1 | 1 | Disabled | Disabled | Disabled
Note: CD = 0; NW = 1 is an invalid combination.
Notes: The L1 data cache is controlled by two bits in one of the control registers, labeled
the CD (cache disable) and NW (not write-through) bits (Table 5.5). There are
also two Pentium 4 instructions that can be used to control the data cache: INVD
invalidates (flushes) the internal cache memory and signals the external cache (if
any) to invalidate. WBINVD writes back and invalidates internal cache and then
writes back and invalidates external cache.
Both the L2 and L3 caches are eight-way set-associative
with a line size of 128bytes.

## Slide 39: Figure 5.18 IBM z13 CPC Drawer Logical Structure
Notes: Figure 5.18 illustrates the logical interconnections of the z13 cache system,
showing the structure of a single processor drawer. A maximum system, called
a central processing complex (CPC) consists of four drawers. Each drawer consists
of two processor nodes, with each node containing 3 processor unit (PU) chips and
one storage control (SC) chip. Each PU includes up to 8 cores. The L1, L2, and L3
caches are contained on each PU chip, and a separate SC chip holds the L4 cache
for a processor node. Thus a maximum configuration contains 192 cores. Some key
characteristics of each level are as follows:
■ L1 cache: Each core contains a 96-kB L1 I-cache and a 128-kB D-cache, for
a maximum total of 18 MB of L1 I-cache and 24 MB of L1 D-cache. The L1
caches are designed as write-through caches.
■ L2 cache: Each core contains a 2-MB L2 I-cache and a 2-MB L2 D-cache, for
a maximum total of 384 MB of L2 I-cache and 384 MB of L2 D-cache. The L2
caches are designed as write-through caches.
■ L3 cache: Each PU chip contains a 64-MB L3 cache, for a maximum total of
1.5 GB of L3 cache. The L3 cache is 16-way set associative and uses a line size
of 256 bytes. The L3 cache uses the write-back policy.
■ L4 cache: Each processor node contains a 480-MB L4 cache for a maximum
total of 3.75 GB of L4 cache. The L4 cache is organized as a 30-way
set-associative cache. The L4 cache uses the write-back policy.
The use of an L3 cache that is shared by 8 cores on a chip facilitates low-latency
cross-processor cache line sharing and provides cache efficiency effects by elimination
of redundant lines (single copy, multiple users), which is not possible with
private caches. Thus, there are efficiency gains by devoting a substantial portion of
each PU chip to a shared L3 cache as opposed to either increasing the size of the L2
caches or providing private L3 caches for each core.
There are also efficiency benefits from providing an L4 cache chip on the same
processor node, or motherboard, as the PU chips. The L4 cache enables smooth
scaling from a single processor chip to a maximum system configuration by providing
a significant buffer before main memory.
The interconnection design contributes to the overall efficiency of this
arrangement. Within each PU chip, 160-GB/s bus bandwidth is used between L1/L2
and L2/L3 cache boundaries. The 80-GB/s XBus provides tightly coupled interconnection
within a node at the L3/L4 cache boundary. The high-speed S-Bus connects
via L4 between the nodes of a drawer, and A-Bus connections are provide to other
drawers.
The cache write policy is tailored to the configuration. The L1 and L2 caches
are write-through, taking advantage of the high-speed on-chip connection to the
next cache level. Further, the L3 cache is most efficiently used if it always maintains
the most recent version of any L2 cache line. Going from L3 to L4 is a lower speed,
off-chip transmission and here a write-back policy is preferred to minimize traffic.
Similarly, write-back is preferred going from L4 to main memory.

## Slide 40: Cache Timing Model
Direct-mapped cache access
    The first operation is checking the Tag field of an address against the tag value in the line designated by the Line field
    If there is not a match (miss), the operation is complete
    If there is a match (hit), the cache hardware reads the data block from the line in the cache and then fetches the byte or word indicated by the Offset field of the address
    An advantage is that it allows simple and fast speculation
Fully associative cache
    The line number is not known until the tag comparison is competed
    The hit time is the same as for direct-mapped
    Because this is a content-addressable memory, the miss time is simply the tag comparison time
Set associative
    It is not possible to transmit bytes and compare tags in parallel as can be done with direct-mapped with speculative access
    However, the circuitry can be designed so that the data block from each line in a set can be loaded and then transmitted once the tag check is made
Notes: We can derive some insight into the timing differences between the different cache
access models by developing equations that show the different time delays. The following
parameters are needed:
tct = time needed to compare the tag field of an address with the tag value in a
cache line.
trl = time needed to read a line from the cache to retrieve the data block in the
cache.
txb = time needed to transmit byte or word to the processor; this includes
extracting the desired bytes from the fetched line and gating these bytes onto
the bus to the processor.
thit = time expended at this cache level in the event of a hit.
tmiss = time expended at this cache level in the event of a miss.
First consider direct-mapped cache access. The first operation is checking the
Tag field of an address against the tag value in the line designated by the Line field.
If there is not a match (miss), then the operation is complete. If there is a match
(hit), then the cache hardware reads the data block from the line in the cache and
then fetches the byte or word indicated by the Offset field of the address.
One of the advantages of a direct-mapped cache is that it allows simple and
fast speculation. Once the address has been computed, the one cache line that
might have a copy of that location in memory is known. That cache entry can
be read, and the processor can continue to work with that data before it finishes
checking that the tag actually matches the requested address. Thus checking and
fetching are performed in parallel.
Next, consider a fully associative cache. In this case, the line number is not
known until the tag comparison is completed. So the hit time is the same as for
direct-mapped. Because this is a content-addressable memory, the miss time is simply
the tag comparison time. That is, the tag comparison is made without the need
to read a line of data from the cache, but is made in parallel to all of the lines of the
cache internally to the cache.
With set associative, it is not possible to transmit bytes and compare tags in
parallel as can be done with direct-mapped with speculative access. However, the
circuitry can be designed so that the data block from each line in a set can be loaded
and then transmitted once the tag check is made.

## Slide 41: Table 5.6 Cache Timing Equations
 | Time for hit | Time for miss
Direct-Mapped | thit = trl + txb + tct | tmiss = trl + tct
Direct-Mapped with Speculation | thit = trl + txb | tmiss = trl + tct
Fully Associative | thit = trl + txb + tct | tmiss = tct
Set-Associative | thit = trl + txb + tct | tmiss = trl + tct
Set-Associative with Way Prediction | thit = trl + txb + (1 – Fp) tct | T= = trl + tct
Notes: Table 5.6 summarizes the cache timing equations.

## Slide 42: Table 5.7 Cache Performance Improvement Techniques
Technique | Reduce t1 | Reduce (1 – h1) | Reduce tpenalty
Way Prediction |   |  | 
Cache Capacity | Small | Large | 
Line Size | Small | Large | 
Degree of Associativity | Decrease | Increase | 
More Flexible Replacement Policies |  |  | 
Cache Unity | Split I-cache and D-cache | Unified cache | 
Prefetching |  |  | 
Write Through |  | Write allocate | No write allocate
Critical Word First |  |  | 
Victim Cache |  |  | 
Wider Busses |  |  | 
Notes: Table 5.7 lists widely used cache performance improvement techniques.

## Slide 43: Summary
Cache
Memory
Chapter 5
Cache memory principles
  Intel x86 cache organization
  The IBM z13 cache organization
  Cache performance modules
      Cache timing model
      Design option for improving performance
  Elements of cache design
  Cache addresses
  Cache size
  Logical cache organization
  Replacement algorithms
  Write policy
  Line size
  Number of caches
  Inclusion policy
Notes: Chapter 5 summary.