## Slide 1: Computer Organization and Architecture Designing for Performance
Chapter 8
Input/Output
11th Edition, Global Edition

## Slide 2: Figure 8.1 Generic Model of an I/O Module
Notes: Thus, an I/O module is required. This module has two major functions
(Figure 8.1):
• Interface to the processor and memory via the system bus or central switch
• Interface to one or more peripheral devices by tailored data links
We begin this chapter with a brief discussion of external devices, followed by
an overview of the structure and function of an I/O module. Then we look at the
various ways in which the I/O function can be performed in cooperation with the
processor and memory: the internal I/O interface. Finally, we examine the external
I/O interface, between the I/O module and the outside world.

## Slide 3: External Devices
Provide a means of exchanging data between the external environment and the computer
Attach to the computer by a link to an I/O module
  The link is used to exchange control, status, and data between the I/O module and the external device
Peripheral device
  An external device connected to an I/O module
Three
categories:
Human readable
  Suitable for communicating with the computer user
  Video display terminals (VDTs), printers
Machine readable
  Suitable for communicating with equipment
  Magnetic disk and tape systems, sensors and actuators
Communication
  Suitable for communicating with remote devices such as a terminal, a machine readable device, or another computer
Notes: I/O operations are accomplished through a wide assortment of external devices
that provide a means of exchanging data between the external environment
and the computer. An external device attaches to the computer by a link to
an I/O module (Figure 8.1). The link is used to exchange control, status, and
data between the I/O module and the external device. An external device connected
to an I/O module is often referred to as a peripheral device or, simply, a
peripheral.
We can broadly classify external devices into three categories:
• Human readable: Suitable for communicating with the computer user
• Machine readable: Suitable for communicating with equipment
• Communication: Suitable for communicating with remote devices
Examples of human-readable devices are video display terminals (VDTs) and
printers. Examples of machine-readable devices are magnetic disk and tape systems,
and sensors and actuators, such as are used in a robotics application. Note
that we are viewing disk and tape systems as I/O devices in this chapter, whereas
in Chapter 7 we viewed them as memory devices. From a functional point of view,
these devices are part of the memory hierarchy, and their use is appropriately discussed
in Chapter 7. From a structural point of view, these devices are controlled by
I/O modules and are hence to be considered in this chapter.
Communication devices allow a computer to exchange data with a remote
device, which may be a human-readable device, such as a terminal, a machine readable
device, or even another computer.

## Slide 4: Figure 8.2 Block Diagram of an External Device
Notes: In very general terms, the nature of an external device is indicated in
Figure 8.2. The interface to the I/O module is in the form of control, data, and status
signals. Control signals determine the function that the device will perform, such as
send data to the I/O module (INPUT or READ), accept data from the I/O module
(OUTPUT or WRITE), report status, or perform some control function particular
to the device (e.g., position a disk head). Data are in the form of a set of bits to
be sent to or received from the I/O module. Status signals indicate the state of the
device. Examples are READY/NOT-READY to show whether the device is ready
for data transfer.
Control logic associated with the device controls the device’s operation in
response to direction from the I/O module. The transducer converts data from electrical
to other forms of energy during output and from other forms to electrical
during input. Typically, a buffer is associated with the transducer to temporarily
hold data being transferred between the I/O module and the external environment.
A buffer size of 8 to 16 bits is common for serial devices, whereas block-
oriented devices such as disk drive controllers may have much larger buffers.
The interface between the I/O module and the external device will be examined
in Section 8.7. The interface between the external device and the environment
is beyond the scope of this book, but several brief examples are given here.
A disk drive contains electronics for exchanging data, control, and status signals with
an I/O module plus the electronics for controlling the disk read/write mechanism.
In a fixed-head disk, the transducer is capable of converting between the magnetic
patterns on the moving disk surface and bits in the device’s buffer (Figure 8.2). A
Moving-head disk must also be able to cause the disk arm to move radially in and
out across the disk’s surface.

## Slide 5: Keyboard/Monitor
International Reference Alphabet (IRA)
Basic unit of exchange is the character
  Associated with each character is a code
  Each character in this code is represented by a unique 7-bit binary code
    128 different characters can be represented
Characters are of two types:
  Printable
    Alphabetic, numeric, and special characters that can be printed on paper or displayed on a screen
  Control
    Have to do with controlling the printing or displaying of characters
    Example is carriage return
    Other control characters are concerned with communications procedures
When the user depresses a key it generates an electronic signal that is interpreted by the transducer in the keyboard and translated into the bit pattern of the corresponding IRA code
This bit pattern is transmitted to the I/O module in the computer
On output, IRA code characters are transmitted to an external device from the I/O module
The transducer interprets the code and sends the required electronic signals to the output device either to display the indicated character or perform the requested control function
Keyboard Codes
Most common means of computer/user interaction
User provides input through the keyboard
The monitor displays data provided by the computer
Notes: The most common means of computer/user interaction is a keyboard/monitor
arrangement. The user provides input through the keyboard. This input is then
transmitted to the computer and may also be displayed on the monitor. In addition,
the monitor displays data provided by the computer.
The basic unit of exchange is the character. Associated with each character
is a code, typically 7 or 8 bits in length. The most commonly used text code is the
International Reference Alphabet (IRA). Each character in this code is represented
by a unique 7-bit binary code; thus, 128 different characters can be represented.
Characters are of two types: printable and control. Printable characters are
the alphabetic, numeric, and special characters that can be printed on paper or displayed
on a screen. Some of the control characters have to do with controlling the
printing or displaying of characters; an example is carriage return. Other control
characters are concerned with communications procedures. See Appendix D for
details.
For keyboard input, when the user depresses a key, this generates an
electronic signal that is interpreted by the transducer in the keyboard and
translated into the bit pattern of the corresponding IRA code. This bit pattern
is then transmitted to the I/O module in the computer. At the computer, the
text can be stored in the same IRA code. On output, IRA code characters are
transmitted to an external device from the I/O module. The transducer at the
device interprets this code and sends the required electronic signals to the output
device either to display the indicated character or perform the requested
control function.

## Slide 6: I/O Functions
The major functions for an I/O module fall into the following categories:
Control and timing
Coordinates the flow of traffic between internal resources and external devices
Processor communication
Involves command decoding, data, status reporting, address recognition
Device communication
Involves commands, status information, and data
Data buffering
Performs the needed buffering operation to balance device and memory speeds
Error detection
Detects and reports transmission errors
Notes: The major functions or requirements for an I/O module fall into the following
categories:
• Control and timing
• Processor communication
• Device communication
• Data buffering
• Error detection
During any period of time, the processor may communicate with one or more
external devices in unpredictable patterns, depending on the program’s need for I/O.
The internal resources, such as main memory and the system bus, must be shared
among a number of activities, including data I/O. Thus, the I/O function includes a
control and timing requirement, to coordinate the flow of traffic between internal
resources and external devices. For example, the control of the transfer of data from
an external device to the processor might involve the following sequence of steps:
1. The processor interrogates the I/O module to check the status of the attached
device.
2. The I/O module returns the device status.
3. If the device is operational and ready to transmit, the processor requests the
transfer of data, by means of a command to the I/O module.
4. The I/O module obtains a unit of data (e.g., 8 or 16 bits) from the external device.
5. The data are transferred from the I/O module to the processor.
If the system employs a bus, then each of the interactions between the processor
and the I/O module involves one or more bus arbitrations.
The preceding simplified scenario also illustrates that the I/O module must
communicate with the processor and with the external device. Processor communication
involves the following:
• Command decoding: The I/O module accepts commands from the processor,
typically sent as signals on the control bus. For example, an I/O module for a
disk drive might accept the following commands: READ SECTOR, WRITE
SECTOR, SEEK track number, and SCAN record ID. The latter two commands
each include a parameter that is sent on the data bus.
• Data: Data are exchanged between the processor and the I/O module over the
data bus.
• Status reporting: Because peripherals are so slow, it is important to know the
status of the I/O module. For example, if an I/O module is asked to send data
to the processor (read), it may not be ready to do so because it is still working
on the previous I/O command. This fact can be reported with a status signal.
Common status signals are BUSY and READY. There may also be signals to
report various error conditions.
• Address recognition: Just as each word of memory has an address, so does
each I/O device. Thus, an I/O module must recognize one unique address for
each peripheral it controls.
On the other side, the I/O module must be able to perform device communication.
This communication involves commands, status information, and data
(Figure 8.2).
An essential task of an I/O module is data buffering. The need for this function
is apparent from Figure 2.1. Whereas the transfer rate into and out of main
memory or the processor is quite high, the rate is orders of magnitude lower for
many peripheral devices and covers a wide range. Data coming from main memory
are sent to an I/O module in a rapid burst. The data are buffered in the I/O module
and then sent to the peripheral device at its data rate. In the opposite direction, data
are buffered so as not to tie up the memory in a slow transfer operation. Thus, the
I/O module must be able to operate at both device and memory speeds. Similarly, if
the I/O device operates at a rate higher than the memory access rate, then the I/O
module performs the needed buffering operation.
Finally, an I/O module is often responsible for error detection and for subsequently
reporting errors to the processor. One class of errors includes mechanical
and electrical malfunctions reported by the device (e.g., paper jam, bad disk track).
Another class consists of unintentional changes to the bit pattern as it is transmitted
from device to I/O module. Some form of error-detecting code is often used
to detect transmission errors. A simple example is the use of a parity bit on each
character of data. For example, the IRA character code occupies 7 bits of a byte.
The eighth bit is set so that the total number of 1s in the byte is even (even parity)
or odd (odd parity). When a byte is received, the I/O module checks the parity to
determine whether an error has occurred.

## Slide 7: Figure 8.3 Block Diagram of an I/O Module
Notes: I/O modules vary considerably in complexity and the number of external devices
that they control. We will attempt only a very general description here. (One specific
device, the Intel 8255A, is described in Section 8.4.) Figure 8.3 provides a general
block diagram of an I/O module. The module connects to the rest of the computer
through a set of signal lines (e.g., system bus lines). Data transferred to and from the
module are buffered in one or more data registers. There may also be one or more
status registers that provide current status information. A status register may also
function as a control register, to accept detailed control information from the processor.
The logic within the module interacts with the processor via a set of control
lines. The processor uses the control lines to issue commands to the I/O module.
Some of the control lines may be used by the I/O module (e.g., for arbitration and
status signals). The module must also be able to recognize and generate addresses
associated with the devices it controls. Each I/O module has a unique address or, if
it controls more than one external device, a unique set of addresses. Finally, the I/O
module contains logic specific to the interface with each device that it controls.
An I/O module functions to allow the processor to view a wide range of devices
in a simple-minded way. There is a spectrum of capabilities that may be provided.
The I/O module may hide the details of timing, formats, and the electromechanics
of an external device so that the processor can function in terms of simple read and
write commands, and possibly open and close file commands. In its simplest form,
the I/O module may still leave much of the work of controlling a device (e.g., rewind
a tape) visible to the processor.
An I/O module that takes on most of the detailed processing burden, presenting
a high-level interface to the processor, is usually referred to as an I/O channel or
I/O processor. An I/O module that is quite primitive and requires detailed control
is usually referred to as an I/O controller or device controller. I/O controllers are
commonly seen on microcomputers, whereas I/O channels are used on mainframes.
In what follows, we will use the generic term I/O module when no confusion
results and will use more specific terms where necessary.

## Slide 8: Programmed I/O
Three techniques are possible for I/O operations:
Programmed I/O
  Data are exchanged between the processor and the I/O module
  Processor executes a program that gives it direct control of the I/O operation
  When the processor issues a command it must wait until the I/O operation is complete
  If the processor is faster than the I/O module this is wasteful of processor time
  Interrupt-driven I/O
  Processor issues an I/O command, continues to execute other instructions, and is interrupted by the I/O module when the latter has completed its work
  Direct memory access (DMA)
  The I/O module and main memory exchange data directly without processor involvement
Notes: Three techniques are possible for I/O operations. With programmed I/O, data are
exchanged between the processor and the I/O module. The processor executes a program
that gives it direct control of the I/O operation, including sensing device status,
sending a read or write command, and transferring the data. When the processor
issues a command to the I/O module, it must wait until the I/O operation is complete.
If the processor is faster than the I/O module, this is wasteful of processor time.
With interrupt-driven I/O, the processor issues an I/O command, continues to execute
other instructions, and is interrupted by the I/O module when the latter has completed
its work. With both programmed and interrupt I/O, the processor is responsible for
extracting data from main memory for output and storing data in main memory for
input. The alternative is known as direct memory access (DMA). In this mode, the I/O
module and main memory exchange data directly, without processor involvement.

## Slide 9: Table 8.1 I/O Techniques
 | No Interrupts | Use of Interrupts
I/O-to-memory transfer through processor | Programmed I/O | Interrupt-driven I/O
Direct I/O-to-memory transfer |  | Direct memory access (DMA)
Notes: Table 8.1 indicates the relationship among these three techniques. In this section,
we explore programmed I/O. Interrupt I/O and DMA are explored in the following
two sections, respectively.

## Slide 10: I/O Commands
There are four types of I/O commands that an I/O module may receive when it is addressed by a processor:
Control
  used to activate a peripheral and tell it what to do
Test
  used to test various status conditions associated with an I/O module and its peripherals
Read
  causes the I/O module to obtain an item of data from the peripheral and place it in an internal buffer
Write
  causes the I/O module to take an item of data from the data bus and subsequently transmit that data item to the peripheral
Notes: To execute an I/O-related instruction, the processor issues an address, specifying the
particular I/O module and external device, and an I/O command. There are four types
of I/O commands that an I/O module may receive when it is addressed by a processor:
• Control: Used to activate a peripheral and tell it what to do. For example, a
magnetic-tape unit may be instructed to rewind or to move forward one record.
These commands are tailored to the particular type of peripheral device.
• Test: Used to test various status conditions associated with an I/O module and
its peripherals. The processor will want to know that the peripheral of interest
is powered on and available for use. It will also want to know if the most
recent I/O operation is completed and if any errors occurred.
• Read: Causes the I/O module to obtain an item of data from the peripheral
and place it in an internal buffer (depicted as a data register in Figure 8.3). The
processor can then obtain the data item by requesting that the I/O module
place it on the data bus.
• Write: Causes the I/O module to take an item of data (byte or word) from the
data bus and subsequently transmit that data item to the peripheral.

## Slide 11: Figure 8.4 Three Techniques for Input of a Block of Data
Notes: Figure 8.4a gives an example of the use of programmed I/O to read in a block of
data from a peripheral device (e.g., a record from tape) into memory. Data are read
in one word (e.g., 16 bits) at a time. For each word that is read in, the processor must
remain in a status-checking cycle until it determines that the word is available in the
I/O module’s data register. This flowchart highlights the main disadvantage of this
technique: it is a time-consuming process that keeps the processor busy needlessly.

## Slide 12: I/O Instructions
With programmed I/O there is a close correspondence between the I/O-related instructions that the processor fetches from memory and the I/O commands that the processor issues to an I/O module to execute the instructions
The form of the instruction depends on the way in which external devices are addressed
Each I/O device connected through I/O modules is given a unique identifier or address
When the processor issues an I/O command, the command contains the address of the desired device
Thus each I/O module must interpret the address lines to determine if the command is for itself
Memory-mapped I/O
There is a single address space for memory locations and I/O devices
A single read line and a single write line are needed on the bus
Notes: With programmed I/O, there is a close correspondence between the I/O-related
instructions that the processor fetches from memory and the I/O commands that the
processor issues to an I/O module to execute the instructions. That is, the instructions
are easily mapped into I/O commands, and there is often a simple one-
to-one relationship. The form of the instruction depends on the way in which external
devices are addressed.
Typically, there will be many I/O devices connected through I/O modules to
the system. Each device is given a unique identifier or address. When the processor
issues an I/O command, the command contains the address of the desired device.
Thus, each I/O module must interpret the address lines to determine if the command
is for itself.
When the processor, main memory, and I/O share a common bus, two modes
of addressing are possible: memory mapped and isolated. With memory-mapped
I/O, there is a single address space for memory locations and I/O devices. The processor
treats the status and data registers of I/O modules as memory locations and
uses the same machine instructions to access both memory and I/O devices. So, for
example, with 10 address lines, a combined total of 210 = 1024 memory locations
and I/O addresses can be supported, in any combination.
With memory-mapped I/O, a single read line and a single write line are needed
on the bus. Alternatively, the bus may be equipped with memory read and write
plus input and output command lines. Now, the command line specifies whether the
address refers to a memory location or an I/O device. The full range of addresses
may be available for both. Again, with 10 address lines, the system may now support
both 1024 memory locations and 1024 I/O addresses. Because the address space for
I/O is isolated from that for memory, this is referred to as isolated I/O.

## Slide 13: I/O Mapping Summary
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
    Limited set
Notes: I/O mapping summary.

## Slide 14: Figure 8.5 Memory-Mapped and Isolated I/O
Notes: Figure 8.5 contrasts these two programmed I/O techniques. Figure 8.5a shows
how the interface for a simple input device such as a terminal keyboard might appear
to a programmer using memory-mapped I/O. Assume a 10-bit address, with a 512-
bit memory (locations 0–511) and up to 512 I/O addresses (locations 512–1023).
Two addresses are dedicated to keyboard input from a particular terminal. Address
516 refers to the data register and address 517 refers to the status register, which
also functions as a control register for receiving processor commands. The program
shown will read 1 byte of data from the keyboard into an accumulator register in the
processor. Note that the processor loops until the data byte is available.
With isolated I/O (Figure 8.5b), the I/O ports are accessible only by special
I/O commands, which activate the I/O command lines on the bus.
For most types of processors, there is a relatively large set of different instructions
for referencing memory. If isolated I/O is used, there are only a few I/O
instructions. Thus, an advantage of memory-mapped I/O is that this large repertoire
of instructions can be used, allowing more efficient programming. A disadvantage is
that valuable memory address space is used up. Both memory-mapped and isolated
I/O are in common use.

## Slide 15: Interrupt-Driven I/O
The problem with programmed I/O is that the processor has to wait a long time for the I/O module to be ready for either reception or transmission of data
An alternative is for the processor to issue an I/O command to a module and then go on to do some other useful work
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor
The processor executes the data transfer and resumes its former processing
Notes: The problem with programmed I/O is that the processor has to wait a long time
for the I/O module of concern to be ready for either reception or transmission of
data. The processor, while waiting, must repeatedly interrogate the status of the I/O
module. As a result, the level of the performance of the entire system is severely
degraded.
An alternative is for the processor to issue an I/O command to a module and
then go on to do some other useful work. The I/O module will then interrupt the
processor to request service when it is ready to exchange data with the processor.
The processor then executes the data transfer, as before, and then resumes its
former processing.
Let us consider how this works, first from the point of view of the I/O module.
For input, the I/O module receives a READ command from the processor. The I/O
module then proceeds to read data in from an associated peripheral. Once the data
are in the module’s data register, the module signals an interrupt to the processor
over a control line. The module then waits until its data are requested by the processor.
When the request is made, the module places its data on the data bus and is
then ready for another I/O operation.
From the processor’s point of view, the action for input is as follows. The processor
issues a READ command. It then goes off and does something else (e.g., the
processor may be working on several different programs at the same time). At the
end of each instruction cycle, the processor checks for interrupts (Figure 3.9). When
the interrupt from the I/O module occurs, the processor saves the context (e.g., program
counter and processor registers) of the current program and processes the
interrupt. In this case, the processor reads the word of data from the I/O module
and stores it in memory. It then restores the context of the program it was working
on (or some other program) and resumes execution.
Figure 8.4b shows the use of interrupt I/O for reading in a block of data.
Compare this with Figure 8.4a. Interrupt I/O is more efficient than programmed I/O
because it eliminates needless waiting. However, interrupt I/O still consumes a lot of
processor time, because every word of data that goes from memory to I/O module
or from I/O module to memory must pass through the processor.

## Slide 16: Figure 8.6 Simple Interrupt Processing
Notes: Let us consider the role of the processor in interrupt-driven I/O in more detail.
The occurrence of an interrupt triggers a number of events, both in the processor
hardware and in software. Figure 8.6 shows a typical sequence. When an I/O device
completes an I/O operation, the following sequence of hardware events occurs:
1. The device issues an interrupt signal to the processor.
2. The processor finishes execution of the current instruction before responding
to the interrupt, as indicated in Figure 3.9.
3. The processor tests for an interrupt, determines that there is one, and sends an
acknowledgment signal to the device that issued the interrupt. The acknowledgment
allows the device to remove its interrupt signal.
4. The processor now needs to prepare to transfer control to the interrupt routine.
To begin, it needs to save information needed to resume the current program at
the point of interrupt. The minimum information required is (a) the status of the
processor, which is contained in a register called the program status word (PSW),
and (b) the location of the next instruction to be executed, which is contained in
the program counter. These can be pushed onto the system control stack.
5. The processor now loads the program counter with the entry location of the
interrupt-handling program that will respond to this interrupt. Depending on
the computer architecture and operating system design, there may be a single
program; one program for each type of interrupt; or one program for each
device and each type of interrupt. If there is more than one interrupt-handling
routine, the processor must determine which one to invoke. This information
may have been included in the original interrupt signal, or the processor may
have to issue a request to the device that issued the interrupt to get a response
that contains the needed information.

## Slide 17: Figure 8.7 Changes in Memory and Registers for an Interrupt
Notes: Once the program counter has been loaded, the processor proceeds to the
next instruction cycle, which begins with an instruction fetch. Because the instruction
fetch is determined by the contents of the program counter, the result is that
control is transferred to the interrupt-handler program. The execution of this program
results in the following operations:
6. At this point, the program counter and PSW relating to the interrupted
program have been saved on the system stack. However, there is other information
that is considered part of the “state” of the executing program. In particular,
the contents of the processor registers need to be saved, because these
registers may be used by the interrupt handler. So, all of these values, plus any
other state information, need to be saved. Typically, the interrupt handler will
begin by saving the contents of all registers on the stack. Figure 8.7a shows a
simple example. In this case, a user program is interrupted after the instruction
at location N. The contents of all of the registers plus the address of the next
instruction (N + 1) are pushed onto the stack. The stack pointer is updated to
point to the new top of stack, and the program counter is updated to point to
the beginning of the interrupt service routine.
7. The interrupt handler next processes the interrupt. This includes an examination
of status information relating to the I/O operation or other event that
caused an interrupt. It may also involve sending additional commands or
acknowledgments to the I/O device.
8. When interrupt processing is complete, the saved register values are retrieved
from the stack and restored to the registers (e.g., see Figure 8.7b).
9. The final act is to restore the PSW and program counter values from the stack.
As a result, the next instruction to be executed will be from the previously
interrupted program.
Note that it is important to save all the state information about the interrupted
program for later resumption. This is because the interrupt is not a routine called
from the program. Rather, the interrupt can occur at any time and therefore at any
point in the execution of a user program. Its occurrence is unpredictable. Indeed, as
we will see in the next chapter, the two programs may not have anything in common
and may belong to two different users.

## Slide 18: Design Issues
Two design issues arise in implementing interrupt I/O:
Because there will be multiple I/O modules how does the processor determine which device issued the interrupt?
If multiple interrupts have occurred how does the processor decide which one to process?
Notes: Two design issues arise in implementing interrupt I/O. First, because there will
almost invariably be multiple I/O modules, how does the processor determine which
device issued the interrupt? And second, if multiple interrupts have occurred, how
does the processor decide which one to process?

## Slide 19: Device Identification
Four general categories of techniques are in common use:
  Multiple interrupt lines
  Between the processor and the I/O modules
  Most straightforward approach to the problem
  Consequently even if multiple lines are used, it is likely that each line will have multiple I/O modules attached to it
  Software poll
  When the processor detects an interrupt it branches to an interrupt-service routine whose job is to poll each I/O module to determine which module caused the interrupt
  Time consuming
  Daisy chain (hardware poll, vectored)
  The interrupt acknowledge line is daisy chained through the modules
  Vector – address of the I/O module or some other unique identifier
  Vectored interrupt – processor uses the vector as a pointer to the appropriate device-service routine, avoiding the need to execute a general interrupt-service routine first
  Bus arbitration (vectored)
  An I/O module must first gain control of the bus before it can raise the interrupt request line
  When the processor detects the interrupt it responds on the interrupt acknowledge line
  Then the requesting module places its vector on the data lines
Notes: Let us consider device identification first. Four general categories of techniques
are in common use:
• Multiple interrupt lines
• Software poll
• Daisy chain (hardware poll, vectored)
• Bus arbitration (vectored)
The most straightforward approach to the problem is to provide multiple interrupt
lines between the processor and the I/O modules. However, it is impractical to
dedicate more than a few bus lines or processor pins to interrupt lines. Consequently,
even if multiple lines are used, it is likely that each line will have multiple I/O modules
attached to it. Thus, one of the other three techniques must be used on each line.
One alternative is the software poll. When the processor detects an interrupt,
it branches to an interrupt-service routine whose job it is to poll each I/O module
to determine which module caused the interrupt. The poll could be in the form of a
separate command line (e.g., TESTI/O). In this case, the processor raises TESTI/O
and places the address of a particular I/O module on the address lines. The I/O module
responds positively if it sets the interrupt. Alternatively, each I/O module could
contain an addressable status register. The processor then reads the status register
of each I/O module to identify the interrupting module. Once the correct module is
identified, the processor branches to a device-service routine specific to that device.
The disadvantage of the software poll is that it is time consuming. A more efficient
technique is to use a daisy chain, which provides, in effect, a hardware poll. An example
of a daisy-chain configuration is shown in Figure 3.26. For interrupts, all I/O modules
share a common interrupt request line. The interrupt acknowledge line is daisy chained
through the modules. When the processor senses an interrupt, it sends out an interrupt
acknowledge. This signal propagates through a series of I/O modules until it gets to a
requesting module. The requesting module typically responds by placing a word on
the data lines. This word is referred to as a vector and is either the address of the I/O
module or some other unique identifier. In either case, the processor uses the vector as
a pointer to the appropriate device-service routine. This avoids the need to execute a
general interrupt-service routine first. This technique is called a vectored interrupt.
There is another technique that makes use of vectored interrupts, and that is
bus arbitration. With bus arbitration, an I/O module must first gain control of the
bus before it can raise the interrupt request line. Thus, only one module can raise the
line at a time. When the processor detects the interrupt, it responds on the interrupt
acknowledge line. The requesting module then places its vector on the data lines.

## Slide 20: Figure 8.8 Use of the 82C59A Interrupt Controller
Notes: The Intel 80386 provides a single Interrupt Request (INTR) and a single Interrupt
Acknowledge (INTA) line. To allow the 80386 to handle a variety of devices and priority
structures, it is usually configured with an external interrupt arbiter, the 82C59A.
External devices are connected to the 82C59A, which in turn connects to the 80386.
Figure 8.8 shows the use of the 82C59A to connect multiple I/O modules for the
80386. A single 82C59A can handle up to eight modules. If control for more than eight
modules is required, a cascade arrangement can be used to handle up to 64 modules.
The 82C59A’s sole responsibility is the management of interrupts. It accepts
interrupt requests from attached modules, determines which interrupt has the highest
priority, and then signals the processor by raising the INTR line. The processor
acknowledges via the INTA line. This prompts the 82C59A to place the appropriate
vector information on the data bus. The processor can then proceed to process the
interrupt and to communicate directly with the I/O module to read or write data.
The 82C59A is programmable. The 80386 determines the priority scheme to
be used by setting a control word in the 82C59A. The following interrupt modes are
possible:
• Fully nested: The interrupt requests are ordered in priority from 0 (IR0)
through 7 (IR7).
Rotating: In some applications a number of interrupting devices are of equal
priority. In this mode a device, after being serviced, receives the lowest priority
in the group.
• Special mask: This allows the processor to inhibit interrupts from certain devices.

## Slide 21: Figure 8.9 The Intel 8255A Programmable Peripheral Interface
Notes: As an example of an I/O module used for programmed I/O and interrupt-
driven I/O, we consider the Intel 8255A Programmable Peripheral Interface. The 8255A is
a single-chip, general-purpose I/O module originally designed for use with the Intel
80386 processor. It has since been cloned by other manufacturers and is a widely
used peripheral controller chip. Its uses include as a controller for simple I/O devices
for microprocessors and in embedded systems, including microcontroller systems.
Figure 8.9 shows a general block diagram plus the pin assignment for the
40-pin package in which it is housed.
The right side of the block diagram of Figure 8.9a is the external interface
of the 8255A. The 24 I/O lines are divided into three 8-bit groups (A, B, C). Each
group can function as an 8-bit I/O port, thus providing connection for three peripheral
devices. In addition, group C is subdivided into 4-bit groups (CA and CB ), which
may be used in conjunction with the A and B I/O ports. Configured in this manner,
group C lines carry control and status signals.
The left side of the block diagram is the internal interface to the microprocessor
system bus. It includes an 8-bit bidirectional data bus (D0 through D7), used to
transfer data between the microprocessor and the I/O ports and to transfer control
information.
The processor controls the 8255A by means of an 8-bit control register in the
processor. The processor can set the value of the control register to specify a variety
of operating modes and configurations. From the processor point of view, there is
a control port, and the control register bits are set in the processor and then sent to
the control port over lines D0—D7.

## Slide 22: Figure 8.10 The Intel 8255A Control Word
Notes: Thus, when the processor sets both A1 and A2 to 1, the 8255A interprets the
8-bit value on the data bus as a control word. When the processor transfers an 8-bit
control word with line D7 set to 1 (Figure 8.10a), the control word is used to configure
the operating mode of the 24 I/O lines. The three modes are:
■ Mode 0: This is the basic I/O mode. The three groups of eight external lines
function as three 8-bit I/O ports. Each port can be designated as input or output.
Data may only be sent to a port if the port is defined as output, and data
may only be read from a port if the port is set to input.
■ Mode 1: In this mode, ports A and B can be configured as either input or
output, and lines from port C serve as control lines for A and B. The control
signals serve two principal purposes: “handshaking” and interrupt request.
Handshaking is a simple timing mechanism. One control line is used by the
sender as a DATA READY line, to indicate when the data are present on the
I/O data lines. Another line is used by the receiver as an ACKNOWLEDGE,
indicating that the data have been read and the data lines may be cleared.
Another line may be designated as an INTERRUPT REQUEST line and tied
back to the system bus.
■ Mode 2: This is a bidirectional mode. In this mode, port A can be configured
as either the input or output lines for bidirectional traffic on port B, with the
port B lines providing the opposite direction. Again, port C lines are used for
control signaling.
When the processor sets D7 to 0 (Figure 8.10b), the control word is used to
program the bit values of port C individually. This feature is rarely used.

## Slide 23: Figure 8.11 Keyboard/Display Interface to 8255A
Notes: Because the 8255A is programmable via the
control register, it can be used to control a variety of simple peripheral devices.
Figure 8.11 illustrates its use to control a keyboard/display terminal. The keyboard
provides 8 bits of input. Two of these bits, SHIFT and CONTROL, have special
meaning to the keyboard-handling
program executing in the processor. However,
this interpretation is transparent to the 8255A, which simply accepts the 8 bits of
data and presents them on the system data bus. Two handshaking control lines are
provided for use with the keyboard.
The display is also linked by an 8-bit data port. Again, two of the bits have
special meanings that are transparent to the 8255A. In addition to two handshaking
lines, two lines provide additional control functions.

## Slide 24: Drawbacks of Programmed and Interrupt-Driven I/O
Both forms of I/O suffer from two inherent drawbacks:
  The I/O transfer rate is limited by the speed with which the processor can test and service a device
  The processor is tied up in managing an I/O transfer; a number of instructions must be executed for each I/O transfer
When large volumes of data are to be moved a more efficient technique is direct memory access (DMA)
Notes: Interrupt-driven I/O, though more efficient than simple programmed I/O, still
requires the active intervention of the processor to transfer data between memory
and an I/O module, and any data transfer must traverse a path through the processor.
Thus, both these forms of I/O suffer from two inherent drawbacks:
1. The I/O transfer rate is limited by the speed with which the processor can test
and service a device.
2. The processor is tied up in managing an I/O transfer; a number of instructions
must be executed for each I/O transfer (e.g., Figure 8.5).
There is somewhat of a trade-off between these two drawbacks. Consider the
transfer of a block of data. Using simple programmed I/O, the processor is dedicated
to the task of I/O and can move data at a rather high rate, at the cost of doing
nothing else. Interrupt I/O frees up the processor to some extent at the expense of
the I/O transfer rate. Nevertheless, both methods have an adverse impact on both
processor activity and I/O transfer rate.
When large volumes of data are to be moved, a more efficient technique is
required: direct memory access (DMA).

## Slide 25: Figure 8.12 Typical DMA Block Diagram
Notes: DMA involves an additional module on the system bus. The DMA module
(Figure 8.12) is capable of mimicking the processor and, indeed, of taking over
control of the system from the processor. It needs to do this to transfer data to
and from memory over the system bus. For this purpose, the DMA module must
use the bus only when the processor does not need it, or it must force the processor
to suspend operation temporarily. The latter technique is more common and is
referred to as cycle stealing, because the DMA module in effect steals a bus cycle.
When the processor wishes to read or write a block of data, it issues a
command to the DMA module, by sending to the DMA module the following
information:
• Whether a read or write is requested, using the read or write control line
between the processor and the DMA module
• The address of the I/O device involved, communicated on the data lines
The starting location in memory to read from or write to, communicated on
the data lines and stored by the DMA module in its address register
• The number of words to be read or written, again communicated via the data
lines and stored in the data count register
The processor then continues with other work. It has delegated this I/O operation
to the DMA module. The DMA module transfers the entire block of data, one
word at a time, directly to or from memory, without going through the processor.
When the transfer is complete, the DMA module sends an interrupt signal to the
processor. Thus, the processor is involved only at the beginning and end of the
transfer (Figure 8.4c).

## Slide 26: Figure 8.13 DMA and Interrupt Breakpoints during an Instruction Cycle
Notes: Figure 8.13 shows where in the instruction cycle the processor may be suspended.
In each case, the processor is suspended just before it needs to use the bus.
The DMA module then transfers one word and returns control to the processor.
Note that this is not an interrupt; the processor does not save a context and do
something else. Rather, the processor pauses for one bus cycle. The overall effect
is to cause the processor to execute more slowly. Nevertheless, for a multiple-word
I/O transfer, DMA is far more efficient than interrupt-driven or programmed I/O.

## Slide 27: Figure 8.14 Alternative DMA Configurations
Notes: The DMA mechanism can be configured in a variety of ways. Some possibilities
are shown in Figure 8.14. In the first example, all modules share the same system
bus. The DMA module, acting as a surrogate processor, uses programmed I/O to
exchange data between memory and an I/O module through the DMA module. This
configuration, while it may be inexpensive, is clearly inefficient. As with processor controlled
programmed I/O, each transfer of a word consumes two bus cycles.
The number of required bus cycles can be cut substantially by integrating the
DMA and I/O functions. As Figure 8.14b indicates, this means that there is a path
between the DMA module and one or more I/O modules that does not include the
system bus. The DMA logic may actually be a part of an I/O module, or it may be a
separate module that controls one or more I/O modules. This concept can be taken
one step further by connecting I/O modules to the DMA module using an I/O bus
(Figure 8.14c). This reduces the number of I/O interfaces in the DMA module to one
and provides for an easily expandable configuration. In both of these cases (Figures
8.14b and c), the system bus that the DMA module shares with the processor and
memory is used by the DMA module only to exchange data with memory. The
exchange of data between the DMA and I/O modules takes place off the system
bus.

## Slide 28: Figure 8.15 8237 DMA Usage of System Bus
Notes: The Intel 8237A DMA controller interfaces to the 80 x 86 family of processors and
to DRAM memory to provide a DMA capability. Figure 8.15 indicates the location
of the DMA module. When the DMA module needs to use the system buses (data,
address, and control) to transfer data, it sends a signal called HOLD to the processor.
The processor responds with the HLDA (hold acknowledge) signal, indicating
that the DMA module can use the buses. For example, if the DMA module is to
transfer a block of data from memory to disk, it will do the following:
1. The peripheral device (such as the disk controller) will request the service of
DMA by pulling DREQ (DMA request) high.
2. The DMA will put a high on its HRQ (hold request), signaling the CPU
through its HOLD pin that it needs to use the buses.
3.The CPU will finish the present bus cycle (not necessarily the present instruction)
and respond to the DMA request by putting high on its HDLA (hold
acknowledge), thus telling the 8237 DMA that it can go ahead and use the
buses to perform its task. HOLD must remain active high as long as DMA is
performing its task.
4. DMA will activate DACK (DMA acknowledge), which tells the peripheral
device that it will start to transfer the data.
5. DMA starts to transfer the data from memory to peripheral by putting the
address of the first byte of the block on the address bus and activating MEMR,
thereby reading the byte from memory into the data bus; it then activates IOW
to write it to the peripheral. Then DMA decrements the counter and increments
the address pointer and repeats this process until the count reaches zero
and the task is finished.
6. After the DMA has finished its job it will deactivate HRQ, signaling the CPU
that it can regain control over its buses.

## Slide 29: Fly-By DMA Controller
Data does not pass through and is not stored in DMA chip
DMA can only transfer data between an I/O port and a memory address
Not between two I/O ports or two memory locations
Can do memory to memory via register
8237 contains four DMA channels
Can be programmed independently
Any one of the channels may be active at any moment
These channels are numbered 0, 1, 2, and 3
Notes: While the DMA is using the buses to transfer data, the processor is idle.
Similarly, when the processor is using the bus, the DMA is idle. The 8237 DMA
is known as a fly-by DMA controller. This means that the data being moved from
one location to another does not pass through the DMA chip and is not stored in
the DMA chip. Therefore, the DMA can only transfer data between an I/O port
and a memory address, but not between two I/O ports or two memory locations.
However, as explained subsequently, the DMA chip can perform a memory-to-memory
transfer via a register.
The 8237 contains four DMA channels that can be programmed independently,
and any one of the channels may be active at any moment. These channels are
numbered 0, 1, 2, and 3.

## Slide 30: Table 8.2 Intel 8237A Registers
Bit | Command | Status | Mode | Single Mask | All Mask
D0 | Memory- to- memory E/D | Channel 0 has reached TC | Channel select | Select channel mask bit | Clear/set chan- nel 0 mask bit
D1 | Channel 0 address hold E/D | Channel 1 has reached TC |  |  | Clear/set chan- nel 1 mask bit
D2 | Controller E/D | Channel 2 has reached TC | Verify/write/read transfer | Clear/set mask bit | Clear/set chan- nel 2 mask bit
D3 | Normal/com- pressed timing | Channel 3 has reached TC |  |  | Clear/set chan-nel 3 mask bit
D4 | Fixed/rotating priority | Channel 0 request | Auto- initialization E/D |  | 
D5 | Late/extended write selection | Channel 0 request | Address increment/ decrement select |  | 
D6 | DREQ sense active high/low | Channel 0 request |  |  | 
D7 | DACK sense active high/low | Channel 0 request | Demand/single/ block/cascade mode select |  | 
E/D = enable/disable
TC = terminal count
Notes: The 8237 has a set of five control/command registers to program and control
DMA operation over one of its channels (Table 8.2):
• Command: The processor loads this register to control the operation of the
DMA. D0 enables a memory-to-memory transfer, in which channel 0 is used
to transfer a byte into an 8237 temporary register and channel 1 is used to
transfer the byte from the register to memory. When memory-to-memory is
enabled, D1 can be used to disable increment/decrement on channel 0 so that
a fixed value can be written into a block of memory. D2 enables or disables
DMA.
• Status: The processor reads this register to determine DMA status. Bits
D0–D3 are used to indicate if channels 0–3 have reached their TC (terminal
count). Bits D4–D7 are used by the processor to determine if any channel has
a DMA request pending.
• Mode: The processor sets this register to determine the mode of operation
of the DMA. Bits D0 and D1 are used to select a channel. The other bits
select various operation modes for the selected channel. Bits D2 and D3
determine if the transfer is from an I/O device to memory (write) or from
memory to I/O (read), or a verify operation. If D4 is set, then the memory
address register and the count register are reloaded with their original
values at the end of a DMA data transfer. Bits D6 and D7 determine the
way in which the 8237 is used. In single mode, a single byte of data is transferred.
Block and demand modes are used for a block transfer, with the
demand mode allowing for premature ending of the transfer. Cascade
mode allows multiple 8237s to be cascaded to expand the number of channels
to more than 4.
• Single Mask: The processor sets this register. Bits D0 and D1 select the channel.
Bit D2 clears or sets the mask bit for that channel. It is through this register
that the DREQ input of a specific channel can be masked (disabled) or
unmasked (enabled). While the command register can be used to disable the
whole DMA chip, the single mask register allows the programmer to disable
or enable a specific channel.
• All Mask: This register is similar to the single mask register except that all four
channels can be masked or unmasked with one write operation.
In addition, the 8237A has eight data registers: one memory address register
and one count register for each channel. The processor sets these registers to indicate
the location of size of main memory to be affected by the transfers.

## Slide 31: Direct Cache Access (DCA)
DMA is not able to scale to meet the increased demand due to dramatic increases in data rates for network I/O
Demand is coming primarily from the widespread deployment of 10-Gbps and 100-Gbps Ethernet switches to handle massive amounts of data transfer to and from database servers and other high-performance systems
Another source of traffic comes from Wi-Fi in the gigabit range
Network Wi-Fi devices that handle 3.2 Gbps and 6.76 Gbps are becoming widely available and producing demand on enterprise systems
Notes: DMA has proved an effective means of enhancing performance of I/O with peripheral
devices and network I/O traffic. However, for the dramatic increases in data
rates for network I/O, DMA is not able to scale to meet the increased demand.
This demand is coming primarily from the widespread deployment of 10-Gbps and
100-Gbps Ethernet switches to handle massive amounts of data transfer to and from
database servers and other high-performance systems [STAL16]. A secondary but
increasingly important source of traffic comes from Wi-Fi in the gigabit range. Network Wi-Fi
devices that handle 3.2 Gbps and 6.76 Gbps are becoming widely
available and producing demand on enterprise systems [STAL16].
In this section, we will show how enabling the I/O function to have direct
access to the cache can enhance performance, a technique known as direct cache
access (DCA). Throughout this section, we are concerned only with the cache that
is closest to main memory, referred to as the last-level cache. In some systems,
this will be an L2 cache, in others an L3 cache.
To begin, we describe the way in which contemporary multicore systems use
on-chip shared cache to enhance DMA performance. This approach involves enabling
the DMA function to have direct access to the last-level
cache. Next we examine cache-related
performance issues that manifest when high-speed network traffic
is processed. From there, we look at several different strategies for DCA that are
designed to enhance network protocol processing performance. Finally, this section
describes a DCA approach implemented by Intel, referred to as Direct Data I/O.

## Slide 32: Figure 8.16 Xeon E5-2600/4600 Chip Architecture
Notes: Intel Xeon is Intel’s high-end, high-performance
processor family, used in servers, high-performance workstations, and
supercomputers. Many of the members of the Xeon family use a ring interconnect
system, as illustrated for the Xeon E5-2600/4600 in Figure 8.16.
The E5-2600/4600 can be configured with up to eight cores on a single chip.
Each core has dedicated L1 and L2 caches. There is a shared L3 cache of up to
20 MB. The L3 cache is divided into slices, one associated with each core although
each core can address the entire cache. Further, each slice has its own cache pipeline,
so that requests can be sent in parallel to the slices.
The bidirectional high-speed ring interconnect links cores, last-level
cache, PCIe, and integrated memory controller (IMC).
In essence, the ring operates as follows:
1. Each component that attaches to the bidirectional ring (QPI, PCIe, L3 cache,
L2 cache) is considered a ring agent, and implements ring agent logic.
2. The ring agents cooperate via a distributed protocol to request and allocate
access to the ring, in the form of time slots.
3. When an agent has data to send, it chooses the ring direction that results in the
shortest path to the destination and transmits when a scheduling slot is available.
The ring architecture provides good performance and scales well for multiple
cores, up to a point. For systems with a greater number of cores, multiple rings are
used, with each ring supporting some of the cores.
In traditional DMA operation, data is exchanged
between main memory and an I/O device by means of the system interconnection
structure, such as a bus, ring, or QPI point-to-point matrix. So, for example, if the
Xeon E5-2600/4600 used a traditional DMA technique, output would proceed as
follows. An I/O driver running on a core would send an I/O command to the I/O
controller (labeled PCIe in Figure 8.16) with the location and size of the buffer in
main memory containing the data to be transferred. The I/O controller issues a read
request that is routed to the memory controller hub (MCH), which accesses the data
on DDR3 memory and puts it on the system ring for delivery to the I/O controller.
The L3 cache is not involved in this transaction and one or more off-chip memory
reads are required. Similarly, for input, data arrives from the I/O controller and is
delivered over the system ring to the MCH and written out to main memory. The
MCH must also invalidate any L3 cache lines corresponding to the updated memory
locations. In this case, one or more off-chip memory writes are required. Further, if
an application wants to access the new data, a main memory read is required.
With the availability of large amounts of last-level cache, a more efficient
technique is possible, and is used by the Xeon E5-2600/4600. For output, when the
I/O controller issues a read request, the MCH first checks to see if the data is in the
L3 cache. This is likely to be the case, if an application has recently written data
into the memory block to be output. In that case, the MCH directs data from the L3
cache to the I/O controller; no main memory accesses are needed. However, it also
causes the data to be evicted from cache, that is, the act of reading by an I/O device
causes data to be evicted. Thus, the I/O operation proceeds efficiently because it
does not require main memory access. But, if an application does need that data
in the future, it must be read back into the L3 cache from main memory. The input
operation on the Xeon E5-2600/4600 operates as described in the previous paragraph;
the L3 cache is not involved. Thus, the performance improvement involves only output operations.
A final point. Although the output transfer is directly from cache to the I/O
controller, the term direct cache access is not used for this feature. Rather the term
is reserved for the I/O protocol application, as described in the remainder of this
section.

## Slide 33: Cache-Related Performance Issues (1 of 2)
Network traffic is transmitted in the form of a sequence of protocol blocks called packets or protocol data units
The lowest, or link, level protocol is typically Ethernet, so that each arriving and departing block of data consists of an Ethernet packet containing as payload the higher-level protocol packet
The higher-level protocols are usually the Internet Protocol (IP), operating on top of Ethernet and the Transmission Control Protocol (TCP), operating on top of IP
The Ethernet payload consists of a block of data with a TCP header and an IP header
For outgoing data, Ethernet packets are formed in a peripheral component, such as in I/O controller or network interface controller (NIC)
For incoming traffic, the I/O controller strips off the Ethernet information and delivers the TCP/IP packet to the host CPU
Notes: Network traffic is transmitted in the form of a sequence of protocol blocks, called
packets or protocol data units. The lowest, or link, level protocol is typically
Ethernet, so that each arriving and departing block of data consists of an Ethernet
packet containing as payload the higher-level protocol packet. The higher-level protocols
are usually the Internet Protocol (IP), operating on top of Ethernet, and
the Transmission Control Protocol (TCP), operating on top of IP. Accordingly, the
Ethernet payload consists of a block of data with a TCP header and an IP header.
For outgoing data, Ethernet packets are formed in a peripheral component, such
as an I/O controller or network interface controller (NIC). Similarly, for incoming
traffic, the I/O controller strips off the Ethernet information and delivers the TCP/
IP packet to the host CPU.

## Slide 34: Cache-Related Performance Issues (2 of 2)
For both outgoing and incoming traffic the core, main memory, and cache are all involved
In a DMA scheme, when an application wishes to transmit data, it places that data in an application-assigned buffer in main memory
The core transfers this to a system buffer in main memory and creates the necessary TCP and IP headers, which are also buffered in system memory
The packet is then picked up via DMA for transfer via the NIC
This activity engages not only main memory but also the cache
Similar transfers between system and application buffers are required for incoming traffic
Notes: For both outgoing and incoming traffic, the core, main memory, and cache
are all involved. In a DMA scheme, when an application wishes to transmit data, it
places that data in an application-assigned buffer in main memory. The core transfers
this to a system buffer in main memory and creates the necessary TCP and IP
headers, which are also buffered in system memory. The packet is then picked up
via DMA for transfer via the NIC. This activity engages not only main memory but
also the cache. For incoming traffic, similar transfers between system and application
buffers are required.
When large volumes of protocol traffic are processed, two factors in this scenario
degrade performance. First, the core consumes valuable clock cycles in copying
data between system and application buffers. Second, because memory speeds have
not kept up with CPU speeds, the core loses time waiting on memory reads and
writes. In this traditional way of processing protocol traffic, the cache does not help
because the data and protocol headers are constantly changing and thus the cache
must constantly be updated.

## Slide 35: Packet Traffic Steps:
Incoming
Packet arrives
DMA
NIC interrupts host
Retrieve descriptors and headers
Cache miss occurs
Header is processed
Payload transferred
Packet transfer requested
Packet created
Output operation invoked
DMA transfer
NIC signals completion
Driver frees buffer
Outgoing
Notes: To clarify the performance issue and to explain the benefit of DCA as a way
of improving performance, let us look at the processing of protocol traffic in more
detail for incoming traffic. In general terms, the following steps occur:
1. Packet arrives. The NIC receives an incoming Ethernet packet. The NIC processes
and strips off the Ethernet control information. This includes doing an
error detection calculation. The remaining TCP/IP packet is then transferred
to the system’s DMA module, which generally is part of the NIC. The NIC
also creates a packet descriptor with information about the packet, such as its
buffer location in memory.
2. DMA. The DMA module transfers data, including the packet descriptor, to
main memory. It must also invalidate the corresponding cache lines, if any.
3. NIC interrupts host. After a number of packets have been transferred, the
NIC issues an interrupt to the host processor.
4. Retrieve descriptors and headers. The core processes the interrupt, invoking
an interrupt handling procedure, which reads the descriptor and header of the
received packets.
5. Cache miss occurs. Because this is new data coming in, the cache lines corresponding
to the system buffer containing the new data are invalidated. Thus,
the core must stall to read the data from main memory into cache, and then to
core registers.
6. Header is processed. The protocol software executes on the core to analyze
the contents of the TCP and IP headers. This will likely include accessing a
transport control block (TCB), which contains context information related
to TCP. The TCB access may or may not trigger a cache miss, necessitating a
main memory access.
7. Payload transferred. The data portion of the packet is transferred from the
system buffer to the appropriate application buffer.
A similar sequence of steps occurs for outgoing packet traffic, but there are
some differences that affect how the cache is managed. For outgoing traffic, the
following steps occur:
1. Packet transfer requested. When an application has a block of data to transfer
to a remote system, it places the data in an application buffer and alerts the
OS with some type of system call.
2. Packet created. The OS invokes a TCP/IP process to create the TCP/IP packet
for transmission. The TCP/IP process accesses the TCB (which may involve a
cache miss) and creates the appropriate headers. It also reads the data from
the application buffer, and then places the completed packet (headers plus
data) in a system buffer. Note that the data that is written into the system buffer
also exists in the cache. The TCP/IP process also creates a packet descriptor
that is placed in memory shared with the DMA module.
3. Output operation invoked. This uses a device driver program to signal the
DMA module that output is ready for the NIC.
4. DMA transfer. The DMA module reads the packet descriptor. Then, a
DMA transfer is performed from main memory or the last level cache to the NIC.
Note that DMA transfers invalidate the cache line in cache even in
the case of a read (by the DMA module). If the line is modified, this causes a
write back. The core does not do the invalidates. The invalidates happen when
the DMA module reads the data.
5. NIC signals completion. After the transfer is complete, the NIC signals the
driver on the core that originated the send signal.
6. Driver frees buffer. Once the driver receives the completion notice, if frees
up the buffer space for reuse. The core must also invalidate the cache lines
containing the buffer data.
As can be seen, network I/O involves a number of accesses to cache and main
memory and the movement of data between an application buffer and a system
buffer. The heavy involvement of main memory becomes a bottleneck, as both core
and network performance outstrip gains in memory access times.

## Slide 36: Direct Cache Access Strategies
Simplest strategy was implemented as a prototype on a number of Intel Xeon processors between 2006 and 2010
This form of DCA applies only to incoming network traffic
The DCA function in the memory controller sends a prefetch hint to the core as soon as the data is available in system memory
This enables the core to prefetch the data packet from the system buffer
Much more substantial gains can be realized by avoiding the system buffer in main memory altogether
The packet and packet descriptor information are accessed only once in the system buffer by the core
For incoming packets, the core reads the data from the buffer and transfers the packet payload to an application buffer
It has no need to access that data in the system buffer again
Cache injection
Implemented in Intel’s Xeon processor line, referred to as Direct Data I/O
Notes: Several strategies have been proposed for making more efficient use of caches for
network I/O, with the general term direct cache access applied to all of these strategies.
The simplest strategy is one that was implemented as a prototype on a number
of Intel Xeon processors between 2006 and 2010 [KUMA07, INTE08]. This form of
DCA applies only to incoming network traffic. The DCA function in the memory
controller sends a prefetch hint to the core as soon as the data is available in system
memory. This enables the core to prefetch the data packet from the system buffer,
thus avoiding cache misses and the associated waste of core cycles.
While this simple form of DCA does provide some improvement, much more
substantial gains can be realized by avoiding the system buffer in main memory
altogether. For the specific function of protocol processing, note that the packet
and packet descriptor information are accessed only once in the system buffer by
the core. For incoming packets, the core reads the data from the buffer and transfers
the packet payload to an application buffer. It has no need to access that data
in the system buffer again. Similarly, for outgoing packets, once the core has placed
the data in the system buffer, it has no need to access that data again. Suppose,
therefore, that the I/O system were equipped not only with the capability of directly
accessing main memory, but also of accessing the cache, both for input and output
operations. Then it would be possible to use the last-level cache instead of the main
memory to buffer packets and descriptors of incoming and outgoing packets.
This last approach, which is a true DCA, was proposed in [HUGG05]. It has
also been described as cache injection [LEON06]. A version of this more complete
form of DCA is implemented in Intel’s Xeon processor line, referred to as Direct
Data I/O [INTE12].

## Slide 37: Figure 8.17 Comparison of DMA and DDIO
Notes: Intel Direct Data I/O (DDIO) is implemented on all of the Xeon E5 family of processors.
Its operation is best explained with a side-by-side
comparison of transfers with and without DDIO.
First, we look at the case of a packet arriving at the NIC from the
network. Figure 8.17a shows the steps involved for a DMA operation. The NIC
initiates a memory write (1). Then the NIC invalidates the cache lines corresponding
to the system buffer (2). Next, the DMA operation is performed, depositing the
packet directly into main memory (3). Finally, after the appropriate core receives a
DMA interrupt signal, the core can read the packet data from memory through the
cache (4).
Before discussing the processing of an incoming packet using DDIO, we need
to summarize the discussion of cache write policy from Chapter 5, and introduce a
new technique. For the following discussion, there are issues relating to cache coherency
that arise in a multiprocessor or multicore environment. These are discussed
in Chapter 19 but the details need not concern us here. Recall that there are two
techniques for dealing with an update to a cache line:
■ Write through: All write operations are made to main memory as well as to
the cache, ensuring that main memory is always valid. Any other core–cache
module can monitor traffic to main memory to maintain consistency within its
own local cache.
■ Write back: Updates are made only in the cache. When an update occurs, a
dirty bit associated with the line is set. Then, when a block is replaced, it is
written back to main memory if and only if the dirty bit is set.
DDIO uses the write-back strategy in the L3 cache.
A cache write operation may encounter a cache miss, which is dealt with by
one of two strategies:
■ Write allocate: The required line is loaded into the cache from main memory.
Then, the line in the cache is updated by the write operation. This scheme is
typically used with the write-back method.
■ Non-write allocate: The block is modified directly in main memory. No change is
made to the cache. This scheme is typically used with the write-through method.
With the above in mind, we can describe the DDIO strategy for inbound
transfers initiated by the NIC.
1. If there is a cache hit, the cache line is updated, but not main memory; this is
simply the write-back strategy for a cache hit. The Intel literature refers to this
as write update .
2. If there is a cache miss, the write operation occurs to a line in the cache that will not
be written back to main memory. Subsequent writes update the cache line, again
with no reference to main memory or no future action that writes this data to main
memory. The Intel documentation [INTE12] refers to this as write allocate, which
unfortunately is not the same meaning for the term in the general cache literature.
The DDIO strategy is effective for a network protocol application because the
incoming data need not be retained for future use. The protocol application is going
to write the data to an application buffer, and there is no need to temporarily store
it in a system buffer.
Figure 8.17b shows the operation for DDIO input. The NIC initiates a memory
write (1). Then the NIC invalidates the cache lines corresponding to the system buffer
and deposits the incoming data in the cache (2). Finally, after the appropriate core
receives a DCA interrupt signal, the core can read the packet data from the cache (3).
Figure 8.17c shows the steps involved for a DMA operation for
outbound packet transmission. The TCP/IP protocol handler executing on the core reads
data in from an application buffer and writes it out to a system buffer. These data access
operations result in cache misses and cause data to be read from memory and into the L3
cache (1). When the NIC receives notification for starting a transmit operation, it reads
the data from the L3 cache and transmits it (2). The cache access by the NIC causes the
data to be evicted from the cache and written back to main memory (3).
Figure 8.17d shows the steps involved for a DDIO operation for packet transmission.
The TCP/IP protocol handler creates the packet to be transmitted and
stores it in allocated space in the L3 cache, but not in main memory (2). The read
operation initiated by the NIC is satisfied by data from the cache, without causing
evictions to main memory.
It should be clear from these side-by-side comparisons that DDIO is more
efficient than DMA for both incoming and outgoing packets and is therefore better
able to keep up with the high packet traffic rate.

## Slide 38: Evolution of the I/O Function
The CPU directly controls a peripheral device.
A controller or I/O module is added. The CPU uses programmed I/O without interrupts.
Same configuration as in step 2 is used, but now interrupts are employed. The CPU need not spend time waiting for an I/O operation to be performed, thus increasing efficiency.
The I/O module is given direct access to memory via DMA. It can now move a block of data to or from memory without involving the CPU, except at the beginning and end of the transfer.
The I/O module is enhanced to become a processor in its own right, with a specialized instruction set tailored for I/O
The I/O module has a local memory of its own and is, in fact, a computer in its own right. With this architecture a large set of I/O devices can be controlled with minimal CPU involvement.
Notes: As computer systems have evolved, there has been a pattern of increasing complexity
and sophistication of individual components. Nowhere is this more evident than
in the I/O function. We have already seen part of that evolution. The evolutionary
steps can be summarized as follows:
1. The CPU directly controls a peripheral device. This is seen in simple microprocessor-
controlled devices.
2. A controller or I/O module is added. The CPU uses programmed I/O without
interrupts. With this step, the CPU becomes somewhat divorced from the specific
details of external device interfaces.
3. The same configuration as in step 2 is used, but now interrupts are employed.
The CPU need not spend time waiting for an I/O operation to be performed,
thus increasing efficiency.
4. The I/O module is given direct access to memory via DMA. It can now move
a block of data to or from memory without involving the CPU, except at the
beginning and end of the transfer.
5. The I/O module is enhanced to become a processor in its own right, with a
specialized instruction set tailored for I/O. The CPU directs the I/O processor
to execute an I/O program in memory. The I/O processor fetches and executes
these instructions without CPU intervention. This allows the CPU to specify a
sequence of I/O activities and to be interrupted only when the entire sequence
has been performed.
6. The I/O module has a local memory of its own and is, in fact, a computer
in its own right. With this architecture, a large set of I/O devices can be
controlled, with minimal CPU involvement. A common use for such an
architecture has been to control communication with interactive terminals.
The I/O processor takes care of most of the tasks involved in controlling the
terminals.
As one proceeds along this evolutionary path, more and more of the I/O
function is performed without CPU involvement. The CPU is increasingly
relieved of I/O-related tasks, improving performance. With the last two steps
(5–6), a major change occurs with the introduction of the concept of an I/O module
capable of executing a program. For step 5, the I/O module is often referred
to as an I/O channel. For step 6, the term I/O processor is often used. However,
both terms are on occasion applied to both situations. In what follows, we will use
the term I/O channel.

## Slide 39: Figure 8.18 I/O Channel Architecture
Notes: The I/O channel represents an extension of the DMA concept. An I/O
channel has the ability to execute I/O instructions, which gives it complete control
over I/O operations. In a computer system with such devices, the CPU does
not execute I/O instructions. Such instructions are stored in main memory to
be executed by a special-purpose processor in the I/O channel itself. Thus, the
CPU initiates an I/O transfer by instructing the I/O channel to execute a program
in memory. The program will specify the device or devices, the area or
areas of memory for storage, priority, and actions to be taken for certain error
conditions. The I/O channel follows these instructions and controls the data
transfer.
Two types of I/O channels are common, as illustrated in Figure 8.18. A
selector channel controls multiple high-speed devices and, at any one time, is
dedicated to the transfer of data with one of those devices. Thus, the I/O channel
selects one device and effects the data transfer. Each device, or a small set of
devices, is handled by a controller, or I/O module, that is much like the I/O modules
we have been discussing. Thus, the I/O channel serves in place of the CPU in
controlling these I/O controllers. A multiplexor channel can handle I/O with multiple
devices at the same time. For low-speed devices, a byte multiplexor accepts or
transmits characters as fast as possible to multiple devices. For example, the resultant
character stream from three devices with different rates and individual streams
A1A2A3A4 …, B1B2B3B4 …, and C1C2C3C4 … might be A1B1C1A2C2A3B2C3A4,
and so on. For high-speed devices, a block multiplexor interleaves blocks of data
from several devices.

## Slide 40: Universal Serial Bus (USB)
Widely used for peripheral connections
Is the default interface for slower speed devices
Commonly used high-speed I/O
Has gone through multiple generations
  USB 1.0
    Defined a Low Speed data rate of 1.5 Mbps and a Full Speed rate of 12 Mbps
  USB 2.0
    Provides a data rate of 480 Mbps
  USB 3.0
    Higher speed bus called SuperSpeed in parallel with the USB 2.0 bus
    Signaling speed of SuperSpeed is 5 Gbps, but due to signaling overhead the usable data rate is up to 4 Gbps
  USB 3.1
    Includes a faster transfer mode called SuperSpeed+
    This transfer mode achieves a signaling rate of 10 Gbps and a theoretical usable data rate of 9.7 Gbps
Is controlled by a root host controller which attaches to devices to create a local network with a hierarchical tree topology
Notes: USB is widely used for peripheral connections. It is the default interface for slower
speed devices, such as keyboard and pointing devices, but is also commonly used for
high-speed I/O, including printers, disk drives, and network adapters.
USB has gone through multiple generations. The first version, USB 1.0,
defined a Low Speed data rate of 1.5 Mbps and a Full Speed rate of 12 Mbps. USB
2.0 provides a data rate of 480 Mbps. USB 3.0 includes a new, higher speed bus
called SuperSpeed in parallel with the USB 2.0 bus. The signaling speed of Super-
Speed is 5 Gbps, but due to signaling overhead, the usable data rate is up to 4 Gbps.
The most recent specification is USB 3.1, which includes a faster transfer mode
called SuperSpeed+ . This transfer mode achieves a signaling rate of 10 Gbps and a
theoretical usable data rate of 9.7 Gbps.
A USB system is controlled by a root host controller, which attaches to devices
to create a local network with a hierarchical tree topology.

## Slide 41: FireWire Serial Bus
Was developed as an alternative to small computer system interface (SCSI) to be used on smaller systems, such as personal computers, workstations, and servers
Objective was to meet the increasing demands for high I/O rates while avoiding the bulky and expensive I/O channel technologies developed for mainframe and supercomputer systems
IEEE standard 1394, for a High Performance Serial Bus
Uses a daisy chain configuration, with up to 63 devices connected off a single port
1022 FireWire buses can be interconnected using bridges
Provides for hot plugging which makes it possible to connect and disconnect peripherals without having to power the computer system down or reconfigure the system
Provides for automatic configuration
No terminations and the system automatically performs a configuration function to assign addresses
Notes: FireWire was developed as an alternative to small computer system interface (SCSI)
to be used on smaller systems, such as personal computers, workstations, and servers.
The objective was to meet the increasing demands for high I/O rates on these systems,
while avoiding the bulky and expensive I/O channel technologies developed
for mainframe and supercomputer systems. The result is the IEEE standard 1394, for
a High Performance Serial Bus, commonly known as FireWire.
FireWire uses a daisy-chain configuration, with up to 63 devices connected
off a single port. Moreover, up to 1022 FireWire buses can be interconnected using
bridges, enabling a system to support as many peripherals as required.
FireWire provides for what is known as hot plugging, which makes it possible
to connect and disconnect peripherals without having to power the computer system
down or reconfigure the system. Also, FireWire provides for automatic configuration;
it is not necessary manually to set device IDs or to be concerned with the relative
position of devices. With FireWire, there are no terminations, and the system
automatically performs a configuration function to assign addresses. A FireWire bus
need not be a strict daisy chain. Rather, a tree-structured configuration is possible.
An important feature of the FireWire standard is that it specifies a set of three
layers of protocols to standardize the way in which the host system interacts with the
peripheral devices over the serial bus. The physical layer defines the transmission media
that are permissible under FireWire and the electrical and signaling characteristics of
each. Data rates from 25 Mbps to 3.2 Gbps are defined. The link layer describes the
transmission of data in the packets. The transaction layer defines a request–
response protocol that hides the lower-layer details of FireWire from applications.

## Slide 42: SCSI
Small Computer System Interface
A once common standard for connecting peripheral devices to small and medium-sized computers
Has lost popularity to USB and FireWire in smaller systems
High-speed versions remain popular for mass memory support on enterprise systems
Physical organization is a shared bus, which can support up to 16 or 32 devices, depending on the generation of the standard
  The bus provides for parallel transmission rather than serial, with a bus width of 16 bits on earlier generations and 32 bits on later generations
  Speeds range from 5 Mbps on the original SCSI-1 specification to 160 Mbps on SCSI-3 U3
Notes: SCSI is a once common standard for connecting peripheral devices (disks, modems,
printers, etc.) to small and medium-sized computers. Although SCSI has evolved to
higher data rates, it has lost popularity to such competitors as USB and FireWire
in smaller systems. However, high-speed versions of SCSI remain popular for mass
memory support on enterprise systems. For example, the IBM zEnterprise EC12
and other IBM mainframes offer support for SCSI, and a number of Seagate hard
drive systems use SCSI.
The physical organization of SCSI is a shared bus, which can support up to 16
or 32 devices, depending on the generation of the standard. The bus provides for
parallel transmission rather than serial, with a bus width of 16 bits on earlier generations
and 32 bits on later generations. Speeds range from 5 Mbps on the original
SCSI-1 specification to 160 Mbps on SCSI-3 U3.

## Slide 43: Thunderbolt
Provides up to 10 Gbps throughput in each direction and up to 10 Watts of power to connected peripherals
Most recent and fastest peripheral connection technology to become available for general-purpose use
Developed by Intel with collaboration from Apple
The technology combines data, video, audio, and power into a single high-speed connection for peripherals such as hard drives, RAID arrays, video-capture boxes, and network interfaces
Notes: The most recent, and fastest, peripheral connection technology to become available for
general-purpose use is Thunderbolt, developed by Intel with collaboration from Apple.
One Thunderbolt cable can manage the work previously required of multiple cables.
The technology combines data, video, audio, and power into a single high-speed connection
for peripherals such as hard drives, RAID (Redundant Array of Independent
Disks) arrays, video-capture boxes, and network interfaces. It provides up to 10 Gbps
throughput in each direction and up to 10 Watts of power to connected peripherals.

## Slide 44: InfiniBand
I/O specification aimed at the high-end server market
First version was released in early 2001
Heavily relied on by IBM zEnterprise series of mainframes
Standard describes an architecture and specifications for data flow among processors and intelligent I/O devices
Has become a popular interface for storage area networking and other large storage configurations
Enables servers, remote storage, and other network devices to be attached in a central fabric of switches and links
The switch-based architecture can connect up to 64,000 servers, storage systems, and networking devices
Notes: InfiniBand is an I/O specification aimed at the high-end server market. The first
version of the specification was released in early 2001 and has attracted numerous
vendors. For example, IBM zEnterprise series of mainframes has relied heavily on
InfiniBand for a number of years. The standard describes an architecture and specifications
for data flow among processors and intelligent I/O devices. InfiniBand has
become a popular interface for storage area networking and other large storage configurations.
In essence, InfiniBand enables servers, remote storage, and other network
devices to be attached in a central fabric of switches and links. The switch-based
architecture can connect up to 64,000 servers, storage systems, and networking devices.

## Slide 45: PCI Express and SATA
High-speed bus system for connecting peripherals of a wide variety of types and speeds
SATA
Serial Advanced Technology Attachment
An interface for disk storage systems
Provides data rates of up to 6 Gbps, with a maximum per device of 300 Mbps
Widely used in desktop computers and in industrial and embedded applications
PCI Express
Notes: PCI Express is a high-speed
bus system for connecting peripherals of a wide variety
of types and speeds. Chapter 3 discusses PCI Express in detail.
Serial ATA (Serial Advanced Technology Attachment) is an interface for disk storage
systems. It provides data rates of up to 6 Gbps, with a maximum per device of
300 Mbps. SATA is widely used in desktop computers, and in industrial and embedded
applications.

## Slide 46: Ethernet
Predominant wired networking technology
Has evolved to support data rates up to 100 Gbps and distances from a few meters to tens of km
Has become essential for supporting personal computers, workstations, servers, and massive data storage devices in organizations large and small
Began as an experimental bus-based 3-Mbps system
Has moved from bus-based to switch-based
  Data rate has periodically increased by an order of magnitude
  There is a central switch with all of the devices connected directly to the switch
  Ethernet systems are currently available at speeds up to 100 Gbps
Notes: Ethernet is the predominant wired networking technology, used in homes, offices,
data centers, enterprises, and wide-area networks. As Ethernet has evolved to support
data rates up to 100 Gbps and distances from a few meters to tens of km, it
has become essential for supporting personal computers, workstations, servers, and
massive data storage devices in organizations large and small.
Ethernet began as an experimental bus-based 3-Mbps system. With a bus system,
all of the attached devices, such as PCs, connect to a common coaxial cable,
much like residential cable TV systems. The first commercially-available Ethernet,
and the first version of IEEE 802.3, were bus-based systems operating at 10
Mbps. As technology has advanced, Ethernet has moved from bus-based
to switch-based, and the data rate has periodically increased by an order of magnitude. With
switch-based systems, there is a central switch, with all of the devices connected
directly to the switch. Currently, Ethernet systems are available at speeds up to 100
Gbps. Here’s a brief chronology.
■ 1983: 10 Mbps (megabit per second, million bits per second)
■ 1995: 100 Mbps
■ 1998: 1 Gbps (gigabit per second, billion bits per second)
■ 2003: 10 Gbps
■ 2010: 40 Gbps and 100 Gbps

## Slide 47: Wi-Fi
Is the predominant wireless Internet access technology
Now connects computers, tablets, smart phones, and other electronic devices such as video cameras TVs and thermostats
In the enterprise has become an essential means of enhancing worker productivity and network effectiveness
Public hotspots have expanded dramatically to provide free Internet access in most public places
As the technology of antennas, wireless transmission techniques, and wireless protocol design has evolved, the IEEE 802.11 committee has been able to introduce standards for new versions of Wi-Fi at higher speeds
Current version is 802.11ac (2014) with a maximum data rate of 3.2 Gbps
Notes: Wi-Fi is the predominant wireless Internet access technology, used in homes, offices,
and public spaces. Wi-Fi in the home now connects computers, tablets, smart phones,
and a host of electronic devices, such as video cameras, TVs, and thermostats. Wi-Fi
in the enterprise has become an essential means of enhancing worker productivity
and network effectiveness. And public Wi-Fi hotspots have expanded dramatically
to provide free Internet access in most public places.
As the technology of antennas, wireless transmission techniques, and wireless
protocol design has evolved, the IEEE 802.11 committee has been able to introduce
standards for new versions of Wi-Fi at ever-higher speeds. Once the standard is
issued, industry quickly develops the products. Here’s a brief chronology, starting
with the original standard, which was simply called IEEE 802.11, and showing the
maximum data rate for each version:
■ 802.11 (1997): 2 Mbps (megabit per second, million bits per second)
■ 802.11a (1999): 54 Mbps
■ 802.11b (1999): 11 Mbps
■ 802.11n (1999): 600 Mbps
■ 802.11g (2003): 54 Mbps
■ 802.11ad (2012): 6.76 Gbps (billion bits per second)
■ 802.11ac (2014): 3.2 Gbps

## Slide 48: Figure 8.19 IBM z13 I/O Channel Structure
Logical
partition
Logical
partition
Logical
partition
Logical
partition
d
1
5
p
a
r
t
i
t
i
o
n
s
p
e
r
c
h
a
n
n
e
l
s
u
b
s
y
s
t
e
m
d
8
5
p
a
r
t
i
t
i
o
n
s
p
e
r
s
y
s
t
e
m
Channel
S
u
b
s
y
s
t
e
m
Channel
S
u
b
s
y
s
t
e
m
Channel
S
u
b
s
y
s
t
e
m
Channel
S
u
b
s
y
s
t
e
m
6 channel
s
u
b
s
y
s
t
e
m
s
Channel
S
u
b
s
y
s
t
e
m
4
s
u
b
c
h
a
n
n
e
l
s
e
t
s
p
e
r
c
h
a
n
n
e
l
s
u
b
s
y
s
t
e
m
up to 64k
c
h
a
n
n
e
l
s
p
e
r
s
u
b
c
h
a
n
n
e
l
s
e
t
S
u
b
c
h
a
n
n
e
l
Set
S
u
b
c
h
a
n
n
e
l
Set
S
u
b
c
h
a
n
n
e
l
Set
S
u
b
c
h
a
n
n
e
l
Set
Notes: The z13 has a dedicated I/O subsystem that manages all I/O operations, completely
off- loading this processing and memory burden from the main processors.
Figure 8.19 shows the logical structure of the I/O subsystem. Of the 168
core processors, up to 24 of these can be dedicated for I/O use, creating 46 channel
subsystems (CSS) . Each CSS is made up of the following elements:
■ System assist processor (SAP): The SAP is a core processor configured for I/O
operation. Its role is to offload I/O operations and manage channels and the
I/O operations queues. It relieves the other processors of all I/O tasks, allowing
them to be dedicated to application logic.
■ Hardware system area (HSA): The HSA is a reserved part of the system memory
containing the I/O configuration. It is used by SAPs. A fixed amount of
32 GB is reserved, which is not part of the customer purchased memory. This provides for
greater configuration flexibility and higher availability by eliminating planned and preplanned outages.
■ Logical partitions: A logical partition is a form of virtual machine, which is in
essence, a logical processor defined at the operating system level. Each CSS
supports up to 16 logical partitions.
■ Subchannels: A subchannel appear to a program as a logical device and contain
the information required to perform an I/O operation. One subchannel
exists for each I/O device addressable by the CSS. A subchannel is used by the
channel subsystem code running on a partition to pass an I/O request to the
channel subsystem. A subchannel is assigned for each device defined to the
logical partition. Up to 196k subchannels are supported per CSS.
■ Channel path: A channel path is a single interface between a channel subsystem
and one or more control units, via a channel. Commands and data are sent
across a channel path to perform I/O requests. Each CSS can have up to 256
channel paths.
■ Channel: Channels are small processors that communicate with the I/O control
units (CUs). They manage the data transfer between memory and the
external devices.
This elaborate structure enables the mainframe to manage a massive number
of I/O devices and communication links. All I/O processing is offloaded from
the application and server processors, enhancing performance. The channel subsystem
processors are somewhat general in configuration, enabling them to manage
a wide variety of I/O duties and to keep up with evolving requirements. The channel
processors are specifically programmed for the I/O control units to which they
interface.

## Slide 49: Figure 8.20 IBM z13 I/O System Structure
Notes: To explain the I/O system organization, we need to first briefly explain the physical
layout of the z13. The system has the following characteristics:
• Weight: 2567 kg (5657 lbs)
• Width: 1.847 m (6.06 ft)
• Depth: 1.806 m (5.9 ft)
• Height: 2.154 m (7.1 ft)
Not exactly a laptop.
The system consists of two large bays called frames bolted together, that house
the various components of the z13. The A frame houses four processor drawers
interconnected via Ethernet, and one PCIe I/O drawer, which contains I/O hardware,
including multiplexors and channels. The A frame also includes two support
servers used by a system manager for platform management, battery backup, and a
cooling unit (water or air).
The Z frame houses up to four I/O drawers, which can be a combination of
PCIe drawers and customer-selected I/O drawers. The Z frame also includes battery
backup and a keyboard/display tray, which contains the keyboards and the displays
that are connected to the support servers.
With this background, we now show a typical configuration of the z13 I/O system
structure (Figure 8.20). Each z13 processor drawer supports two types of internal
(i.e., internal to the A and Z frames) I/O infrastructures: PCI Express (PCIe)
and Infiniband. Each processor drawer includes a card containing the channel controller
which provides connectivity to the I/O drawers. These channel controllers
are referred to as fanouts .
The InfiniBand connections from the processor book to the I/O drawers
are via a Host Channel Adapter (HCA) fanout, which has InfiniBand links to
InfiniBand multiplexors in the I/O drawer. The InfiniBand multiplexors are used
to interconnect servers, communications infrastructure equipment, storage, and
embedded systems. In addition to using InfiniBand to interconnect systems, all of
which use InfiniBand, the InfiniBand multiplexor supports other I/O technologies,
such as Ethernet. Ethernet connections provide 1-Gbps and 10-Gbps connections
to a variety of devices that support this popular local area network technology. One
noteworthy use of Ethernet is to construct large server farms, particularly to interconnect
blade servers with each other and with other mainframes.
The PCIe connections from the processor book to the I/O drawers are via
a PCIe fanout to PCIe switches. The PCIe switches can connect to a number of
I/O device controllers. Typical examples for z13 are 1-Gbps and 10-Gbps Ethernet,
Fiber Channel, and (OSA) Express Controller. OSA is an I/O adapter technology
that provides streamlined, high-speed transfer between system memory and a highspeed
network interface, such as Ethernet.

## Slide 50: Summary
Chapter 8
  External devices
  I/O modules
  Programmed I/O
  Interrupt-driven I/O
  Direct memory access
Input/Output
  Direct Cache Access
  I/O channels and processors
  External interconnection standards
  IBM zEnterprise EC12 I/O structure
Notes: Chapter 8 summary.