## Slide 1: Computer Organization and Architecture Designing for Performance
Chapter 12
Digital Logic
11th Edition, Global Edition

## Slide 2: Boolean Algebra
Mathematical discipline used to design and analyze the behavior of the digital circuitry in digital computers and other digital systems
Named after George Boole
  English mathematician
  Proposed basic principles of the algebra in 1854
  Claude Shannon suggested Boolean algebra could be used to solve problems in relay-switching circuit design
  Is a convenient tool:
  Analysis
    It is an economical way of describing the function of digital circuitry
  Design
    Given a desired function, Boolean algebra can be applied to develop a simplified implementation of that function
Notes: 2
The digital circuitry in digital computers and other digital systems is designed, and its behavior is analyzed, with the use of a mathematical discipline known as Boolean algebra. The name is in honor of an English mathematician George Boole, who proposed the basic principles of this algebra in 1854 in his treatise, An Investigation of the Laws of Thought on Which to Found the Mathematical Theories of Logic and Probabilities. In 1938, Claude Shannon, a research assistant in the Electrical Engineering Department at M.I.T., suggested that Boolean algebra could be used to solve problems in relay-switching circuit design [SHAN38]. Shannon’s techniques were subsequently used in the analysis and design of electronic digital circuits. Boolean algebra turns out to be a convenient tool in two areas:
• Analysis: It is an economical way of describing the function of digital circuitry.
• Design: Given a desired function, Boolean algebra can be applied to develop a simplified implementation of that function.

## Slide 3: Table 12.2 Correspondence Between Boolean Algebra and Operations on Sets
Boolean |  | Sets | 
Function | Description | Function | Description
A AND B | 1 if and only if A and B are 1 | A  B | Set of elements that belong to both A and B (intersection)
A OR B | 1 if A or B or both are 1; 0 if both A and B are 0 | A  B | Set of elements that belong to A or B or both (union)
A OR B | 1 if and only if A is 0 | A | Set of elements not in A (complement of A)
Notes: 4
It can be helpful for visualizing Boolean operations to illustrate corresponding operations
on sets. We can define a set as a collection of elements S, together with a rule
that determines what elements belong to S. For example, the set of positive integers
less than 5 is {1, 2, 3, 4}.
Logical operations can be performed on sets in much the same way as on
Boolean variables. Corresponding to the basic Boolean operations of AND, OR,
and NOT are the logical set operations of intersection, union, and complement;
these are shown in Table 12.2.
The intersection of two sets A and B is the set of all elements that belong to both
A and B. This operation is designated with the operator ∩ . For example, if A is the
set of positive integers less than 5 and B is the set of even positive integers less than
10, then A ∩ B = { 2 , 4 } . Intersection corresponds to the Boolean operator AND.
The union of two sets A and B is the set of all elements that belong to A or B
or both. This operation is designated with the operator ∪. For A and B defined in
the preceding paragraph, A ∪ B = { 1 , 2 , 3 , 4 , 6 , 8 } . Union corresponds to the
Boolean operator OR.
The complement of a set A depends on the context. Generally, attention is
confined to subsets of some given set X, which is considered as the universal set for
this context. The complement of a set S, designated by an S, consists of all the elements
in the universal set not found in S. For example, if X is the set of all positive
integers, then for A and B defined above, A is the set of all integers greater than 4,
and B is the set consisting of all odd positive integers plus all even positive integers
greater than 9. Complement corresponds to the Boolean operator NOT.

## Slide 4: Boolean Variables and Operations
Makes use of variables and operations
  Are logical
  A variable may take on the value 1 (TRUE) or 0 (FALSE)
  Basic logical operations are AND, OR, and NOT
  AND
  Yields true (binary value 1) if and only if both of its operands are true
  In the absence of parentheses the AND operation takes precedence over the OR operation
  When no ambiguity will occur the AND operation is represented by simple concatenation instead of the dot operator
  OR
  Yields true if either or both of its operands are true
  NOT
  Inverts the value of its operand
Notes: 3
As with any algebra, Boolean algebra makes use of variables and operations. In this case, the variables and operations are logical variables and operations. Thus, a variable may take on the value 1 (TRUE) or 0 (FALSE). The basic logical operations
are AND, OR, and NOT, which are symbolically represented by dot, plus sign, and overbar:
A AND B = A * B
A OR B = A + B
NOT A = Ā
The operation AND yields true (binary value 1) if and only if both of its operands are true. The operation OR yields true if either or both of its operands are true. The unary operation NOT inverts the value of its operand.
In the absence of parentheses, the AND operation takes precedence over the OR operation. Also, when no ambiguity will occur, the AND operation is represented by simple concatenation instead of the dot operator.

## Slide 5: Table 12.1 Boolean Operators
(b) Boolean Operators Extended to More than Two Inputs (A, B, . . .)
Operation | Expression | Output = 1 if
AND | A · B · … | All of the set {A, B, …} are 1.
OR | A + B + … | Any of the set {A, B, …} are 1.
NAND | A · B · … | Any of the set {A, B, …} are 0.
NOR | A + B + … | All of the set {A, B, …} are 0.
XOR | A  B  … | The set {A, B, …} contains an odd number of ones.
A | B | NOT A (A) | A AND B (A · B) | A OR B (A + B) | A NAND B (A · B) | A NOR B (A + B) | A XOR B (A  B)
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
(a) Boolean Operators of Two Input Variables
Notes: 4
Table 12.1a defines the basic logical operations in a form known as a truth table, which lists the value of an operation for every possible combination of values of operands. The table also lists three other useful operators: XOR, NAND, and NOR. The exclusive-or (XOR) of two logical operands is 1 if and only if exactly one of the operands has the value 1. The NAND function is the complement (NOT) of
the AND function, and the NOR is the complement of OR.
As we shall see, these three new operations can be useful in implementing certain digital circuits.
The logical operations, with the exception of NOT, can be generalized to more than two variables, as shown in Table 12.1b.

## Slide 6: Figure 12.1 Basic Boolean Functions of Two Variables
Notes: With these definitions in mind, we can visualize the Boolean operators defined
in Table 12.1a using Figure 12.1. The Boolean variables are represented by circles,
which can also be viewed as sets depicted in a Venn diagram. From the perspective
of Boolean algebra, the surrounding rectangle, including the circles, represents all
possible combinations of values of A and B. From a set perspective, the surrounding
rectangle represents the universal set.

## Slide 7: Figure 12.2 Venn Diagram for Three Boolean Variables
Notes: Figure 12.2 depicts Venn diagrams corresponding to three Boolean variables.
The three-bit numbers give the Boolean values for ABC in the different
regions.

## Slide 8: Table 12.3 Basic Identities of Boolean Algebra
Basic Postulates |  | 
A · B = B · A A · (B + C) = (A · B) + (A · C) 1 · A = A A · = 0 | A + B = B + A A + (B · C) = (A + B) · (A + C) 0 + A = A A + = 1 | Commutative Laws Distributive Laws Identity Elements Inverse Elements
Other Identities |  | 
0 · A = 0 A · A = A A · (B · C) = (A · B) · C = + | 1 + A = 1 A + A = A A + (B + C) = (A + B) + C = | Associative Laws DeMorgan’s Theorem
Basic Postulates |  | 
 |  | Commutative Laws Distributive Laws Identity Elements Inverse Elements
Other Identities |  | 
 |  | Associative Laws DeMorgan’s Theorem
Notes: Table 12.3 summarizes key identities of Boolean algebra. The equations have
been arranged in two columns to show the complementary, or dual, nature of the
AND and OR operations. There are two classes of identities: basic rules (or postulates ),
which are stated without proof, and other identities that can be derived from
the basic postulates. The postulates define the way in which Boolean expressions
are interpreted. One of the two distributive laws is worth noting because it differs
from what we would find in ordinary algebra:
A + (B * C) = (A + B) * (A + C)
The two bottom-most expressions are referred to as DeMorgan’s theorem. We can
restate them as follows:
A NOR B = AND B
A NAND B = OR B
The reader is invited to verify the expressions in Table 12.3 by substituting
actual values (1s and 0s) for the variables A, B, and C.
.
Table 12.3 summarizes key identities of Boolean algebra. The equations have
been arranged in two columns to show the complementary, or dual, nature of the
AND and OR operations. There are two classes of identities: basic rules (or postulates ),
which are stated without proof, and other identities that can be derived from
the basic postulates. The postulates define the way in which Boolean expressions
are interpreted. One of the two distributive laws is worth noting because it differs
from what we would find in ordinary algebra:
A + (B * C) = (A + B) * (A + C)
The two bottom-most expressions are referred to as DeMorgan’s theorem. We can
restate them as follows:
A NOR B = Ā AND B
A NAND B = Ā OR B
The reader is invited to verify the expressions in Table 12.3 by substituting
actual values (1s and 0s) for the variables A, B, and C.
.

## Slide 9: Figure 12.3 Basic Logic Gates
Notes: The fundamental building block of all digital logic circuits is the gate. Logical functions
are implemented by the interconnection of gates.
A gate is an electronic circuit that produces an output signal that is a simple
Boolean operation on its input signals. The basic gates used in digital logic are
AND, OR, NOT, NAND, NOR, and XOR. Figure 12.3 depicts these six gates. Each
gate is defined in three ways: graphic symbol, algebraic notation, and truth table.
The symbology used in this chapter is from the IEEE standard, IEEE Std 91. Note
that the inversion (NOT) operation is indicated by a circle.
Each gate shown in Figure 12.3 has one or two inputs and one output. However,
as indicated in Table 12.1b, all of the gates except NOT can have more than
two inputs. Thus, (X + Y + Z) can be implemented with a single OR gate with
three inputs. When one or more of the values at the input are changed, the correct
output signal appears almost instantaneously, delayed only by the propagation time
of signals through the gate (known as the gate delay ). The significance of this delay
is discussed in Section 12.3. In some cases, a gate is implemented with two outputs,
one output being the negation of the other output.
Here we introduce a common term: we say that to assert a signal is to cause a
signal line to make a transition from its logically false (0) state to its logically true
(1) state. The true (1) state is either a high or low voltage state, depending on the
type of electronic circuitry.
Typically, not all gate types are used in implementation. Design and fabrication
are simpler if only one or two types of gates are used. Thus, it is important to
identify functionally complete sets of gates. This means that any Boolean function
can be implemented using only the gates in the set. The following are functionally
complete sets:
■ AND, OR, NOT
■ AND, NOT
■ OR, NOT
■ NAND
■ NOR
It should be clear that AND, OR, and NOT gates constitute a functionally
complete set, because they represent the three operations of Boolean algebra. For
the AND and NOT gates to form a functionally complete set, there must be a way
to synthesize the OR operation from the AND and NOT operations.

## Slide 10: Figure 12.4 Some Uses of NAND Gates
Notes: Similarly, the OR and NOT operations are functionally complete because
they can be used to synthesize the AND operation.
Figure 12.4 shows how the AND, OR, and NOT functions can be implemented
solely with NAND gates.

## Slide 11: Figure 12.5 Some Uses of NOR Gates
Notes: Figure 12.5 shows the same thing for NOR
gates. For this reason, digital circuits can be, and frequently are, implemented
solely with NAND gates or solely with NOR gates.
With gates, we have reached the most primitive circuit level of computer
hardware. An examination of the transistor combinations used to construct gates
departs from that realm and enters the realm of electrical engineering. For our purposes,
however, we are content to describe how gates can be used as building blocks
to implement the essential logical circuits of a digital computer.

## Slide 12: Combinational Circuit
An interconnected set of gates whose output at any time is a function only of the input at that time
The appearance of the input is followed almost immediately by the appearance of the output, with only gate delays
Consists of n binary inputs and m binary outputs
Can be defined in three ways:
Truth table
For each of the 2n possible combinations of input signals, the binary value of each of the m output signals is listed
Graphical symbols
The interconnected layout of gates is depicted
Boolean equations
Each output signal is expressed as a Boolean function of its input signals
Notes: A combinational circuit is an interconnected set of gates whose output at any time is a function only of the input at that time. As with a single gate, the appearance of the input is followed almost immediately by the appearance of the output, with only gate delays.
In general terms, a combinational circuit consists of n binary inputs and m binary outputs. As with a gate, a combinational circuit can be defined in three ways:
Truth table: For each of the 2n possible combinations of input signals, the binary value of each of the m output signals is listed.
Graphical symbols: The interconnected layout of gates is depicted.
Boolean equations: Each output signal is expressed as a Boolean function of
its input signals.

## Slide 13: Table 12.4 A Boolean Function of Three Variables
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: Any Boolean function can be implemented in electronic form as a network of gates. For any given function, there are a number of alternative realizations. Consider the Boolean function represented by the truth table in Table 12.4.
There are three combinations of input values that cause F to be 1, and if any one of these combinations occurs, the result is 1. This form of expression, for self- evident reasons, is known as the sum of products (SOP) form.

## Slide 14: Figure 12.6 Sum-of-Products Implementation of Table 12.4
Notes: Figure 12.6 shows a straightforward implementation with AND, OR, and NOT gates.

## Slide 15: Figure 12.7 Product-of-Sums Implementation of Table 12.4
Notes: Another form can also be derived from the truth table. The SOP form
expresses that the output is 1 if any of the input combinations that produce 1 is true.
We can also say that the output is 1 if none of the input combinations that produce
0 is true.
This is in Product of sums (POS) form, which is illustrated in Figure 12.7. For clarity, NOT gates are not shown. Rather, it is assumed that each input signal and its complement are available. This simplifies the logic diagram and makes the inputs to the gates more readily apparent.
Thus, a Boolean function can be realized in either SOP or POS form. At this point, it would seem that the choice would depend on whether the truth table contains more 1s or 0s for the output function: The SOP has one term for each 1, and the POS has one term for each 0. However, there are other considerations:
It is often possible to derive a simpler Boolean expression from the truth table than either SOP or POS
It may be preferable to implement the function with a single gate type (NAND or NOR)
The significance of the first point is that, with a simpler Boolean expression, fewer gates will be needed to implement the function. Three methods that can be used to achieve simplification are
• Algebraic simplification
• Karnaugh maps
• Quine–McCluskey tables

## Slide 16: Figure 12.8 Simplified Implementation of Table 12.4
Notes: Algebraic simplification involves the application of the identities of Table 12.3 to reduce the Boolean expression to one with fewer elements.
For example, consider again Equation (12.1).
This expression can be implemented as shown in Figure 12.8. The simplification of Equation (12.1) was done essentially by observation. For more complex expressions, some more systematic approach is needed.

## Slide 17: Figure 12.9 The Use of Karnaugh Maps to Represent Boolean Functions
Notes: For purposes of simplification, the Karnaugh map is a convenient way of representing a Boolean function of a small number (up to four) of variables. The map is an array of 2n squares, representing all possible combinations of values of n binary variables. Figure 12.9a shows the map of four squares for a function of two variables. It is essential for later purposes to list the combinations in the order 00, 01, 11, 10. Because the squares corresponding to the combinations are to be used for recording information, the combinations are customarily written above the squares. In the case of three variables, the representation is an arrangement of eight squares (Figure 12.9b), with the values for one of the variables to the left and for the other two variables above the squares. For four variables, 16 squares are needed, with the arrangement indicated in Figure 12.9c.
The map can be used to represent any Boolean function in the following
way. Each square corresponds to a unique product in the sum-of-products
form, with a 1 value corresponding to the variable and a 0 value corresponding to the
NOT of that variable. Thus, the product AB corresponds to the fourth square
in Figure 12.9a. For each such product in the function, 1 is placed in the corresponding
square. Thus, for the two-variable example, the map corresponds to
AB + AB. Given the truth table of a Boolean function, it is an easy matter to
construct the map: for each combination of values of variables that produce a
result of 1 in the truth table, fill in the corresponding square of the map with 1.
Figure 12.9b shows the result for the truth table of Table 12.4. To convert from a
Boolean expression to a map, it is first necessary to put the expression into what
is referred to as canonical form: each term in the expression must contain each
variable. So, for example, if we have Equation (12.3), we must first expand it into
the full form of Equation (12.1) and then convert this to a map.
The labeling used in Figure 12.9d emphasizes the relationship between variables
and the rows and columns of the map. Here the two rows embraced by the
symbol A are those in which the variable A has the value 1; the rows not embraced
by the symbol A are those in which A is 0; similarly for B, C, and D.

## Slide 18: Figure 12.10 The Use of Karnaugh Maps
Notes: Once the map of a function is created, we can often write a simple algebraic expression for it by noting the arrangement of the 1s on the map. The principle is as follows. Any two squares that are adjacent differ in only one of the variables. If two adjacent squares both have an entry of one, then the corresponding product terms differ in only one variable. In such a case, the two terms can be merged by eliminating that variable. For example, in Figure 12.10a, the two adjacent squares correspond to the two terms ABCD and ABCD.
This process can be extended in several ways. First, the concept of adjacency can be extended to include wrapping around the edge of the map. Thus, the top square of a column is adjacent to the bottom square, and the leftmost square of a row is adjacent to the rightmost square. These conditions are illustrated in Figures 12.10b and c. Second, we can group not just 2 squares but 2n adjacent squares (i.e., 2, 4, 8, etc.). The next three examples in Figure 12.10 show groupings of 4 squares. Note that in this case, two of the variables can be eliminated. The last three examples show groupings of 8 squares, which allow three variables to be eliminated.
We can summarize the rules for simplification as follows:
1. Among the marked squares (squares with a 1), find those that belong to a unique largest block of 1, 2, 4, or 8 and circle those blocks.
2. Select additional blocks of marked squares that are as large as possible and as few in number as possible, but include every marked square at least once. The results may not be unique in some cases. For example, if a marked square combines with exactly two other squares, and there is no fourth marked square to complete a larger group, then there is a choice to be made as two which of the two groupings to choose. When you are circling groups, you are allowed to use the same 1 value more than once.
3. Continue to draw loops around single marked squares, or pairs of adjacent marked squares, or groups of four, eight, and so on in such a way that every marked square belongs to at least one loop; then use as few of these blocks as possible to include all marked squares.

## Slide 19: Figure 12.11 Overlapping Groups
Notes: Figure 12.11a, based on Table 12.4, illustrates the simplification process. If any
isolated 1s remain after the groupings, then each of these is circled as a group of 1s.
Finally, before going from the map to a simplified Boolean expression, any group of 1s that is completely overlapped by other groups can be eliminated. This is shown in Figure 12.11b. In this case, the horizontal group is redundant and may be ignored in creating the Boolean expression.
One additional feature of Karnaugh maps needs to be mentioned. In some cases, certain combinations of values of variables never occur, and therefore the corresponding output never occurs. These are referred to as “don’t care” conditions. For each such condition, the letter “d” is entered into the corresponding square of the map. In doing the grouping and simplification, each “d” can be treated as a 1 or 0, whichever leads to the simplest expression.

## Slide 20: Table 12.5 Truth Table for the One-Digit Packed Decimal Incrementer
Number | Input |  |  |  | Number | Output |  |  | 
 | A | B | C | D |  | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 3 | 0 | 0 | 1 | 1
3 | 0 | 0 | 1 | 1 | 4 | 0 | 1 | 0 | 0
4 | 0 | 1 | 0 | 0 | 5 | 0 | 1 | 0 | 1
5 | 0 | 1 | 0 | 1 | 6 | 0 | 1 | 1 | 0
6 | 0 | 1 | 1 | 0 | 7 | 0 | 1 | 1 | 1
7 | 0 | 1 | 1 | 1 | 8 | 1 | 0 | 0 | 0
8 | 0 | 0 | 0 | 0 | 9 | 1 | 0 | 0 | 1
9 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Don’t care condition | 1 | 0 | 1 | 0 |  | d | d | d | d
 | 1 | 0 | 1 | 1 |  | d | d | d | d
 | 1 | 1 | 0 | 0 |  | d | d | d | d
 | 1 | 1 | 0 | 1 |  | d | d | d | d
 | 1 | 1 | 1 | 0 |  | d | d | d | d
 | 1 | 1 | 1 | 1 |  | d | d | d | d
Notes: Table 12.5 shows the truth table for producing a 4-bit result that is one more than a 4-bit BCD input. The addition is modulo 10. Thus, 9 + 1 = 0. Also, note that six of the input codes produce “don’t care” results, because those are not valid BCD inputs.

## Slide 21: Figure 12.12 Karnaugh Maps for the Incrementer
Notes: Figure 12.12 shows the resulting Karnaugh maps for each of the output variables. The d squares are used to achieve the best possible groupings.

## Slide 22: Table 12.6 First Stage of Quine–McCluskey Method
Product Term | Index | A | B | C | D | 
D | 1 | 0 | 0 | 0 | 1 |  
B D | 5 | 0 | 1 | 0 | 1 | 
B C | 6 | 0 | 1 | 1 | 0 | 
A B | 12 | 1 | 1 | 0 | 0 | 
B C D | 7 | 0 | 1 | 1 | 1 | 
A C D | 11 | 1 | 0 | 1 | 1 | 
A B D | 13 | 1 | 1 | 0 | 1 | 
A B C D | 15 | 1 | 1 | 1 | 1 | 
Product Term | Index | A | B | C | D | 
 | 1 | 0 | 0 | 0 | 1 |  
 | 5 | 0 | 1 | 0 | 1 | 
 | 6 | 0 | 1 | 1 | 0 | 
 | 12 | 1 | 1 | 0 | 0 | 
 | 7 | 0 | 1 | 1 | 1 | 
 | 11 | 1 | 0 | 1 | 1 | 
 | 13 | 1 | 1 | 0 | 1 | 
A B C D | 15 | 1 | 1 | 1 | 1 | 
Notes: For more than four variables, the Karnaugh map method becomes increasingly cumbersome. With five variables, two 16 * 16 maps are needed, with one map considered to be on top of the other in three dimensions to achieve adjacency. Six variables require the use of four 16 * 16 tables in four dimensions! An alternative approach is a tabular technique, referred to as the Quine–McCluskey method. The method is suitable for programming on a computer to give an automatic tool for producing minimized Boolean expressions.
The first step is to construct a table in which each row corresponds to one of the product terms of the expression. The terms are grouped according to the number of complemented variables. That is, we start with the term with no complements, if it exists, then all terms with one complement, and so on. Table 12.6 shows the list for our example expression, with horizontal lines used to indicate the grouping. For clarity, each term is represented by a 1 for each uncomplemented variable and a 0 for each complemented variable. Thus, we group terms according to the number of 1s they contain. The index column is simply the decimal equivalent and is useful in what follows.
The next step is to find all pairs of terms that differ in only one variable, that is, all pairs of terms that are the same except that one variable is 0 in one of the terms and 1 in the other. Because of the way in which we have grouped the terms, we can do this by starting with the first group and comparing each term of the first group with every term of the second group. Then compare each term of the second group with all of the terms of the third group, and so on. Whenever a match is found, place a check next to each term, combine the pair by eliminating the variable that differs in the two terms, and add that to a new list. This process continues until the entire original table has been examined.
The new table is organized into groups, as indicated, in the same fashion as the first table. The second table is then processed in the same manner as the first. That is, terms that differ in only one variable are checked and a new term produced for a third table. In this example, the third table that is produced contains only one term: BD.
In general, the process would proceed through successive tables until a table with no matches was produced. In this case, this has involved three tables.

## Slide 23: Table 12.7 Last Stage of Quine–McCluskey Method
 | ABCD | AB | AB | ACD | BCD |  |  | 
BD | X | X |  |  | X |  | X | 
D |  |  |  |  |  |  |  | 
B C |  |  |  |  |  |  |  | 
A B |  |  |  |  |  |  |  | 
A C D |  |  |  |  |  |  |  | 
 | ABCD |  |  |  |  |  |  | 
BD | X | X |  |  | X |  | X | 
 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 
A C D |  |  |  |  |  |  |  | 
X
X
X
X
Notes: Once the process just described is completed, we have eliminated many of the possible terms of the expression. Those terms that have not been eliminated are used to construct a matrix, as illustrated in Table 12.7. Each row of the matrix corresponds to one of the terms that have not been eliminated (has no check) in any of the tables used so far. Each column corresponds to one of the terms in the original expression. An X is placed at each intersection of a row and a column such that the row element is “compatible” with the column element. That is, the variables present in the row element have the same value as the variables present in the column element. Next, circle each X that is alone in a column. Then place a square around each X in any row in which there is a circled X. If every column now has either a squared or a circled X, then we are done, and those row elements whose Xs have been marked constitute the minimal expression.
In cases in which some columns have neither a circle nor a square, additional processing is required. Essentially, we keep adding row elements until all columns are covered.

## Slide 24: Figure 12.13 NAND Implementation of Table 12.4
Notes: Another consideration in the implementation of Boolean functions concerns the types of gates used. It is sometimes desirable to implement a Boolean function solely with NAND gates or solely with NOR gates. Although this may not be the minimum-gate implementation, it has the advantage of regularity, which can simplify the manufacturing process.

## Slide 25: Figure 12.14 4-to-1 Multiplexer Representation
Notes: The multiplexer connects multiple inputs to a single output. At any time, one of the inputs is selected to be passed to the output. A general block diagram representation is shown in Figure 12.14. This represents a 4-to-1 multiplexer. There are four input lines, labeled D0, D1, D2, and D3. One of these lines is selected to provide the output signal F. To select one of the four possible inputs, a 2-bit selection code is needed, and this is implemented as two select lines labeled S1 and S2.

## Slide 26: Table 12.8 4-to-1 Multiplexer Truth Table
S2 | S1 | F
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
Notes: An example 4-to-1 multiplexer is defined by the truth table in Table 12.8. This is a simplified form of a truth table. Instead of showing all possible combinations of input variables, it shows the output as data from line D0, D1, D2, or D3.

## Slide 27: Figure 12.15 Multiplexer Implementation
Notes: Figure 12.15 shows an implementation using AND, OR, and NOT gates. S1 and S2 are connected to the AND gates in such a way that, for any combination of S1 and S2, three of the AND gates will output 0. The fourth AND gate will output the value of the selected line, which is either 0 or 1. Thus, three of the inputs to the OR gate are always 0, and the output of the OR gate will equal the value of the selected input gate. Using this regular organization, it is easy to construct multiplexers of size 8-to-1, 16-to-1, and so on.

## Slide 28: Figure 12.16 Multiplexer Input to Program Counter
Notes: Multiplexers are used in digital circuits to control signal and data routing. An example is the loading of the program counter (PC). The value to be loaded into the program counter may come from one of several different sources:
* A binary counter, if the PC is to be incremented for the next instruction
*The instruction register, if a branch instruction using a direct address has just been executed
*The output of the ALU, if the branch instruction specifies the address using a displacement mode
These various inputs could be connected to the input lines of a multiplexer, with the PC connected to the output line. The select lines determine which value is loaded into the PC. Because the PC contains multiple bits, multiple multiplexers are used, one per bit. Figure 12.16 illustrates this for 16-bit addresses.

## Slide 29: Figure 12.17 Decoder with 3 Inputs and 23 = 8 Outputs
Notes: A decoder is a combinational circuit with a number of output lines, only one of which is asserted at any time. Which output line is asserted depends on the pattern of input lines. In general, a decoder has n inputs and 2n outputs. Figure 12.17shows a decoder with three inputs and eight outputs.

## Slide 30: Figure 12.18 Address Decoding
Notes: Decoders find many uses in digital computers. One example is address decoding. Suppose we wish to construct a 1K-byte memory using four 256 * 8-bit RAM chips. We want a single unified address space, which can be broken down as follows:
Address Chip
0000-00FF 0
0100-01FF 1
0200-02FF 2
0300-03FF 3
Each chip requires 8 address lines, and these are supplied by the lower-order 8 bits of the address. The higher-order 2 bits of the 10-bit address are used to select one of the four RAM chips. For this purpose, a 2-to-4 decoder is used whose output enables one of the four chips, as shown in Figure 12.18.

## Slide 31: Figure 12.19 Implementation of a Demultiplexer Using a Decoder
Notes: With an additional input line, a decoder can be used as a demultiplexer. The demultiplexer performs the inverse function of a multiplexer; it connects a single input to one of several outputs. This is shown in Figure 12.19. As before, n inputs are decoded to produce a single one of 2n outputs. All of the 2n output lines are ANDed with a data input line. Thus, the n inputs act as an address to select a particular out- put line, and the value on the data input line (0 or 1) is routed to that output line.
The configuration in Figure 12.19 can be viewed in another way. Change the label on the new line from Data Input to Enable. This allows for the control of the timing of the decoder. The decoded output appears only when the encoded input is present and the enable line has a value of 1.

## Slide 32: Read-Only Memory (ROM)
Memory that is implemented with combinational circuits
  Combinational circuits are often referred to as “memoryless” circuits because their output depends only on their current input and no history of prior inputs is retained
Memory unit that performs only the read operation
  Binary information stored in a ROM is permanent and is created during the fabrication process
  A given input to the ROM (address lines) always produces the same output (data lines)
  Because the outputs are a function only of the present inputs, ROM is a combinational circuit
Notes: Combinational circuits are often referred to as “memoryless” circuits, because their output depends only on their current input and no history of prior inputs is retained. However, there is one sort of memory that is implemented with combinational circuits, namely read-only memory (ROM).
Recall that a ROM is a memory unit that performs only the read operation. This implies that the binary information stored in a ROM is permanent and was created during the fabrication process. Thus, a given input to the ROM (address lines) always produces the same output (data lines). Because the outputs are a function only of the present inputs, the ROM is in fact a combinational circuit.

## Slide 33: Table 12.9 Truth Table for a ROM
Input |  |  |  | Output |  |  | 
X1 | X2 | X3 | X4 | Z1 | Z2 | Z3 | Z4
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
Notes: A ROM can be implemented with a decoder and a set of OR gates. As an example, consider Table 12.9. This can be viewed as a truth table with four inputs and four outputs. For each of the 16 possible input values, the corresponding set of values of the outputs is shown. It can also be viewed as defining the contents of a 64-bit ROM consisting of 16 words of 4 bits each. The four inputs specify an address, and the four outputs specify the contents of the location specified by the address. Figure 12.20 shows how this memory could be implemented using a 4-to-16 decoder and four OR gates. As with the PLA, a regular organization is used, and the interconnections are made to reflect the desired result.

## Slide 34: Figure 12.20 A 64-Bit ROM
Notes: Figure 12.20 shows how this memory could be implemented using a 4-to-16
decoder and four OR gates. As with the PLA, a regular organization is used, and
the interconnections are made to reflect the desired result.

## Slide 35: Table 12.10 Binary Addition Truth Tables
(a) Single- Bit Addition |  |  | 
A | B | SUM | CARRY
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
(b) Addition with Carry Input |  |  |  | 
Cin | A | B | SUM | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Binary addition differs from Boolean algebra in that the result includes a carry term.
However, addition can still be dealt with in Boolean terms. In Table 12.10a, we show the logic for adding two input bits to produce a 1-bit sum and a carry bit. This truth table could easily be implemented in digital logic. However, we are not interested in performing addition on just a single pair of bits. Rather, we wish to add two n-bit numbers. This can be done by putting together a set of adders so that the carry from one adder is provided as input to the next.
For a multiple-bit adder to work, each of the single-bit adders must have three inputs, including the carry from the next-lower-order adder. The revised truth table appears in Table 12.10b.

## Slide 36: Figure 12.21 4-Bit Adder
Notes: A 4-bit adder is depicted in Figure 12.21.

## Slide 37: Figure 12.22 Implementation of an Adder
Notes: Figure 12.22 is an implementation using AND, OR, and NOT gates.

## Slide 38: Figure 12.23 Construction of a 32-Bit Adder Using 8-Bit Adders
Notes: Thus we have the necessary logic to implement a multiple-bit adder such as shown in Figure 12.23. Note that because the output from each adder depends on the carry from the previous adder, there is an increasing delay from the least significant to the most significant bit. Each single-bit adder experiences a certain amount of gate delay, and this gate delay accumulates. For larger adders, the accumulated delay can become unacceptably high.
If the carry values could be determined without having to ripple through all the previous stages, then each single-bit adder could function independently, and delay would not accumulate. This can be achieved with an approach known as carry lookahead.
Figure 12.23 shows how a 32-bit adder can be constructed out of four 8-bit adders. In this case, the carry must ripple through the four 8-bit adders, but this will be substantially quicker than a ripple through thirty-two 1-bit adders.

## Slide 39: Sequential Circuit
Current output depends not only on the current input, but also on the past history of inputs
Makes use of combinational circuits
Sequential
Circuit
Notes: Combinational circuits implement the essential functions of a digital computer. However, except for the special case of ROM, they provide no memory or state information, elements also essential to the operation of a digital computer. For the latter purposes, a more complex form of digital logic circuit is used: the sequential circuit. The current output of a sequential circuit depends not only on the current input, but also on the past history of inputs. Another and generally more useful way to view it is that the current output of a sequential circuit depends on the current input and the current state of that circuit.
In this section, we examine some simple but useful examples of sequential circuits. As will be seen, the sequential circuit makes use of combinational circuits.

## Slide 40: Flip-Flops
Simplest form of sequential circuit
There are a variety of flip-flops, all of which share two properties:
        The flip-flop is a bistable device. It exists in one of two states and, in the absence of input, remains in that state. Thus, the flip-flop can function as a 1-bit memory.
        The flip-flop has two outputs, which are always the complements of each other.
Notes: The simplest form of sequential circuit is the flip-flop. There are a variety of flip- flops, all of which share two properties:
The flip-flop is a bistable device. It exists in one of two states and, in the absence of input, remains in that state. Thus, the flip-flop can function as a 1-bit memory.
The flip-flop has two outputs, which are always the complements of each other.

## Slide 41: Figure 12.24 The S–R Latch Implemented with NOR Gates
Notes: Figure 12.24 shows a common configuration known as the S–R flip-flop or S–R latch.
The circuit has two inputs, S (Set) and R (Reset), and two outputs, and consists of two NOR gates connected in a feedback arrangement.

## Slide 42: Figure 12.25 NOR S–R Latch Timing Diagram
Notes: Figure 12.25 NOR S-R Latch Timing Diagram.

## Slide 43: Table 12.12 The S–R Latch
(a) Characteristic Table |  | 
Current Inputs | Current State | Next State
SR | Qn | Qn+1
00 | 0 | 0
00 | 1 | 1
01 | 0 | 0
01 | 1 | 0
10 | 0 | 1
10 | 1 | 1
11 | 0 | –
11 | 1 | –
(b) Simplified Characteristic Table |  | 
A | B | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | –
(c) Response to Series of Inputs |  |  |  |  |  |  |  |  |  | 
t | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
S | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
R | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Qn+1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Notes: The S–R latch can be defined with a table similar to a truth table, called a characteristic table, which shows the next state or states of a sequential circuit as a function of current states and inputs. In the case of the S–R latch, the state can be defined by the value of Q. Table 12.12a shows the resulting characteristic table. Observe that the inputs S = 1,R = 1 are not allowed, because these would pro- duce an inconsistent output. The table can be expressed more compactly, as in Table 12.12b. An illustration of the behavior of the S–R latch is shown in Table 12.12c .

## Slide 44: Figure 12.26 Clocked S–R Flip-Flop
Notes: The output of the S–R latch changes, after a brief time delay, in response to a change in the input. This is referred to as asynchronous operation. More typically, events in the digital computer are synchronized to a clock pulse, so that changes occur only when a clock pulse occurs. Figure 12.26 shows this arrangement. This device is referred to as a clocked S–R flip-flop. Note that the R and S inputs are passed to the NOR gates only during the clock pulse.

## Slide 45: Figure 12.27 D Flip-Flop
Notes: One problem with S–R flip-flop is that the condition R = 1,S = 1 must be avoided. One way to do this is to allow just a single input. The D flip-flop accomplishes this. Figure 12.27 shows a gate implementation of the D flip-flop. By using an inverter, the non-clock inputs to the two AND gates are guaranteed to be the opposite of each other.
The D flip-flop is sometimes referred to as the data flip-flop because it is, in effect, storage for one bit of data. The output of the D flip-flop is always equal to the most recent value applied to the input. Hence, it remembers and produces the last input. It is also referred to as the delay flip-flop, because it delays a 0 or 1 applied to its input for a single clock pulse.

## Slide 46: Figure 12.28 J–K Flip-Flop
Notes: Another useful flip-flop is the J–K flip-flop. Like the S–R flip-flop, it has two inputs. However, in this case all possible combinations of input values are valid. Figure 12.28 shows a gate implementation of the J–K flip-flop.

## Slide 47: Figure 12.29 Basic Flip-Flops
Notes: Figure 12.29 shows its characteristic table (along with those for the S–R and D flip-flops). Note that the first three combinations are the same as for the S–R flip-flop. With no input asserted, the output is stable. If only the J input is asserted, the result is a set function, causing the output to be 1; if only the K input is asserted, the result is a reset function, causing the output to be 0. When both J and K are 1, the function performed is referred to as the toggle function: the output is reversed. Thus, if Q is 1 and 1 is applied to J and K, then Q becomes 0. The reader should verify that the implementation of Figure 12.28 produces this characteristic function.

## Slide 48: Figure 12.30 8-Bit Parallel Register
Notes: A parallel register consists of a set of 1-bit memories that can be read or written simultaneously. It is used to store data. The registers that we have discussed throughout this book are parallel registers.
The 8-bit register of Figure 12.30 illustrates the operation of a parallel register using D flip-flops. A control signal, labeled load, controls writing into the register from signal lines, D11 through D18. These lines might be the output of multiplexers, so that data from a variety of sources can be loaded into the register.

## Slide 49: Figure 12.31 5-Bit Shift Register
Notes: A shift register accepts and/or transfers information serially. Consider, for example, Figure 12.31, which shows a 5-bit shift register constructed from clocked D flip-flops. Data are input only to the leftmost flip-flop. With each clock pulse, data are shifted to the right one position, and the rightmost bit is transferred out.
Shift registers can be used to interface to serial I/O devices. In addition, they can be used within the ALU to perform logical shift and rotate functions. In this
latter capacity, they need to be equipped with parallel read/write circuitry as well as serial.

## Slide 50: Counter
A register whose value is easily incremented by 1 modulo the capacity of the register
After the maximum value is achieved the next increment sets the counter value to 0
An example of a counter in the CPU is the program counter
Can be designated as:
  Asynchronous
    Relatively slow because the output of one flip-flop triggers a change in the status of the next flip-flop
  Synchronous
    All of the flip-flops change state at the same time
    Because it is faster it is the kind used in CPUs
Notes: Another useful category of sequential circuit is the counter. A counter is a register whose value is easily incremented by 1 modulo the capacity of the register; that is, after the maximum value is achieved the next increment sets the counter value to 0. Thus, a register made up of n flip-flops can count up to 2n - 1. An example of a counter in the CPU is the program counter.
Counters can be designated as asynchronous or synchronous, depending on the way in which they operate. Asynchronous counters are relatively slow because the output of one flip-flop triggers a change in the status of the next flip-flop. In a synchronous counter, all of the flip-flops change state at the same time. Because the latter type is much faster, it is the kind used in CPUs. However, it is useful to begin the discussion with a description of an asynchronous counter.

## Slide 51: Figure 12.33 Design of a Synchronous Counter
Notes: An asynchronous counter is also referred to as a ripple counter, because the change that occurs to increment the counter starts at one end and “ripples” through to the other end
The ripple counter has the disadvantage of the delay involved in changing value, which is proportional to the length of the counter. To overcome this disadvantage, CPUs make use of synchronous counters, in which all of the flip-flops of the counter change at the same time. In this subsection, we present a design for a 3-bit synchronous counter. In doing so, we illustrate some basic concepts in the design of a synchronous circuit.
For a 3-bit counter, three flip-flops will be needed. Let us use J–K flip-flops. Label the uncomplemented output of the three flip-flops A, B, and C, respectively, with C representing the least significant bit. The first step is to construct a truth table that relates the J–K inputs and outputs, to allow us to design the overall circuit. Such a truth table is shown in Figure 12.33a. The first three columns show the possible combinations of outputs A, B, and C. They are listed in the order that they will appear as the counter is incremented. Each row lists the current value of A, B, C and the inputs to the three flip-flops that will be required to reach the next value of C, B, and A.
Let us return to Figure 12.33a. Consider the first row. We want the value of A to remain 0, the value of B to remain 0, and the value of C to go from 0 to 1 with the next application of a clock pulse. The excitation table shows that to maintain an output of 0, we must have inputs of J = 0 and don’t care for K. To effect a transition from0to1,theinputsmustbeJ = 1andK = d. These values are shown in the first row of the table. By similar reasoning, the remainder of the table can be filled in.
Having constructed the truth table of Figure 12.33a, we see that the table shows the required values of all of the J and K inputs as functions of the current values of C, B,, and A. With the aid of Karnaugh maps, we can develop Boolean expressions for these six functions. This is shown in part b of the figure. For example, the Karnaugh map for the variable Ja (the J input to the flip-flop that produces the A output) yields the expression Ja = BC. When all six expressions are derived, it is a straightforward matter to design the actual circuit, as shown in part c of the figure.

## Slide 52: Table 12.13 PLD Terminology
Programmable Logic Device (PLD) A general term that refers to any type of integrated circuit used for implementing digital hard- ware, where the chip can be configured by the end user to realize different designs. Programming of such a device often involves placing the chip into a special programming unit, but some chips can also be configured “in-system.” Also referred to as a field- programmable device (FPD). Programmable Logic Array (PLA) A relatively small PLD that contains two levels of logic, an AND-plane and an OR- plane, where both levels are programmable. Programmable Array Logic (PAL) A relatively small PLD that has a programmable AND-plane followed by a fixed OR-plane. Simple PLD (SPLD) A PLA or PAL. Complex PLD (CPLD) A more complex PLD that consists of an arrangement of multiple SPLD-like blocks on a single chip. Field- Programmable Gate Array (FPGA) A PLD featuring a general structure that allows very high logic capacity. Whereas CPLDs feature logic resources with a wide number of inputs (AND planes), FPGAs offer more narrow logic resources. FPGAs also offer a higher ratio of flip- flops to logic resources than do CPLDs. Logic Block A relatively small circuit block that is replicated in an array in an FPD. When a circuit is implemented in an FPD, it is first decomposed into smaller subcircuits that can each be mapped into a logic block. The term logic block is mostly used in the context of FPGAs, but it could also refer to a block of circuitry in a CPLD.
Notes: As the level of integration provided by integrated circuits increases, other considerations apply. Early integrated circuits, using small-scale integration (SSI), provided from one to ten gates on a chip. Each gate is treated independently, in the building-block approach described so far. To construct a logic function, a number of these chips are laid out on a printed circuit board and the appropriate pin interconnections are made.
Increasing levels of integration made it possible to put more gates on a chip and to make gate interconnections on the chip as well. This yields the advantages of decreased cost, decreased size, and increased speed (because on-chip delays are of shorter duration than off-chip delays). A design problem arises, however. For each particular logic function or set of functions, the layout of gates and interconnections on the chip must be designed. The cost and time involved in such custom chip design is high. Thus, it becomes attractive to develop a general-purpose chip that can be readily adapted to specific purposes. This is the intent of the programmable logic device (PLD).
There are a number of different types of PLDs in commercial use. Table 12.13 lists some of the key terms and defines some of the most important types. In this section, we first look at one of the simplest such devices, the programmable logic array (PLA) and then introduce perhaps the most important and widely used type of PLD, the field-programmable gate array (FPGA).

## Slide 53: Figure 12.34 An Example of a Programmable Logic Array (PLA)
Notes: The PLA is based on the fact that any Boolean function (truth table) can be expressed in a sum-of-products (SOP) form, as we have seen. The PLA consists of a regular arrangement of NOT, AND, and OR gates on a chip. Each chip input is passed through a NOT gate so that each input and its complement are available to each AND gate. The output of each AND gate is available to each OR gate, and the output of each OR gate is a chip output. By making the appropriate connections, arbitrary SOP expressions can be implemented.
Figure 12.34a shows a PLA with three inputs, eight gates, and two outputs. On the left is a programmable AND array. The AND array is programmed by establishing a connection between any PLA input or its negation and any AND gate input by connecting the corresponding lines at their point of intersection. On the right is a programmable OR array, which involves connecting AND gate outputs to OR gate inputs. Most larger PLAs contain several hundred gates, 15 to 25 inputs, and 5 to 15 outputs. The connections from the inputs to the AND gates, and from the AND gates to the OR gates, are not specified until programming time.
PLAs are manufactured in two different ways to allow easy programming (making of connections). In the first, every possible connection is made through a fuse at every intersection point. The undesired connections can then be later removed by blowing the fuses. This type of PLA is referred to as a field-programmable logic array (FPLA). Alternatively, the proper connections can be made during chip fabrication by using an appropriate mask supplied for a particular interconnection pattern. In either case, the PLA provides a flexible, inexpensive way of implementing digital logic functions.
Figure 12.34b shows a programmed PLA that realizes two Boolean expressions.

## Slide 54: Figure 12.35 Structure of an FPGA
Notes: The PLA is an example of a simple PLD (SPLD). The difficulty with increasing capacity of a strict SPLD architecture is that the structure of the programmable logic-planes grows too quickly in size as the number of inputs is increased. The only feasible way to provide large capacity devices based on SPLD architectures is then to integrate multiple SPLDs onto a single chip and provide interconnect to programmably connect the SPLD blocks together. Many commercial PLD products exist on the market today with this basic structure, and are collectively referred to as Complex PLDs (CPLDs). The most important type of CPLD is the FPGA.
An FPGA consists of an array of uncommitted circuit elements, called logic blocks, and interconnect resources. An illustration of a typical FPGA architecture is shown in Figure 12.35. The key components of an FPGA are;
• Logic block: The configurable logic blocks are where the computation of the user’s circuit takes place.
• I/O block: The I/O blocks connect I/O pins to the circuitry on the chip.
• Interconnect: These are signal paths available for establishing connections
among I/O blocks and logic blocks.

## Slide 55: Figure 12.36 A Simple FPGA Logic Block
Notes: The logic block can be either a combinational circuit or a sequential circuit.
In essence, the programming of a logic block is done by downloading the
contents of a truth table for a logic function. Figure 12.36 shows an example of
a simple logic block consisting of a D flip-flop, a 2-to-1 multiplexer, and a 16-bit
lookup table. The lookup table is a memory consisting of 16 1-bit elements, so
that 4 input lines are required to select one of the 16 bits. Larger logic blocks
have larger lookup tables and multiple interconnected lookup tables. The combinational
logic realized by the lookup table can be output directly or stored in
the D flip-flop and output synchronously. A separate one-bit memory controls
the multiplexer to determine whether the output comes directly from the lookup table or from the flip-flop.
By interconnecting numerous logic blocks, very complex logic functions can be easily implemented.

## Slide 56: Summary
Chapter 12
Boolean Algebra
Gates
Combinational Circuits
  Implementation of Boolean Functions
  Multiplexers
  Decoders
  Read-Only-Memory
  Adders
Digital
Logic
  Sequential Circuits
  Flip-Flops
  Registers
  Counters
  Programmable Logic Devices
  Programmable Logic Array
  Field-Programmable Gate Array
Notes: Chapter 12 summary.